CPUC Confirmation Number:

Title of the Proposed Program:

Large Lighting System Voltage Controller (Electric City Corp. - Energy Saver™) Retrofit Incentive Program for SDG&E Service Territory

Proposing Program Administer Company:

Electro-Test, Inc. (a Division of Emerson Corp.)

# Contact Info:		Jay Raggio, PE, CEM

Manager, Energy Services

jay.raggio@electro-test.com

Address:			3470 Fostoria Way

Suite A

San Ramon, CA  94583

Phone No.:		(925) 328-3408 - Office

(925) 260-0695 – Mobile

Other Programs Proposed:

Supermarket E-Commissioning		Conf. No.

Convenience Store EMS Retrofits	 	Conf. No.

# Table of Contents

## Section I.	Program Overview	1

## Section II.	Program Process	3

## Section III.	Customer Description	8

## Section IV.	Measure and Activity Descriptions	10

## Section V.	Goals	12

## Section VI.	Program Evaluation, Measurement	13

and Verification (EM&V)

## Section VII.	Qualifications	16

## Section VIII.	Budget	31

### Program Workbook								32

Appendices Contained in Paper Copies of Proposal

Appendix 1 – Electro-Test Inc Corporate Brochure

Appendix 2 – Emerson Financial Statement

Appendix 3 – Electric City Corp. Energy Saver™ Cut Sheet

Appendix 4 – Harris Company Test Report

Appendix 5 – Electric City Corp. SEC Form 10K

# Section I.		Program Overview

Large Lighting System Voltage Controller Retrofit Incentive Program for SDG&E Service Territory

Program Concept

Electro-Test, Inc.’s (eti) proposed Large Lighting System Voltage Controller Retrofit Incentive Program for the SDG&E Service Territory is a hardware/incentive program.  The program seeks to improve the energy performance of potentially hundreds of commercial and institutional facilities located within San Diego & Electric Company’s (SDG&E) service territory that receive their electrical service from SDG&E.  The lighting systems voltage controller retrofits will be promoted through this program by means of meaningful financial incentives (up to 40% of project costs) offered to facility owners that implement the installation of a simple, powerful and robust lighting system voltage controller package designed specifically for energy management applications by Electric City Corporation (ELC).  The ELC voltage controller technology, branded Energy Saver™/Global Commander®, will modulate voltages for large HID and/or fluorescent lighting systems in facilities for optimal energy efficiency.  It is worthwhile to note that the ELC Energy Saver™ product currently is an eligible technology in utility energy efficiency incentive programs in other states, Illinois for example.  The technology was also awarded a grant by the CPUC in 2001 for retrofit projects at the California State University campuses throughout the state.

## Program Rationale

Many facility types such as large retail stores, supermarkets, and commercial office buildings are highly energy intensive building types, having average energy intensities of over 30 kWh/ sq. ft./yr.  They contain many energy consuming systems and components but typically lighting systems are their largest component of energy use.

Current industry lighting system design practices for such facilities are conservative in nature and often result in spaces that have light levels that exceed the standards for light levels recommended by the Illuminating Engineering Society (IES) for the specific space types.  Further, the existing lighting systems are, for the most part, incapable of effectively adjusting their artificial light level contributions during conditions of high ambient natural light availability.

Very meaningful gains in reducing the annual energy consumption by large lighting systems can be achieved by exploiting the unique non linear performance attributes of modern electronic ballasts.  Namely, by reducing the voltage level of the power supplied to the lighting systems by pre determined amounts, energy can be saved while the light levels in the building spaces remain at entirely acceptable levels.

Interactive energy savings are also realized as heat generation from the lighting systems is also reduced which relieves cooling loads on the building’s HVAC systems.

Program Objectives

It is the objective of eti’s proposed program to stimulate the installation of ELC Energy Saver™ lighting system voltage controller systems in at least 50 facilities in 2004 and at least another 100 facilities in 2005.  Based upon typical energy consumption data for such facilities, these installation objectives translate to the following conservative annual energy savings and peak demand reductions:

Annual Energy Savings

- ~6 million kWh

- ~12 million kWh

## Program Total	~18 million kWh

Peak Demand Reduction

2004		~1,000 kW

- ~2,000 kW

Program Total	~3,000 kW

Total Resource Cost (TRC) Ratio

The following Program Workbook indicates this Program achieves a TRC ratio of 3.608.  Please note that eti has placed the total cost for projects that Host Customers will bear into the Incremental Measure Cost (IMC) cell in the CPUC’s workbook.  The rationale being that Host Customers do not have to make the decision to implement the Energy Saver™ retrofits and they will still be able to conduct their normal business.  Thus, making such an implementation decision creates an entirely incremental cost from the Host Customer’s perspective.

# Section II.	Program Process

Large Lighting System Voltage Controller Retrofit Incentive Program for PG&E Service Territory

#### Program Implementation

eti’s proposed program differs from programs currently offered by utilities, and others, primarily in that it does not focus specifically on equipment replacements such as fluorescent lamps and ballasts, electric motors or chiller packages.  Instead the program promotes an enabling technology for optimizing a facility’s lighting system energy performance.  The enabling technology in this case is an Internet web enabled programmable voltage modulation device based upon a patented “continuous tap” auto-transformer technology.

The ELC Energy Saver™ technology will enable a fundamental shift in common industry practice. Namely, from on-site and intermittent on/off control of energy consuming lighting systems to automated entire system dimming control and continuous monitoring and documenting of the energy performance of the lighting systems.  For example, a corporate facility manager can remotely establish desired energy conservation lighting levels for numerous facilities located within a wide geographic area.  Or, lighting system output levels can be automatically adjusted downward to take advantage of available ambient natural light levels with adjustment corrections made throughout the day.  Any local override of the desired light levels would result in an alarm back to the facility manager who then can quickly take action to remedy the energy wasteful situation.

## Marketing Plan

Undoubtedly, the number of large retail, commercial and institutional facilities located in California where the ELC Energy Saver™ product can be effectively applied number in the thousands.

The majority of such facilities are affiliated with national retail chains or commercial property management companies of which the following companies are just a few typical examples where strong customer interest already has been expressed in the Energy Saver™ product:

Kilroy Real Estate			Gillette

Transwestern			Indy Mac Bank

Target Corporation		San Francisco International Airport

Kohl’s				Intel

### Raley’s Markets				Bank of America

Sports Chalet			General Electric

Marketing of the ELC Energy Saver™ project incentive opportunity will be accomplished by directly engaging corporate level decision-makers with the national retail chain and property management companies.  These individuals are cognizant of the number, location, size, age, and future plans for the various facilities.  Thus, a positive decision to implement the ELC Energy Saver™ technology can be made by a single or small number of individuals and yet result in projects being implemented at numerous facilities.

For example, an individual internal “champion” for the ELC Energy Saver™ technology has influenced the corporate management at Raley’s Supermarkets to consider reaching a positive decision to implement the systems at 80 of its facilities in California.

ELC employs a national marketing and sales organization having several personnel responsible for California.  These individuals are already knowledgeable of the targeted national companies, their structures and have relationships with their individuals are who are responsible for facility improvement or energy matters.  If eti’s program is selected for funding, the ELC marketing and sales personnel for California will be informed and trained in the meaningful and time sensitive project incentive opportunity.  In turn, they will engage the key individuals with the national chains to inform them of the opportunity.

eti, for its part, will inform the broader marketplace of facility owners and operators regarding the project incentive opportunity through interactions with trade organizations and interest groups.  These groups include for example:

### California Grocers Association

Northern California Grocers Association
Building Owner and Managers Associations
Association of Facility Engineers

These forums will enable solely independent facility owners to learn of and seek to participate in the eti project incentive program.

#### Customer Enrollment

It is anticipated that customer enrollment will be at the national corporate chain level with each corporation participating in the program providing the store identification numbers, addresses, contact names and utility account numbers for the each of the individual facilities it wishes to enroll.  The use and exchange of spreadsheet tools for facility data sets will serve to ease the collection and management of customer facility data.

Enrollment of individual customers resulting from eti’s own outreach activities will be handled by providing a designated point of contact with eti to obtain the required company and facility information required for program participation.

All customers will be required to sign a program participation agreement with eti specifying the roles, responsibilities, and obligations of each party, the timing and amount of the project incentives and provide a mechanism for dispute resolution.

#### Materials

The materials required for eti’s Large Lighting Systems Voltage Controller Retrofit Program projects include the following for each project site:

### Energy Saver™ controller modules

Miscellaneous light level sensors

## Electrical contactors, relays, and enclosures

Signal wiring and conduit

Ethernet or other communications connections

Six (6) parties will be involved in the ELC Energy Saver™ retrofit projects for each participating site.  They include the following:

| Project Participant | Responsibilities |
| --- | --- |
| Host Customer’s corporate decision maker | Approve specific project scope, cost, and schedule. Issue a furnish and install contract to ELC or its local distributor. Enter into a program participation agreement with eti. |
| Host Customer’s local on-site management personnel | Coordinate the on-site activities of the ELC deployment team (facility auditing and system installation/commissioning) |
| Electric City Corporation (equipment supplier) | Manufacture and deliver the Energy Saver™ controller modules to project sites. |
| ELC deployment team | Perform and document facility audits. Manage the physical installation of the Energy Saver™ controller modules. Commission the systems. Perform long term energy performance remote monitoring. |
| Local electrical contractor firm | Install all hardware systems and components under the project management of the ELC deployment team. |
| Electro-Test, Inc. (eti) | Enroll Host Customers in the ELC Energy Saver™ incentive program. Assure all requirements for participation are fulfilled. Document specific individual project features. Perform required M&V activities and document project performance results. Disperse incentive payments to Host Customers. Document and report on program achievements to the CPUC. |

- Payment of Incentives

The incentive amount proposed for eti’s Large Lighting Systems Voltage Controller Retrofit Incentive Program is $0.065/kWh of annual energy savings up to 40% of the project installed cost, or approximately $7,000 to $20,000 per site.

Since it is anticipated that multiple project sites will be enrolled for each participating Host Customer, the payment of incentives is likely to be in a block wise fashion.  For example, an incentive payment will be made to a Host Customer for each block of 10 completed project sites.

Incentive payments will be made only after certification by the ELC deployment team that a project’s Energy Saver system is entirely installed, its operation commissioned, and three (3) months’ performance data is indicating that the anticipated demand and energy savings are being achieved.

F.  Staff and Subcontractor Responsibilities

The responsibilities of the Staff and Subcontractors are as follows:

| Program Participant | Responsibilities |
| --- | --- |
| Emerson Electro-Test, Inc. (eti) – Program Administrator | Administer the SDG&E territory Large Lighting System Voltage Controller Retrofit Incentive Program. Perform Marketing of the retrofit incentive opportunity to end-users. Enroll Host Customers in the program. Assure all requirements for program participation are fulfilled by all participants. Document specific individual project features. Perform required M&V activities and document project performance results. Disperse incentive payments to Host Customers. Document and report on program achievements to the CPUC. |
| Electric City Corporation - Equipment Supplier | Perform the sales and marketing of the retrofit incentive opportunity to the end user market. Enter into furnish and install project agreements with end users. Manufacture and deliver the Energy Saver™ voltage controller modules to project sites. |

| Program Participant | Responsibilities |
| --- | --- |
| Local deployment team – Project Manager | Perform and document facility audits. Manage the physical installation of the Energy Saver™ controller modules. Commission the systems. Perform long term energy performance remote monitoring. |

#### G.  Work Plan and Timeline for Implementation

## The anticipated timeline for Program achievement milestones is presented in the following table.

###### Timeline for Implementation

| Program Achievement | Anticipated Date |
| --- | --- |
| CPUC selection of eti as Program Administrator – Large Lighting System Voltage Controller Retrofit Incentive Program | January 2004 |
| eti‘s Program roll out to the end user market | March 2004 |
| Initial project enrollment | April 2004 |
| 20 projects enrolled | August 2004 |
| 50 projects enrolled | December 2004 |
| 75 projects enrolled | April 2005 |
| 100 projects enrolled | August 2005 |
| 150 projects enrolled | December 2005 |

# Section III.	Customer Description

Large Lighting System Voltage Controller Retrofit Incentive Program

#### Customer Description

Targeted customers (project sites) for the eti Large Lighting System Voltage Controller Retrofit Incentive Program are primarily facilities owned and operated by national retail chains and national property management firms.  Examples of such companies include:

Raley’s Markets

Target Corporation

Kohl’s

### Kilroy Real Estate

Sports Chalet

Bank of America

Intel

General Electric

Within SDG&E’s service territory there are several hundred such facilities.  They are numerous within major urban areas and suburban areas.

Each of the targeted facilities is, in itself, a commercial customer account of the serving utility, in this case SDG&E, likely having an A6-TOU tariff schedule.  In general, investment decisions for these facilities are made by central corporate departments and decision-makers.  These same departments and decision makers often have responsibilities as well for managing the operating costs for the facilities.  As these facilities are large consumers of energy, energy cost management is a key and persistent objective of these departments and decision-makers.

B.	Customer Eligibility

The criteria for customers to be eligible for participation in eti’s program include the following:

Must be an electric distribution customer of SDG&E.

Must have an annual electric consumption of at least 500,000 kWh.

Must have no plans for discontinuing operations for at least five (5) years.

Must be willing to execute and abide by a Program Participation Agreement with eti.

#### Geographic Area

Individual project sites can be located throughout SDG&E’s service territory.  Because of the nature of the market, targeted customers will be densest within major urban areas, less so in suburban areas, and least dense in rural areas.

To the extent that a major urban area or suburban area is also a transmission-constrained area, projects implemented through this program in those areas may serve, in aggregate, to provide meaningful grid relief.

Section IV.	Measure and Activity Descriptions

Large Lighting System Voltage Controller Retrofit Incentive Program for PG&E Service Territory

#### Energy Savings Assumptions

The energy savings assumptions for this proposed program are based on the performance experience gained at similar projects located in other utility service territories.  For example, in 14 stores of a regional supermarket chain located in Northern California.

In these projects, the ELC Energy Saver™ systems were installed and commissioned at each site.  The systems were configured to control the operation of facilities’ HID or fluorescent lighting, which, constituted the bulk of the facilities’ total electrical demand and energy consumption.

System voltage setpoints were controlled, monitored, and documented by means of Internet/Web connectivity with the Energy Saver™ modules.

Utility billing data was compared over a month period with the same month’s utility billing data for the same period in the previous year.  Facility equipment and operations were essentially identical between the two periods.

The evaluation results showed the average performance of the population of 14 stores was a 1,750,000 kWh reduction in annual energy usage.  For purposes of this Program plan, it is assumed that the overall population of projects enrolled in the program will deliver on average, 120,000 kWh annual energy savings per site and 20 kW average coincident peak demand reduction per site.  These are believed to be conservative values with actual performance values being potentially better.

#### B.  Deviations from Standard Cost-Effectiveness Values

Net to Gross Ratio – A Net to Gross Ratio of 0.95 is appropriate to the eti Program.  Since the lighting system voltage controller retrofit measure is a relatively new energy services market entrant, it is unlikely that significant numbers of facility owners would adopt the technology in the absence of a meaningful incentive program.

Estimated Useful Life – The estimated useful life of the ELC Energy Saver™ voltage controller system is comparable to other commercially established electronic controller systems, namely 15 years.

Incremental Measure Cost - As there is no new end use equipment installed as part of the proposed retrofit projects, there is no associated incremental measure cost over the cost of equipment having minimum efficiencies established by code or law.

#### C.  Rebate Amounts

The rebate amount proposed for the eti Large Lighting System voltage Controller Retrofit Incentive Program is $0.065/kWh for annual energy savings, up to 40% of the individual projects’ installed cost.  This typically may be an incentive of between $5,200 and $10,300 per site assuming one appropriately sized Energy Saver™ module is adequate for the connected lighting system load.  Because the ELC Energy Saver™ module is highly scalable, it can accommodate the control functions required for essentially most types and forms of retail and commercial facilities.  Small differences in the numbers of fixtures controlled among facilities will minimally affect the total project costs.  Thus, project costs are anticipated to be relatively uniform across all projects of similar size and the associated rebate amounts similarly uniform across all projects of similar size.

A rebate amount of $0.065/kWh of energy savings up to 40% of project installed cost was chosen as a meaningful driver to influence responsible corporate authorities to quickly decide to implement ELC Energy Saver™ projects.  After the affect of the Program rebate, the pay back period for the ELC Energy Saver™ retrofit projects should approximately be between one and two years, comfortably within most corporation’s required pay back period for capital investments.

From a Program marketing perspective, communicating to potential customers that, within a limited time window of opportunity, close to one half of proposed projects’ costs can be covered by Program project incentives will be a powerful sales feature and greatly enhance the probability of achieving the Program’s goals.

#### D.  Activities Descriptions

Program activities not expected to directly contribute energy savings will include auditing and documenting the existing in place energy consuming systems and equipment.  The equipment audit is needed as a reliable source of information in the future if achieved longer term energy performance is substantially different than anticipated.  The audit information records will assist in determining if energy consuming equipment have been added or removed.

This activity should add less than $1,000 to an individual project’s costs.

# Section V.	Goals

Large Lighting System Voltage Controller Retrofit Incentive Program for SDG&E Service Territory

## A.  Program Goals

The proposed eti Large Lighting System Voltage Controller Retrofit Incentive Program has the following as its goals for the SDG&E service territory:

###### eti Program Goals

| Program Achievement | Annual Energy Savings Contribution, kWh | Peak Demand Reduction Contribution, kW | Anticipated Date |
| --- | --- | --- | --- |
| 20 projects enrolled | 2,400,000 | 400 | August 2004 |
| 50 projects enrolled | 6,000,000 | 1,000 | December 2004 |
| 75 projects enrolled | 9,000,000 | 1,500 | April 2005 |
| 100 projects enrolled | 12,000,000 | 2,000 | August 2005 |
| 150 projects enrolled | 18,000,000 | 3,000 | December 2005 |

# Section VI.	Program Evaluation, Measurement and

# Verification (EM&V)

Large Lighting System Voltage Controller Retrofit Incentive Program

#### A.  Program Evaluation Approach

The Large Lighting System Voltage Controller Retrofit Incentive Program, if successful, will result in hundreds of essentially similar facilities being retrofit with essentially similar voltage controller hardware designed to improve their energy consumption performance.  The Energy Saver™ systems primarily will control large lighting system circuits powering HID and or fluorescent lighting systems.

Utility billing for these facilities is normally accomplished by means of interval metering.  Monthly energy consumption is identified by kWh consumption within PG&E pricing periods.  Peak kW by PG&E pricing period is also provided from the interval metering.

In consideration of the foregoing, eti’s proposed Program Evaluation Approach has the following features:

Energy savings will be determined by measuring kW and kWh of the large lighting systems operating at their normal utility supplied voltage levels and later at the pre determined reduced voltages desired by the facility owner.  These pre project measurements will be obtained for one month both prior to and following the commissioning of the Energy Saver™ systems.  These measurements can be obtained by the standard Energy Saver™ product as it includes a revenue quality meter.

The kW and kWh measurements will be obtained again following the commissioning of the operation of the Energy Saver™ systems for a period of one month.

The pre and post Energy Saver™ commissioning kW and kWh will be compared and differences taken to be the kW demand reduction and kWh energy savings attributable solely to the operation of the installed Energy Saver™ systems.  The one month energy savings performance data will be extrapolated to determine annual energy savings.

If longer monitoring periods are desired by the CPUC, they can be easily provided by the Energy Saver™’s performance monitoring features.

It is proposed to increase the credited energy savings determined by the foregoing direct metering measurements by 10% to conservatively account for the “interactive HVAC savings” from the reduced lighting system heat contributions to the facility’s cooling loads.

At this time, it is envisioned that all sites enrolled in the program will undergo the site specific energy savings evaluation described in the foregoing paragraphs.  As experience is gained with the energy savings performance attributable to the Energy Saver™ retrofits, eti may propose to transition to a sampling based approach that assigns to a larger population of facilities of similar size and geographic region the energy savings calculated from a randomly selected but smaller representative sample number of facilities.

B.	Suggested EM&V Contractors

Suggested EM&V Contractor No. 1 – Electro-Test, Inc itself

eti may be unique among the entities that are seeking to perform as a Third Party Energy Efficiency Program Administrator in 2004 and 2005 because its core business skills and market offerings include the measurement and assessment of electrical power systems performance for commercial, institutional, and industrial customers as well as, a comprehensive portfolio of energy engineering and energy management services.  In its six (6) Regional Service Centers, located throughout California, eti employs over 100 highly trained and experienced electrical field engineers and technicians.  A substantial number of these personnel have obtained knowledge and skills certifications from the National Electrical Testing Association (NETA).  eti also possesses a large inventory of modern, calibrated, power measurement instruments.  Thus, these skilled eti personnel can readily and effectively perform the on-site measurements of the electrical performance of facility power systems.

Likewise, eti’s Energy Services Division, located in San Ramon, CA, employs a cadre of energy engineering professionals.  These individuals are experienced in developing and implementing M&V plans.

eti is currently a partner company in PG&E’s Power Saving Partners DSM program.  In that program, eti has enrolled 48 commercial and institutional customers and is implementing its approved M&V plans for over 150 individual project sites.  To date, eti has prepared over 200 annual peak demand reduction and energy savings analysis reports that have been reviewed and found acceptable by PG&E’s technical consultant, Nexant, Inc.

eti possesses the skills, qualifications and resources to perform the EV&M for its Large Lighting System Voltage controller Retrofit Incentive Program.

More information is provided in the following Section VII. - Qualifications

Suggested EM&V Contractor No. 2 – Nexant, Inc.

Nexant, Inc. (formerly Schiller & Associates) is a well-respected energy consulting firm in California, as well as in several other states.  It is presently under contract with PG&E and SCE to provide review and evaluation of M&V plans and review and evaluation of M&V plan annual savings reports.

Nexant, Inc. is equally qualified to provide the EM&V activities for eti’s proposed program.  It does not possess, however, the depth of in-house physical power systems performance measurement capabilities that eti possesses.

# Section VII.	Qualifications

Large Lighting System Voltage Controller Retrofit Incentive Program

A.	Primary Program Implementer – Electro-Test, Inc.

Electro-Test Inc. (eti) is the nation’s leading independent electrical power systems testing company.  Founded in 1972, it has grown to an organization having over 300 employees located in over 30 regional service centers throughout the United States.  In 1996, eti was acquired by Emerson Corporation, a Fortune 500 company, providing electrical and electronic components and services worldwide.  eti is a wholly owned subsidiary of Emerson Corporation.  eti’s customers include many Fortune 500 companies, among them, Bank of America, Chevron Oil, Applied Materials, and many others.

In 1995, eti established an energy services group to provide its customers with site specific solutions to manage and reduce their energy related costs.  This core group of experienced energy professionals will provide the energy efficiency program administration and EM&V services encompassed by the scope of the CPUC’s September 2003 RFP Soliciting 2004-2005 Energy Efficiency Program Proposals.

The individuals on eti’s energy services team are seasoned professionals with access to both routine and unique software and hardware tools to enable them to provide the services described in the RFP in a competent, timely, and cost effective manner.

A key attribute of eti is its track record of superior performance as a DSM service provider to Pacific Gas & Electric Company (PG&E) since 1996 through two contracts in its Power Saving Partners (PSP) energy savings stimulus program.  As part of the PSP Program, we have worked with many private commercial companies and public agencies to develop and implement energy efficiency projects.

eti’s many project partners in the PSP program include: Target Stores, Certified Grocers, EquityOffice Properties, El Camino Hospital, Caltrans, University of California at Davis, Central Contra Costa Sanitary District, San Jose Water Pollution Control Plant, City of Oakland, City of Hayward, County of Alameda, and Federal Agencies including the U.S. Post Office, Internal Revenue Service, and the General Services Administration.

eti, through its effective program marketing, enrolled 48 projects in its DSM program which encompass over 150 individual project sites.  Combined, these projects are achieving over 40 million kWh per year in energy savings and have reduced PG&E’s peak load demand by over 5 MW.

eti has also performed as a subcontractor to several national Energy Services companies (ESCO’s) providing M&V services for their large energy efficiency projects enrolled in the Statewide Standard Performance Contract programs.

The following table contains a description of the numbers and types of energy efficiency projects that eti has been involved in and the projects’ measured and verified performance.

| Project Name | Energy Conservation Measures | Peak kW Reduced | Annual kWh Savings |
| --- | --- | --- | --- |
| Oakland Municipal Courthouse | Lighting Efficiency & Controls | 44 | 347,977 |
| Cal Trans LED Traffic Lights | Lighting Efficiency | 740 | 6,382,379 |
| Target Stores (34 locations) | Lighting Efficiency & Controls | 380 | 2,735,066 |
| Target Stores Distribution Center | Lighting Controls | 111 | 976,947 |
| Marin General Hospital | Lighting Efficiency | 111 | 706,308 |
| USPS - Sacramento (10 locations) | Lighting Efficiency | 63 | 298,218 |
| USPS - San Francisco (8 locations) | Lighting Efficiency | 117 | 561,764 |
| El Camino Hospital Chiller | Chiller Upgrade | 33 | 519,164 |
| Naval Post Graduate School | Lighting Efficiency | 103 | 581,434 |
| Kennedy Wilson Properties ( 8 locations) | Lighting Efficiency | 121 | 590,156 |
| City of West Sacramento LED | Lighting Efficiency | 36 | 305,484 |
| Levi Plaza Parking Garage | Lighting Efficiency | 18 | 156,148 |
| San Jose Water Pollution Control Plant | VFD Retrofit | 255 | 1,898,481 |
| Lincoln Properties | Lighting Efficiency | 71 | 619,739 |
| Alexian Brothers Hospital | Lighting Efficiency | 62 | 459,907 |
| Certified Grocers - Stockton | Lighting Controls | 167 | 1,225,040 |
| Crow Canyon Executive Park | Lighting Efficiency | 32 | 138,983 |
| El Camino Hospital Lighting (4 Buildings) | Lighting Efficiency | 240 | 1,626,630 |
| El Camino Hospital Motors | Motor Efficiency | 48 | 446,152 |
| Monterey Peninsula Hospital | Lighting Efficiency | 112 | 780,167 |
| Alameda County - Santa Rita Prison | Motor Efficiency | 74 | 647,018 |
| University of California at Davis | Lighting Efficiency | 240 | 1,191,790 |
| City of Oakland LEDs | Lighting Efficiency | 433 | 3,463,649 |
| Spieker Properties (16 Buildings) | Lighting Efficiency | 806 | 4,428,706 |
| Spieker Properties - VFD | VFD Retrofit | 25 | 150,320 |
| General Services Administration - Fresno IRS Bldg. | Lighting Efficiency | 160 | 1,186,000 |
| General Services Administration - 450 Golden Gate Ave., S.F. | Lighting Efficiency | 52 | 452,046 |
| GSA - Ninth District Court | Lighting Efficiency | 21 | 183,354 |
| Contra Costa County Sanitation District | Lighting Efficiency | 115 | 811,519 |
| County of Santa Cruz LED Signals | Lighting Efficiency | 47 | 385,581 |
| Town of Danville LED Signals | Lighting Efficiency | 34 | 287,257 |
| City of Hayward LED Signals | Lighting Efficiency | 118 | 1,010,933 |
| Clarion Realty Services (2 Buildings) | Lighting Efficiency | 109 | 560,743 |
| Prentiss Properties - 1901 Harrison Street, Oakland, CA | Lighting Efficiency | 91 | 466,467 |
| City of Gilroy LED Signals | Lighting Efficiency | 18 | 152,070 |
| City of Berkeley LED Signals | Lighting Efficiency | 96 | 821,593 |
| Leprino Foods | Fine Bubble Aeration | 36 | 534,575 |
| Mills Peninsula Hospital | Lighting Efficiency | 361 | 2,287,627 |
| Prentiss Properties - 180 Montgomery St., S.F. | Lighting Efficiency | 171 | 742,914 |
|  | TOTALS | 5,867 | 41,120,303 |

Appendices to the paper copies of this Proposal contain eti’s Corporate Brochure and the most recent Emerson Annual Report.

B.	Program Subcontractors – Electric City Corporation

Electric City Corporation (ELC) is a publicly traded company and having its headquarters located in Elk Grove Village, IL.  ELC has over 20 years experience in the design and manufacture of auto transformer based voltage controller systems for large HID and fluorescent lamped lighting systems.    Its national chain account customers include Food Lion, Kroger, Publix, and CVS Pharmacies.  ELC will be manufacturing and providing its Energy Saver™ product for the projects enrolled in eti’s proposed energy efficiency program.

Designed specifically for large lighting systems, the Energy Saver™ product uses proven technology to provide a cost effective but robust lighting system voltage controller for facility operators. An Appendix to this proposal contains a summary evaluation of the Energy Saver™ product’s performance by the Harris Company, an independent engineering firm.

The Energy Saver™ product modulates the voltage levels supplied to lighting circuits by pre determined amounts or in response to other inputs such as ambient natural light levels.  Better control and management of lighting systems minimizes the cost of operations, extends equipment life, and reduces down time. With the Energy Saver™ product’s capabilities a facility owner can remotely adjust light levels, modify lighting schedules, monitor energy usage, perform remote system diagnostics, and even respond to utility initiated demand response program signals.

The Appendices to the paper copies of this proposal contain ELC’s corporate brochure,

cut sheets for the Energy Saver™ and Global Commander® products, and ELC’s most recent SEC filed 10K Financial Statement.  Also found in the Appendices of the paper copies of this proposal are a summary of end user customer testimonials and associated press releases.

C.  Program Management Resumes

Resumes for eti’s key Program Management personnel follow:

# JAY RAGGIO – EE PROGRAM MANAGER

## PROFESSIONAL

CLASSIFICATION:		MANAGER-ENERGY SERVICES

HIGHLIGHTS:		Years of experience:  31 years

Certifications:  Registered Professional Engineer, Certified Energy Manager, Association of Energy Engineers

Areas of Specialization:  Program Management/Energy Analysis/Audits/Project Development

EDUCATION:		Graduate Studies-Mechanical Engineering

University of California, Berkeley

BS Mechanical Engineering

California State Polytechnic University

PROFESSIONAL

AFFILIATIONS:		Registered Professional Engineer, State of California

(License Number:M-18268)

Member of the American Society of Mechanical Engineers

Certified Energy Manager, Association of Energy Engineers

EMPLOYMENT

HISTORY:			MANGER-ENERGY SERVICES			1998

Electro-Test, Inc.					to present

San Ramon, CA

Responsible for optimizing the benefits to customers from electric utility programs including:  Utility, DSM incentives, rebates, applicable tariffs and rate structure options, and power industry deregulation.

Mange the implementation of energy efficiency services.  Develop cost effective strategies for reducing the cost of energy used by commercial, industrial, and government facilities.

EMPLOYMENT	ENERGY PROJECTS MANGER			1996

HISTORY			Electro-Test, Inc.  					to 1997

(Continued)	Danville, CA

Quantified energy consumption and usage patterns for a large, multi-site, retail chain, a commercial high-rise building, and major healthcare facilities.  Performed the project management functions for several major energy efficiency retrofit projects.  Negotiated with a major electric and gas utility to gain acceptance of a new energy saving technology in its demand side management incentive program.

BUSINESS GROUP MANGER			1988

Pacific Gas and Electric Company			to 1996

San Francisco, CA

Managed the development and implementation of a broad technical products and information program to advance the state of technology in PG&E's operations, reducing customers' costs and improving service reliability.  Led a team of twenty-five scientists, engineers, and technicians conducting over fifty technology implementation projects annually.

ENGINEERING COORDINATOR			1985

Pacific Gas and Electric, Co.				to 1988

Diablo Canyon Rate Case

Responsible for assessing and demonstrating PG&E's corporate prudence in a litigation with the California Public Utilities Commission (CPUC) to recover the $5.4 billion cost of PG&E's Diablo Canyon Nuclear Power Plant.

SENIOR MECHANICAL ENGINEER		1981

Pacific Gas and Electric, Co.				to 1985

Nuclear Projects Department

Project manger of a $20 million water treatment facility.  Responsible for cost and schedule control and management of twenty engineers assigned to the project team.

EMPLOYMENT 	MECHANICAL ENGINEER				1972

HISTORY	Pacific Gas and Electric, Co.				to 1980

(Continued)	Mechanical and Nuclear Engineering Dept.

# DENNIS REISINGER – PROJECT ENROLLMENT MANAGER

## PROFESSIONAL

CLASSIFICATION:		TECHNICAL SPECIALIST

HIGHLIGHTS:		Years of experience:  34 years

Certifications:  Registered Professional Engineer- California,

E7326

Areas of Specialization:  Energy Management, Electromagnetic Field Evaluation

EDUCATION:		BSEE, University of California, Berkeley, 1964

PROFESSIONAL

AFFILIATIONS:		Senior Member of Association of Energy Engineers

Senior Member of Association of Energy Services Professionals

Senior IEEE Member

Past Chairman, Engineering in the Safety and Maintenance of Lines Subcommittee

Member of the Bioelectromagnetic Society

Past Member , NW/SW Transmission Reliability Committee

EEI T&D, T&D Maintenance Management

Pacific Coast Electrical Association

San Francisco Energy Club

Member of the University of California Berkeley Engineering Alumni Association

EMPLOYMENT

HISTORY:			TECHNICAL SPECIALIST				1998

Electro-Test, Inc.					to present

San Ramon, CA

General Responsibilities:

Provide technical support for Energy Services, EMF characterization and assessment services, and other specialties as needed.  Develop and coordinate projects with EPRI, utilities and other interested entities.  Provide energized maintenance safety and efficiency audits including review of 115 kV to 765 kV bare handwork and bare hand-using helicopters.  Expand energy-engineering and measurement services.

MANAGER ENERGY SERVICES			1996

Electro-Test, Inc.					to 1998

Danville, CA

EMPLOYMENT	General Responsibilities:

HISTORY (Continued)	Responsible for optimizing the benefits to customers from electric utility programs including; Utility DSM incentive, rebates, applicable tariffs and rate structure options, and power Industry Deregulation.

Managed the implementation of energy efficiency services.  Developed cost effective strategies for reducing the cost of energy used by commercial, industrial, and government facilities.

Specific Accomplishments:

He led eti to be a successful bidder for Pacific Gas & Electric's demand side Management Program.  He is now supporting that 8-year program to save PG&E 8 MW of demand and 35.4 megawatt hours per year of energy.

Led internal sales personnel and outside contractors, and participated in the successful sales of demand side management to large commercial and industrial customers Sales Commitments totaled $7 million in 1997.

Developed measurement and verification strategies for hospitals, large chain store distribution centers traffic signal conversions and wastewater treatment plants.  Evaluated and implemented lightning retrofit, lighting controls, motor controls, motor efficiency, traffic light LED conversions, and waste water fine bubble aeration energy conservation measures.

TECHNICAL SPECIALIST				1993

Electro-Test, Inc.					to 1996

Danville, CA

General Responsibilities:

Developed and implemented new technical business opportunities.  Developed and coordinated R&D opportunities with EPRI, utilities, and other interested entities.  Developed and implemented, EMF characterization and assessment service and energy engineering and measurement service.  Provided training to eti personnel in field offices.

EMPLOYMENT

HISTORY (Continued)	Mr. Reisinger provided forensic analysis and expert witness services for electrical accidents, electrical equipment failure, and electric and magnetic field characterization and assessment

Assessed magnetic field exposure on field testing engineers and presented findings in poster "Occupational Magnetic Field Exposures in Electrical Industry Work Environments" June 1995 at the Bioelectromagnetics Society Annual Meeting, Boston, MA.

Audited transmission live line maintenance, helicopter bare hand maintenance, and live line department procedures of a large South African utility.  Recommendations included improved tooling, training classes and department re-organization.

MANAGING CONSULTANT			1988

Pacific Gas & Electric					to 1993

San Francisco, CA

Primary responsibility to direct development of transmission system maintenance procedures and assure worker safety.  This included hotstick and barehanded live line procedures, grounding practices, and insulator cleaning techniques.

REGION ELECTRIC OPERATIONS MANAGER	1987

Pacific Gas & Electric					to 1988

San Jose, CA

SUPERVISING ELECTRIC ENGINEER		1984

Pacific Gas & Electric					to 1987

San Francisco, CA

DISTRICT ELECTRIC SUPERINTENDENT	1983

Pacific Gas & Electric					to 1984

Richmond, CA

SUPERVISING ENGINEER				1979

Pacific Gas & Electric					to 1983

San Francisco, CA

DIVISION ELECTRIC ENGINEER			1977

Pacific Gas & Electric					to 1979

Fresno, CA

VARIOUS DISTRIBUTION ENGINEER POSITIONS 1964

Pacific Gas & Electric					      to 1977

LOU J. STIFTER – PROGRAM M&V MANAGER

## PROFESSIONAL

CLASSIFICATION:		ENERGY ENGINEER

HIGHLIGHTS:		Years of experience:  30 years

EDUCATION:	BS, Electrical Engineering, University of Arkansas, Fayetteville, Arkansas, 1969

EMPLOYMENT

HISTORY:			ENERGY ENGINEER			1998

Electro-Test, Inc.				to present

San Ramon, CA

Develops measurement and verification plans for the Demand Side Management (DSM) program.  Oversees and participates in both data collection and support for the DSM program.  Based on energy retro-fit and PG&E sampling requirements, develops plans for measuring and verifying load savings.  Discusses and defends the plan while being evaluated or challenged by PG&E or their representatives.

CONSULTANT				1997

Entor Corporation				to 1998

Santa Clara, CA

(Client:  PG&E)

CONSULTANT				1996

Advent Engineering Services			to 1997

San Ramon, CA

(Client:  Bayer)

CONSULTANT				1990

Project Assistance Corporation		to 1996

Walnut Creek, CA

(Client:  PG&E, Northern States Power)

SENIOR ENGINEER				1986

Cyna Energy Services.			to 1989

Walnut Creek, CA

(Client:  PG&E)

EMPLOYMENT

HISTORY	INSTRUMENT AND CONTROL ENGINEER	1983

(Continued)	Multi-Amp Services					to 1985

Dallas, TX

SENIOR INSTRUMENTATION ENGINEER	1981

Burns and Roe, Inc.					to 1983

Richland, WA

SENIOR ENGINEER					1980

Westinghouse Hanford Company			to 1981

Richland, WA

# JAMES KLESSIG, P.E. -  M&V FIELD SERVICES SUPERVISOR

## PROFESSIONAL

CLASSIFICATION:		SUPERVISING ENGINEER

HIGHLIGHTS:		Years of experience:  21 years

EDUCATION:			BSEE, Harvey Mudd College, Claremont, CA, 1979

Professional Training:

Field Engineering Development Program

Protective Relay Systems and Application

AC & DC Drive Systems

Power Transformer Maintenance

Generator Controls, Protection and Startup

Omega Pak Variable Frequency Drives

Ramsey Variable Frequency Drives

Advanced Vibration Analysis

## PROFESSIONAL

AFFILIATIONS:		NETA Certified Test Technician & Test Technologist #T86-106

Member IEEE

EMPLOYMENT	SUPERVISING ENGINEER		1998

HISTORY	Electro-Test, Inc.				to present

Pleasanton, CA

## Provides direct supervision of field service engineers and technicians while being responsible for all aspects of field service work in the area including customer contact, job estimating, proposal preparation, field work, scheduling, reports and billing.  Performs  complex troubleshooting, specialized tests, inspections, and appraisals on electrical apparatus and electrical systems.  Trains and assists other field service engineers.

SENIOR ENGINEER				1991

Electro-Test, Inc.				 to 1998

Pleasanton, CA

Managed the Measurement and Verification Program of eti’s demand side management contract with PG&E’s “Power Saving Partner’s” program.  Provided technical and computer support for eti field engineers and technicians.  Performed power quality analysis, control system troubleshooting, power system short

EMPLOYMENT	circuit and coordination studies, feasibility studies, harmonic

HISTORY	measurement and analysis, EMI/RFI measurement and analysis and complex relay testing.

(Continued)

Performed independent testing and startup services on co-generation facilities, distribution and transmission equipment, including all voltage classes of circuit breakers, switchgear, transformers and VFD/AFD drive systems.

Performed duties of equipment safety and electrical certification inspector.

Taught Harmonics Analysis, Harmonics and Power Quality and Introduction to System Analysis at the eti Learning Center.

FIELD ENGINEER				1984

Electro-Test, Inc.				to 1991

Pleasanton, CA

Performed simple and complex relay testing, testing and startup of power generation and distribution equipment, electrical safety inspection and certification, power quality studies, and variable speed drive startup and maintenance.

FIELD ENGINEER				1979

General Electric Co.				to 1984

Member of the Installation and Service Engineering Division International Department.  Performed start-up and troubleshooting services for power generation, distribution and utilization equipment, worldwide.

VOLUNTEER ENGINEER			1976

US Peace Corps, Nepal			to 1978

# LORI GATES – PROGRAM DATABASE ADMINISTRATOR

## PROFESSIONAL

CLASSIFICATION:		CORPORATE BUSINESS ADMINISTRATOR

EDUCATION:	Las Positas Community College – AA degree Liberal Arts and Sciences

EMPLOYMENT

HISTORY:			NATIONAL ACCOUNTS

COORDINATOR

Electro-Test, Inc.			2000

San Ramon, CA 		to present

Power Savings Partners Program: prepare and administer monthly invoicing, monthly financial reports, annual program reports, project submittals, contracts, reports, letters, and purchase orders; client, contractor and partner liaison; upgrade and maintain energy management software and custom database.

General: provide various administration services to all divisions and managers as needed.

WHOLESALE CASHIER

Ford Motor Credit Company		1996

Pleasanton, CA 			 to 2000

Provide excellent customer service to Class One truck dealers.  Assure accuracy of flooring and payments for dealers and car rental companies.  Provide assistance in obtaining UCC documentation.  Assist supervisor in preparation of audits to ensure the accuracy of flooring reports.  Provide various administrative services to all areas of branch as requested my management.

SELF EMPLOYED – MANICURIST

At Your Fingertips			1995 to 1996

ADMINISTRATIVE ASSISTANT

Growing Tree Children’s Center	1993 to 1995

CUSTOMER SERVICE

Micro-Sphere Computers		1992 to 1993

ADMINISTRATIVE SUPPORT

Various Companies			1979 to 1992

# Section VIII.	Program Budget

Large Lighting System Voltage Controller Retrofit Incentive Program

eti’s Large Lighting System Voltage Controller Retrofit Incentive Program has a proposed budget as shown in the table below:

Large Lighting System Voltage Controller Retrofit Incentive Program

for SDG&E

Proposed Program Budget

2004 -2005

The total budget for the Program for SDG&E’s service territory is $1,638,150.

| Budget Category | Budget Amount |
| --- | --- |
| Managerial & Clerical Labor | $170,750 |
| Travel & Conference Fees | $12,150 |
| Marketing/Advertising/Outreach | $6,250 |
| Direct Implementation (Financial Incentives to Customers) | $1,164,000 |
| Rebate Processing & Inspection | $15,000 |
| EM&V Labor | $270,000 |
| Total | $1,638,150 |