VERIFICATION

I affirm that the contents of this report are true to the best of my knowledge, signed under penalty of perjury this 30th day of June, 2000, in San Diego, California.

_______________________________

David L. Geier, Director

Distribution Management & Strategies

SAN DIEGO GAS and ELECTRIC

CORRECTIVE MAINTENANCE PROGRAM

REPORT FOR

1999

INTRODUCTION

The Corrective Maintenance Program (CMP) is managed through San Diego Gas and Electric’s (SDG&E) Distribution Management and Strategies Department. By coordinating with the Construction & Operations (C&O) Centers, General Foremen, Inspectors and other personnel, the inspections required by the CMP are performed and follow-up work to correct deficiencies is completed. Corrective action, for items other than those rated as needing immediate attention, is handled on a 12 months cycle.

A listing of inspection schedules is included as Attachment “A” in accordance with General Order 165.

The individual segments for 1999 are as follows:

Patrols

A simple visual inspection of applicable utility equipment and structures, that is designed to identify obvious structural problems and hazards. The patrols were performed using a “drive by” concept.

Detailed overhead visual inspection

A walking program of visual inspection of overhead facilities and primarily pole mounted equipment.

Detailed underground external inspection

An inspection cycle in which the cabinet exterior and supporting structure of each qualifying piece of equipment is inspected. This inspection includes such items as corrosion, identification and warning signage, wire entry and intrusion by dirt and surrounding vegetation. This inspection has been altered to include an internal inspection segment. The internal portion of this inspection was started on July 1, 1999. This inspection is now the same as the "Detailed underground internal inspection", however, the data is being maintained separately for future comparative purposes.

Detailed underground internal inspection

An inspection cycle in which each qualifying piece of equipment is opened for an inspection of the cabinet interior and all components as well as an inspection of the cabinet exterior and supporting structure. An internal inspection incorporates an external inspection and is a superset of the external inspection activities.

Underground oil and gas switch inspection

This is a specialized internal inspection of oil and gas filled switches found in or on underground structures (vaults, manholes, etc.). Oil samples and pressure readings are obtained and recorded, laboratory analysis of oil samples is performed.

INTRODUCTION (Cont.)

Intrusive wood pole reinforcement inspection

Wood pole inspections are performed by a contractor who performs routine inspections for integrity as well as wood preservative treatments and pole reinforcements.

1999 ANNUAL REPORT

# PATROLS

Following is the percentage of SDG&E’s system in urban and rural areas that was patrolled during 1999:

- Urban Area

- % Of system patrolled during year 100 %.

- % of system patrolled during annual cycle 100%.

- Rural Area

- % Of system patrolled during year  35%

- % of system patrolled during 2 year cycle 100%.

Following are the number of problems identified by overhead and underground patrols:

## Overhead Patrol

- Broken hardware ……………  13

- Poles leaning badly /

Damaged ……………………  4

- Broken Crossarms …………. 15

- Foreign Objects …………….  1

- Conductors …………………. 0

- Street lights broken …………0

- Critical Repair ………………. 0

=====

- Total 		                         33

## Underground Patrol

- Off Pad ………………………... 0

- Cabinet  and / or

cover or door damaged ……..  15

- Street Lights broken ………….. 0

- Critical Repair ……………….   5

- Severe Corrosion ……………  125

======

- Total                                         145

# DETAILED INSPECTIONS

## Overhead

- Detailed inspections of all poles in the overhead system will be performed on a 5-year cycle. Approximately 20% of SDG&E’s total pole population will be inspected annually. Small variations in inspected percentages may occur yearly, but 100% will be completed every 5 years. Pole mounted equipment and conductors supported by the poles are inspected at the same time. As with the poles the annual percentage may vary but 100% will be completed every 5 years.   This is the  2nd year of the cycle.

- The detailed overhead inspection requires that each pole position be visited and the pole and the equipment supported by the pole be carefully examined visually for conformance to CPUC General Order 95 requirements. By systematically inspecting all poles and the equipment they support, required equipment inspections will be completed within the time frames prescribed by General Order 165.

- Corrective action, for items other than those needing immediate attention, is handled on a 12 months cycle. Equipment and spans of conductor needing corrective action are managed by the structure that supports them.

DETAILED OVERHEAD INSPECTIONS

- Beach Cities District

- Poles

- Number of poles in District  24,629.

- Number of poles inspected during reporting year  4,451.  Inspected poles as a % of poles in District  18.07%.

- Number of poles inspected during current inspection cycle  9,392. Inspected poles as a % of poles in district  38.1%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity 1,728. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle 38.82%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Overhead Transformer Stations

- Number of overhead transformer stations in District  5,849.

- Number of overhead transformer stations inspected during reporting year  1,136.  Inspected overhead transformer stations as a % of overhead transformer stations in District  19.42%.

- Number of overhead transformer stations inspected during current inspection cycle  2,301. Inspected  transformers as a % of  transformers in district  39.34%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  2,232.

- Number of overhead switching / protective devices inspected during reporting year  519.  Inspected switching / protective devices as a % of switching / protective devices in District  23.25%.

- Number of switching / protective devices inspected during current inspection cycle  958. Inspected switching / protective devices as a % of switching / protective devices in district  42.92%.

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  177.

- Number of overhead regulator / capacitor stations inspected during reporting year  50.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  28.25%.

- Number of regulator / capacitor stations inspected during current inspection cycle  86. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  48.59%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- Beach Cities District (Cont.)

- Overhead Conductors and Cables

- Number of  spans of overhead conductors and cables in District  24,628.

- Number of spans of overhead conductors and cables inspected during reporting year  4,450.  Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  18.07%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle 9,391. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  38.13%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- Eastern District

- Number of poles in District  60,985.

- Number of poles inspected during reporting year  11,890.  Inspected poles as a % of poles in District  19.5%.

- Number of poles inspected during current inspection cycle  23,837. Inspected poles as a % of poles in district  39.09%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity  3,556. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle  29.91%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle  100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Overhead Transformer Stations

- Number of overhead transformer stations in District  17,808.

- Number of overhead transformer stations inspected during reporting year  3,602.

- Inspected overhead transformer stations as a % of overhead transformer stations in District  20.23%.

- Number of overhead transformer stations inspected during current inspection cycle  7,249. Inspected  transformers as a % of  transformers in district  40.7%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  5,188.

- Number of overhead switching / protective devices inspected during reporting year  1,232.  Inspected switching / protective devices as a % of switching / protective devices in District  23.75%.

- Number of switching / protective devices inspected during current inspection cycle  2,501. Inspected switching / protective devices as a % of switching / protective devices in district  48.2%.

- Eastern District (Cont.)

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  276.

- Number of overhead regulator / capacitor stations inspected during reporting year  83.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  30.07%.

- Number of regulator / capacitor stations inspected during current inspection cycle  164. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  59.4%.

- Overhead Conductors and Cables

- Number of spans of overhead conductors and cables in District  60,984.

- Number of spans of overhead conductors and cables inspected during reporting year  11,889. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  19.5%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle  23,836. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  39.09%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- Metro District

- Poles

- Number of poles in District  47,795.

- Number of poles inspected during reporting year  9,069.  Inspected poles as a % of poles in District  18.97%.

- Number of poles inspected during current inspection cycle  18,043. Inspected poles as a % of poles in district  37.75%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity  4,350. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle  47.97%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Overhead Transformer Stations

- Number of overhead transformer stations in District  10,811.

- Number of overhead transformer stations inspected during reporting year  2,229.

- Inspected overhead transformer stations as a % of overhead transformer stations in District  20.62%.

- Number of overhead transformer stations inspected during current inspection cycle  4,319. Inspected  transformers as a % of  transformers in district  39.95%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  3,594.

- Number of overhead switching / protective devices inspected during reporting year  840.  Inspected switching / protective devices as a % of switching / protective devices in District  23.37%.

- Number of switching / protective devices inspected during current inspection cycle  1,584. Inspected switching / protective devices as a % of switching / protective devices in district  44.07%.

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  245.

- Number of overhead regulator / capacitor stations inspected during reporting year  43.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  17.55%.

- Number of regulator / capacitor stations inspected during current inspection cycle  101. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  41.22%.

- Metro District (Cont.)

- Overhead Conductors and Cables

- Number of spans of overhead conductors and cables in District  47,794.

- Number of spans of overhead conductors and cables inspected during reporting year  9,068.  Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  18.97%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle  18,042. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  37.75%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- North Coast District

- Poles

- Number of poles in District  24,966.

- Number of poles inspected during reporting year  5,061.  Inspected poles as a % of poles in District  20.27%.

- Number of poles inspected during current inspection cycle  9,595. Inspected poles as a % of poles in district  38.43%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity  2,229. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle  44.04%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Overhead Transformer Stations

- Number of overhead transformer stations in District  7,050.

- Number of overhead transformer stations inspected during reporting year  1,500.

- Inspected overhead transformer stations as a % of overhead transformer stations in District  21.28%.

- Number of overhead transformer stations inspected during current inspection cycle  2,849. Inspected  transformers as a % of  transformers in district  40.41%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  3,113.

- Number of overhead switching / protective devices inspected during reporting year  585.  Inspected switching / protective devices as a % of switching / protective devices in District  18.79%.

- Number of switching / protective devices inspected during current inspection cycle  1,153. Inspected switching / protective devices as a % of switching / protective devices in district  37.04%.

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  119.

- Number of overhead regulator / capacitor stations inspected during reporting year  23.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  19.33%.

- Number of regulator / capacitor stations inspected during current inspection cycle  43. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  36.13%.

- North Coast District (Cont.)

- Overhead Conductors and Cables

- Number of spans of overhead conductors and cables in District  24,965.

- Number of spans of overhead conductors and cables inspected during reporting year  5,060.  Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  20.27%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle  9,594. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  38.43%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- Northeast District

- Poles

- Number of poles in District  67,328.

- Number of poles inspected during reporting year  13,516.  Inspected poles as a % of poles in District  20.07%.

- Number of poles inspected during current inspection cycle  27,433. Inspected poles as a % of poles in district  40.75%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity  3,556. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle  29.91%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle  99.99%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- P217032 - ETA 12/31/2000 - Damaged hardware, in pond/wetland, to Planning to re-route or remove.

- P319103 - ETA 12/31/2000 - Damaged pole, secondary pole with customer meter, to Planning for customer contact.

- P811639 - ETA 12/31/2000 - Pole leaning, requires stub and anchor in right-of-way, to Real Estate Operations.

- Overhead Transformer Stations

- Number of overhead transformer stations in District  21,030.

- Number of overhead transformer stations inspected during reporting year  4,055.

- Inspected overhead transformer stations as a % of overhead transformer stations in District  19.28%.

- Number of overhead transformer stations inspected during current inspection cycle  8,030. Inspected  transformers as a % of  transformers in district  38.18%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  4,769.

- Number of overhead switching / protective devices inspected during reporting year  795.  Inspected switching / protective devices as a % of switching / protective devices in District  16.67%.

- Number of switching / protective devices inspected during current inspection cycle  2,138. Inspected switching / protective devices as a % of switching / protective devices in district  44.83%.

- Northeast District (Cont.)

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  200.

- Number of overhead regulator / capacitor stations inspected during reporting year  35.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  17.5%.

- Number of regulator / capacitor stations inspected during current inspection cycle  119. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  59.5%.

- Overhead Conductors and Cables

- Number of spans of overhead conductors and cables in District  67,327.

- Number of spans of overhead conductors and cables inspected during reporting year  13,515.  Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  20.07%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle  27,432. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  40.74%.

DETAILED OVERHEAD INSPECTIONS (Cont.)

- Orange County District

- Poles

- Number of poles in District  6,174.

- Number of poles inspected during reporting year  1,140.  Inspected poles as a % of poles in District  18.46%.

- Number of poles inspected during current inspection cycle  2,327. Inspected poles as a % of poles in district  37.69%.

- Number of poles, including pole mounted equipment and spans of conductor, inspected during current inspection cycle coded as needing maintenance activity  490. Poles, including pole mounted equipment and spans of conductor, needing maintenance as a  % of poles inspected during current inspection cycle  42.98%.

- % Of needed corrective actions, including pole mounted equipment and spans of conductor, completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Overhead Transformer Stations

- Number of overhead transformer stations in District  1,377.

- Number of overhead transformer stations inspected during reporting year  234.

- Inspected overhead transformer stations as a % of overhead transformer stations in District  16.99%.

- Number of overhead transformer stations inspected during current inspection cycle  492. Inspected poles as a % of  transformers in district  35.73%.

- Overhead Switching / Protective Devices

- Number of overhead switching / protective devices in District  762.

- Number of overhead switching / protective devices inspected during reporting year  111.  Inspected switching / protective devices as a % of switching / protective devices in District  14.57%.

- Number of switching / protective devices inspected during current inspection cycle  295. Inspected switching / protective devices as a % of switching / protective devices in district  38.71%.

- Overhead Regulator / Capacitor Stations

- Number of overhead regulator / capacitor stations in District  55.

- Number of overhead regulator / capacitor stations inspected during reporting year  8.  Inspected regulator / capacitor stations as a % of regulator / capacitor stations in District  14.55%.

- Number of regulator / capacitor stations inspected during current inspection cycle  23. Inspected regulator / capacitor stations as a % of regulator / capacitor stations in district  41.82%.

- Orange County District (Cont.)

- Overhead Conductors and Cables

- Number of spans of overhead conductors and cables in District  6,173.

- Number of spans of overhead conductors and cables inspected during reporting year  1,139.  Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in District  18.46%.

- Number of spans of overhead conductors and cables inspected during current inspection cycle  2,326. Inspected spans of overhead conductors and cables as a % of spans of overhead conductors and cables in district  37.8%.

## UNDERGROUND (Pad mounted) INSPECTIONS

The underground pad mounted inspection consists of two separate inspection types:

### Dead Front Equipment

- Live Front Equipment

### Dead Front Equipment

Detailed inspections of all dead front, pad-mounted equipment, in the underground system is performed on a 5-year cycle. Approximately 20% of SDG&E’s total pad mounted dead front equipment is inspected annually. Small variations in inspected percentages may occur yearly, but 100% will be completed every 5 years. This is the 2nd year of the cycle. This inspection has been altered to include an internal inspection segment.

A detailed inspection of dead front, pad mounted equipment requires that each dead front, pad mounted piece of equipment be visited and the piece of equipment be  opened and carefully examined externally and internally, by visual methods, for conformance to CPUC General Order 128 requirements.

PAD-MOUNTED DEAD FRONT EQUIPMENT

- Beach Cities District

- Transformers

- Number of pad mounted dead front transformers in District  9,902.

- Number of pad mounted dead front transformers inspected during reporting year  2,337.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  23.60%.

- Number of pad mounted dead front transformers inspected during current inspection cycle 4,355.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  43.98%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  653. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  27.94%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED DEAD FRONT EQUIPMENT (Cont.)

- Eastern District

- Transformers

- Number of pad mounted dead front transformers in District  9,039.

- Number of pad mounted dead front transformers inspected during reporting year  2,058.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  22.77%.

- Number of pad mounted dead front transformers inspected during current inspection cycle 4,047.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  44.77%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  1,403. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  68.17%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED DEAD FRONT EQUIPMENT (Cont.)

- Metro District

- Transformers

- Number of pad mounted dead front transformers in District  9,052.

- Number of pad mounted dead front transformers inspected during reporting year  2331.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  25.75%.

- Number of pad mounted dead front transformers inspected during current inspection cycle  3,858.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  42.62%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  1,720. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  73.79%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED DEAD FRONT EQUIPMENT (Cont.)

- North Coast District

- Transformers

- Number of pad mounted dead front transformers in District  15,283.

- Number of pad mounted dead front transformers inspected during reporting year  3,453.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  22.59%.

- Number of pad mounted dead front transformers inspected during current inspection cycle  5,926.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  38.78%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  2,988. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  86.53%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED DEAD FRONT EQUIPMENT (Cont.)

- Northeast District

- Transformers

- Number of pad mounted dead front transformers in District  16,552.

- Number of pad mounted dead front transformers inspected during reporting year  3,793.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  22.92%.

- Number of pad mounted dead front transformers inspected during current inspection cycle  6,439.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  38.90%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  3,326. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  87.69%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED DEAD FRONT EQUIPMENT (Cont.)

- Orange County District

- Transformers

- Number of pad mounted dead front transformers in District  8,115.

- Number of pad mounted dead front transformers inspected during reporting year  1,745.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  21.50%.

- Number of pad mounted dead front transformers inspected during current inspection cycle 3,161.  Inspected pad mounted dead front transformers as a % of pad mounted dead front transformers in District  38.95%.

- Number of dead front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  1,049. Dead front, pad mounted transformers needing maintenance as a % of dead front, pad mounted transformers inspected during current inspection cycle  60.11%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during reporting year 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of pad mounted dead front regulators / capacitors inspected during current inspection cycle 0.  Inspected pad mounted dead front regulators / capacitors as a % of pad mounted dead front regulators / capacitors in District 0.

- Number of dead front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Dead front, pad mounted regulators / capacitors needing maintenance as a % of dead front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

### Live Front Equipment

- Detailed inspections of all live front, pad mounted equipment, in the underground system will be performed on a 5-year cycle. Approximately 20% of SDG&E’s total pad mounted live front equipment will be inspected annually. Small variations in inspected percentages may occur yearly, but 100% will be completed every 5 years. This is the  2nd year of the cycle.

- A detailed inspection of live front, pad mounted, equipment requires that each live front, pad mounted, piece of equipment be visited and the equipment be opened and carefully examined externally and internally, by visual methods, for conformance to CPUC General Order 128 requirements.

PAD-MOUNTED LIVE FRONT EQUIPMENT

- Beach Cities District

- Transformers

- Number of pad mounted live front transformers in District  821.

- Number of pad mounted live front transformers inspected during reporting year  334.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  40.68%.

- Number of pad mounted live front transformers inspected during current inspection cycle  624.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  76.00%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  99. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle  29.64%.

- % Of needed corrective actions completed during 12 month cycle  99.99%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- D2520970425 - ETA 12/31/2000 - Transformer, facility inaccessible, customer retaining wall, to Real Estate Operations for customer resolution.

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  66.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  13.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  19.7%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  30.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  45.45%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED LIVE FRONT EQUIPMENT (Cont.)

- Eastern District

- Transformers

- Number of pad mounted live front transformers in District  1,265.

- Number of pad mounted live front transformers inspected during reporting year  453.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  35.81%.

- Number of pad mounted live front transformers inspected during current inspection cycle  877.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  69.33%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  286. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle  63.13%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  17.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  1.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  5.88%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  5.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  29.41%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle  0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED LIVE FRONT EQUIPMENT (Cont.)

- Metro District

- Transformers

- Number of pad mounted live front transformers in District  1,040.

- Number of pad mounted live front transformers inspected during reporting year  359.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  34.52%.

- Number of pad mounted live front transformers inspected during current inspection cycle  725.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  69.71%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  230. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle  64.07%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  18.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  4.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  22.22%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  10.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  55.56%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity  2. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle  50.00%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED LIVE FRONT EQUIPMENT (Cont.)

- North Coast District

- Transformers

- Number of pad mounted live front transformers in District  887.

- Number of pad mounted live front transformers inspected during reporting year  302.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  34.05%.

- Number of pad mounted live front transformers inspected during current inspection cycle  569.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  64.15%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  265. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle  87.75%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  3.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  1.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  33.33%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  4.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  100%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity  1. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle 100%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED LIVE FRONT EQUIPMENT (Cont.)

- Northeast District

- Transformers

- Number of pad mounted live front transformers in District  1,348.

- Number of pad mounted live front transformers inspected during reporting year  362.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  26.85%.

- Number of pad mounted live front transformers inspected during current inspection cycle  579.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  42.95%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  309. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle  85.36%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  51.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  27.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  52.94%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  41.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  80.39%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity  23. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle  85.19%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

PAD-MOUNTED LIVE FRONT EQUIPMENT (Cont.)

- Orange County District

- Transformers

- Number of pad mounted live front transformers in District  616.

- Number of pad mounted live front transformers inspected during reporting year  159.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  25.81%.

- Number of pad mounted live front transformers inspected during current inspection cycle  312.  Inspected pad mounted live front transformers as a % of pad mounted live front transformers in District  50.65%.

- Number of live front, pad mounted transformers inspected during current inspection cycle coded as needing maintenance activity  86. Live front, pad-mounted transformers needing maintenance as a  % of live front, pad mounted transformers inspected during current inspection cycle 54.09%.

- % Of needed corrective actions completed during 12 month cycle  99.99%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- D4766456547 - ETA - 12/31/2000 - Transformer corroded, To Real Estate Operations to relocate right-of-way.

- Regulators / Capacitors

- Number of pad mounted live front regulators / capacitors in District  41.

- Number of pad mounted live front regulators / capacitors inspected during reporting year  4.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  9.76%.

- Number of pad mounted live front regulators / capacitors inspected during current inspection cycle  9.  Inspected pad mounted live front regulators / capacitors as a % of pad mounted live front regulators / capacitors in District  21.95%.

- Number of live front, pad mounted regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity  2. Live front, pad mounted regulators / capacitors needing maintenance as a % of live front, pad mounted regulators / capacitors inspected during current inspection cycle  50.00%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

## UNDERGROUND (Sub-surface) INSPECTIONS

- Detailed inspections of all underground subsurface transformers, protective devices, and regulators/capacitors, in the underground system will be performed on a 3-year cycle. Approximately 33% of SDG&E’s total population of these pieces of equipment will be inspected annually. Small variations in inspected percentages may occur yearly, but 100% will be completed every 3 years. This is the  2nd year of the cycle. A detailed inspection of underground subsurface equipment requires that each subsurface enclosure be visited and opened so that the equipment within can be carefully examined visually for conformance to CPUC General Order 128 requirements.

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS

- Beach Cities District

- Transformers

- Number of subsurface transformers in District  337.

- Number of subsurface transformers inspected during reporting year  119.  Inspected subsurface transformers as a % of subsurface transformers in District 29.3%.

- Number of subsurface transformers inspected during current inspection cycle  224.  Inspected subsurface transformers as a % of subsurface transformers in District  66.47%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity  7. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  5.88%.

- % Of needed corrective actions completed during 12 month cycle  71.43%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- M2625269300 - ETA 4/30/2001 -  Transformer, facility inaccessible, cannot open/inspect, project requires re-planning.

- M2629069350 - ETA 4/30/2001 - Transformer, facility inaccessible, cannot open/inspect, project requires re-planning.

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 1.

- Number of subsurface regulators / capacitors inspected during reporting year  1.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District  100%.

- Number of subsurface regulators / capacitors inspected during current inspection cycle  1.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District  100%.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS (Cont.)

- Eastern District

- Transformers

- Number of subsurface transformers in District  151.

- Number of subsurface transformers inspected during reporting year  34.  Inspected subsurface transformers as a % of subsurface transformers in District  22.52%.

- Number of subsurface transformers inspected during current inspection cycle  67.  Inspected subsurface transformers as a % of subsurface transformers in District  44.37%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity  18. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  52.94%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during reporting year 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS (Cont.)

- Metro District

- Transformers

- Number of subsurface transformers in District  623.

- Number of subsurface transformers inspected during reporting year  238.  Inspected subsurface transformers as a % of subsurface transformers in District  38.20%.

- Number of subsurface transformers inspected during current inspection cycle  492.  Inspected subsurface transformers as a % of subsurface transformers in District  78.97%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity  143. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  60.08%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 29.

- Number of subsurface regulators / capacitors inspected during reporting year  3.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District  10.34%.

- Number of subsurface regulators / capacitors inspected during current inspection cycle  23.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District  79.31%.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS (Cont.)

- North Coast District

- Transformers

- Number of subsurface transformers in District  139.

- Number of subsurface transformers inspected during reporting year  29.  Inspected subsurface transformers as a % of subsurface transformers in District  20.86%.

- Number of subsurface transformers inspected during current inspection cycle  62.  Inspected subsurface transformers as a % of subsurface transformers in District  44.60%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity  25. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  86.21%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during reporting year 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS (Cont.)

- Northeast District

- Transformers

- Number of subsurface transformers in District  190.

- Number of subsurface transformers inspected during reporting year  6.  Inspected subsurface transformers as a % of subsurface transformers in District  3.16%.

- Number of subsurface transformers inspected during current inspection cycle  10.  Inspected subsurface transformers as a % of subsurface transformers in District  5.26%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity 3. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  50%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during reporting year 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SUBSURFACE EQUIPMENT INSPECTIONS (Cont.)

- Orange County District

- Transformers

- Number of subsurface transformers in District  320.

- Number of subsurface transformers inspected during reporting year  73.  Inspected subsurface transformers as a % of subsurface transformers in District  22.81%.

- Number of subsurface transformers inspected during current inspection cycle  170.  Inspected subsurface transformers as a % of subsurface transformers in District  53.13%.

- Number of subsurface transformers inspected during current inspection cycle coded as needing maintenance activity  27. Subsurface transformers needing maintenance as a  % of subsurface transformers inspected during current inspection cycle  36.99%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- Regulators / Capacitors

- Number of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during reporting year 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle 0.  Inspected subsurface regulators / capacitors as a % of subsurface regulators / capacitors in District 0.

- Number of subsurface regulators / capacitors inspected during current inspection cycle coded as needing maintenance activity 0. Subsurface regulators / capacitors needing maintenance as a % of subsurface regulators / capacitors inspected during current inspection cycle 0%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

## Underground Switch (Pad mounted and sub-surface) INSPECTIONS

- Detailed inspections of all underground switches, both pad mounted and subsurface, in the underground system are performed on a 3-year cycle. Approximately 33% of SDG&E’s total population of these pieces of equipment are inspected annually. Small variations in inspected percentages may occur yearly, but 100% will be completed every 3 years. This is the  2nd year of the cycle.

- A detailed inspection of underground switches requires that each equipment location, pad mount or subsurface enclosure be visited and opened so that the equipment within can be carefully examined visually for conformance to CPUC General Order 128 requirements. In addition, oil filed switches will have the oil sampled and processed by the lab for conformance with SDG&E standards.

UNDERGROUND SWITCH INSPECTIONS

- Beach Cities District

- Number of underground switches in District  2,254.

- Number of underground switches inspected during reporting year  880.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  39.04%.

- Number of underground switches inspected during current inspection cycle  1396.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  61.93%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  167. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  18.98%.

- % Of needed corrective actions completed during 12 month cycle  97.60%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- M2418773245 - ETA 12/31/2000 - Group switch corroded, to Real Estate Operations to acquire right-of-way to raise and padmount.

- M2578170034 - ETA 12/31/2000 - Group switch leaking, to Real Estate Operations to acquire right-of-way to raise and padmount.

- M2613069420 - ETA 6/30/2000 - Group switch corroded, part of planned circuit upgrade to be constructed.

- M2629069370 - ETA 6/30/2000 - Group switch corroded, part of planned circuit upgrade to be constructed.

UNDERGROUND SWITCH INSPECTIONS (Cont.)

- Eastern District

- Number of underground switches in District  845.

- Number of underground switches inspected during reporting year  233.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  27.57%.

- Number of underground switches inspected during current inspection cycle  439.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  51.95%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  100. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  42.92%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SWITCH INSPECTIONS (Cont.)

- Metro District

- Number of underground switches in District  1,732.

- Number of underground switches inspected during reporting year  640.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  36.95%.

- Number of underground switches inspected during current inspection cycle  1,143.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  65.99%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  164. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  25.63%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SWITCH INSPECTIONS (Cont.)

- North Coast District

- Number of underground switches in District  1,234.

- Number of underground switches inspected during reporting year  308.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  24.96%.

- Number of underground switches inspected during current inspection cycle  564.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  45.70%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  186. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  60.39%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SWITCH INSPECTIONS (Cont.)

- Northeast District

- Number of underground switches in District  1,212.

- Number of underground switches inspected during reporting year  433.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  35.73%.

- Number of underground switches inspected during current inspection cycle  866.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  71.45%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  278. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  64.20%.

- % Of needed corrective actions completed during 12 month cycle 100%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

UNDERGROUND SWITCH INSPECTIONS (Cont.)

- Orange County District

- Number of underground switches in District  754.

- Number of underground switches inspected during reporting year  265.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  35.15%.

- Number of underground switches inspected during current inspection cycle  524.  Inspected underground switches as a % of equipment in sub-surface enclosures in District  69.50%.

- Number of underground switches inspected during current inspection cycle coded as needing maintenance activity  103. Number of underground switches needing maintenance as a  % of the number of underground switches inspected during current inspection cycle  38.87%.

- % Of needed corrective actions completed during 12 month cycle  99.99%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

- M4796555885 - ETA 12/31/2000 - Subsurface group switch, zero gas pressure, job created 4/12/2000 to raise and padmount.

INTRUSIVE POLE INSPECTION

## Wood Pole

- Intrusive inspections of all poles in the overhead system are performed in conformance with CPUC General Order 165 requirements. Approximately 10% of SDG&E’s poles over 15 years of age, that have not had a previous intrusive inspection, will be inspected annually, creating a 10 year inspection cycle. This is the  2nd year of the cycle.  SDG&E poles that are older than 15 years and have had a previous intrusive inspection will be inspected on a 20-year cycle with approximately 5% of these poles being inspected annually.  This is the  2nd year of the cycle.

- Small variations in inspected percentages may occur yearly, but 100% will be completed in conformance with CPUC General Order 165 requirements.

- The intrusive pole testing program at SDG&E is a centralized program that systematically addresses all SDG&E poles on a system wide basis and not on a district by district process. Program direction and records are handled on a centralized basis.

- Intrusive testing of wood poles is normally accomplished by excavating about the pole base and/or a sound and bore of the pole about the groundline area for conformance to CPUC General Order 95 requirements.

### 10 Year Inspection Cycle

- Number of poles in Company  231,889.

- Number of poles inspected during reporting year  24,472.  Inspected poles as a % of poles in Company  10.6%.

- Number of poles inspected during current inspection cycle  48,086. Inspected poles as a % of poles in Company  20.7%.

- Number of poles inspected during current inspection cycle coded as needing maintenance activity  898. Number of poles needing maintenance as a  % of the number of poles inspected during current inspection cycle  3.7%.

- % Of needed corrective actions completed during 12 month cycle  99.99%. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

20-Year Inspection Cycle - SDG&E is inspecting all wood poles on a 10-year cycle at this time.

- Number of poles in Company ____NA___

- Number of poles inspected during reporting year ____NA____.  Inspected poles as a % of poles in Company ___NA____.

- Number of poles inspected during current inspection cycle ___NA_____. Inspected poles as a % of poles in Company.

INTRUSIVE POLE INSPECTION (Cont.)

- Number of poles inspected during current inspection cycle coded as needing maintenance activity ___NA___. Number of poles needing maintenance as a  % of the number of poles inspected during current inspection cycle __NA__ %.

- % Of needed corrective actions completed during 12 month cycle ____NA_____. *

- If this answer is not 100% explain and provide date corrective actions to be completed by:

ATTACHMENT

“A”