June 30, 2006

Stephen Larson

Executive Director

California Public Utilities Commission

505 Van Ness Avenue, Room 5222

San Francisco, California  94102-3298

RE:	PacifiCorp’s (U 901-E) Plan for Inspections, Record Keeping, and Reporting

D.97-03-070

I.95-02-015/R.96-11-004

As required by California D.97-03-070, Appendix A, dated March 31, 1997, PacifiCorp provides an original and five copies of the attached annual report for Inspections, Record Keeping, and Reporting.

If you have any questions regarding this report, please contact Shay LaBray (503) 813-6176.

Respectfully Submitted,

Shay LaBray

Manager, Regulation

Enclosure

Cc:	Wade McCartney, Energy Division

Brian Schumacher, Energy Division

BEFORE THE PUBLIC UTILITES COMMISSION

OF THE STATE OF CALIFORNIA

Commission Order Instituting Investigation	)

into the rates, charges, services, and		)	I.95-02-015

practices of Pacific Gas and Electric		)	(Filed February 22, 1995)

Company.  (U 39 M)				)

____________________________________

Order Instituting Rulemaking for electric	)	R.96-11-004

distribution facility standard setting.		)	(Filed November 8, 1996)

PACIFICORP’S (U901-E) IMPLEMENTATION PLAN FOR INSPECTIONS

USING INDICES SET FORTH IN APPENDIX A OF D.97-03-070

FOR CALENDAR YEAR 2005

PacifiCorp

Inspection and Maintenance Programs

California 2005

The attached sheets demonstrate the status of 2005 Inspections, Conditions found and Corrections in the state of California for PacifiCorp owned facilities.  PacifiCorp has four districts in California: Tulelake, Alturas, Crescent City and Yreka/Mt. Shasta.

# Inspections

Inspections of poles and equipment were completed in 2005 for Urban & Rural Patrol, Detail and Intrusive inspection types.  The information includes the type of equipment, the plan for each inspection category and the actual results of the inspection plan.

# Conditions

Conditions found by the inspections were rated as either A or B priority, with A priority requiring more immediate action than B priority conditions.  All A priority conditions will be completed as soon as possible but in no case later than 12/31/2006.  The B priority conditions found in 2005 are being prioritized and will be completed per Company policy.

The report outlines the following requirements aggregated by district:

- number of conditions found in 2005;

- number of conditions corrected as of December 31, 2005;

- number of conditions outstanding as of December 31, 2005; and

- correction target for immediate hazard and lower priority conditions.

Dated in Portland, Oregon this 28th day of June 2006.

Respectfully Submitted,

Bill Cunningham

Managing Director

825 NE Multnomah, Suite 1500

Portland, Oregon 97232

Bill.Cunningham@PacifiCorp.com

(503) 813-6151 (phone)

(503) 813-6892 (fax)