EleCTRIC SYSTEM RELIABILITY

ANNUAL REPORT

2000

Prepared for

California Public Utilities Commission

February 10, 2001

EXECUTIVE SUMMARY

This Electric System Reliability Annual Report for 2000 has been prepared in response to CPUC Decision 96-09-045.  This Decision imposed additional reliability recording, calculation, and reporting requirements on SDG&E.

The data in this report is presented in tabular form.  System statistics are computed as follows: (1) including transmission, substation, and distribution outages, and (2) excluding planned outages.  SAIDI (System Average Interruption Duration Index) and SAIFI (System Average Interruption Frequency Index) values include sustained outages, which are defined as outages lasting 5 minutes or more.  MAIFI (Momentary Average Interruption Frequency Index) values include momentary outages, which are defined as outages lasting less than 5 minutes.  The units for the reliability measures are:

- SAIDI - minutes of sustained outages per customer per year

- SAIFI - number of sustained outages per customer per year

- MAIFI - number of momentary outages per customer per year.

For the purposes of this report, all calculations include forced outages and exclude planned outages. The measurement of each reliability performance indicator excludes CPUC major events and events that are the direct result of failures in the ISO-controlled bulk power market or non-SDG&E owned transmission facilities.  Major events are defined in CPUC Decision 96-09-045 as an event that meets at least one of the following criteria:

- The event is caused by earthquake, fire, or storms of sufficient intensity to give rise to a state of emergency being declared by the government, or

- Any other disaster not in (1) that affects more than 15% of the system facilities or 10% of the utility’s customers, whichever is less for each event.

A summary of 2000 values follows:

The largest outage event in 2000, which occurred on September 7-8, was due to a lightning storm which affected 13,258 customers.

In 2000, no customers within SDG&E’s territory experienced more than one outage (lasting 5 minutes or more) per month on a rolling annual average basis, after exclusion of major events.

The reliability values in this report differ in some respects from the values reported under SDG&E’s Performance Based Ratemaking (PBR) program.  The values in this report conform to the requirements of CPUC Decision 96-09-045.

TABLE OF CONTENTS

HISTORICAL SYSTEM RELIABILITY DATA	1

TEN LARGEST OUTAGE EVENTS IN 2000	2

TEN LARGEST OUTAGE EVENTS IN 1999	3

TEN LARGEST OUTAGE EVENTS IN 1998	4

TEN LARGEST OUTAGE EVENTS IN 1997	5

TEN LARGEST OUTAGE EVENTS IN 1996	6

TEN LARGEST OUTAGE EVENTS IN 1995	7

TEN LARGEST OUTAGE EVENTS IN 1994	8

TEN LARGEST OUTAGE EVENTS IN 1993	9

TEN LARGEST OUTAGE EVENTS IN 1992	10

TEN LARGEST OUTAGE EVENTS IN 1991	11

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 2000	12

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1999	12

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1998	13

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1997	13

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1996	14

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1995	15

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1994	16

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1993	16

TABLE OF CONTENTS (CONTINUED)

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1992	17

EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM
THE 10 LARGEST OUTAGE EVENTS) FOR 1991	18

CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES
IN A ROLLING 12 MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 2000	19

CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES
IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1999	20

CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES
IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1998	21

CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES
IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1997	22

CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES
IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS)
FOR 1991-1996	23

# HISTORICAL SYSTEM RELIABILITY DATA

# TEN LARGEST OUTAGE EVENTS IN 2000*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1999*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1998*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1997*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1996*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1995*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1994*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1993*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1992*

*Based on SAIDI impact.

# TEN LARGEST OUTAGE EVENTS IN 1991*

*Based on SAIDI impact.

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 2000

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1999

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1998

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1997

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1996

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1995

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1994

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1993

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1992

# EXCLUDABLE CPUC MAJOR EVENT DETAILS (EXTRACTED FROM THE 10 LARGEST OUTAGE EVENTS) FOR 1991

# CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 2000

Data is based upon station outages as reported through SDG&E’s Outage Management System.

# CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1999

Data is based upon station outages as reported through SDG&E’s Outage Management System.

# CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1998

Data is based upon station outages as reported through SDG&E’s Outage Management System.

# CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1997

Data is based upon station outages as reported through SDG&E’s Outage Management System.

# CUSTOMERS EXPERIENCING MORE THAN 12 SUSTAINED OUTAGES IN A ROLLING 12-MONTH PERIOD (EXCLUDING CPUC MAJOR EVENTS) FOR 1991-1996

| Year | District | Circuit Number | Number of Customers Experiencing >12 Sustained Outages |
| --- | --- | --- | --- |
| 1991 |  |  | None |
| 1992 |  |  | None |
| 1993 |  |  | None |
| 1994 |  |  | None |
| 1995 |  |  | None |
| 1996 |  |  | None |

Data for years 1991 through 1994 is based upon complete circuit outages due to historical data limitations.

Data for 1995-1996 is based upon station outages as reported through SDG&E’s Outage Management System.

# Text boxes

##### San Diego Gas & Electric – Distribution Management and Strategies Department

##### San Diego Gas & Electric – Distribution Management and Strategies Department