# General

This is the 2002 Reliability Report for Pacific Gas & Electric Company as required by Decision 96-09-045.  It includes four sections:

- System Indices For The Last 10 Years (1993-2002)

- Significant Outage Events Of 2002

- Customers Experiencing >12 Sustained Outages In 2002

- Historical (1993-2001) Outage Information From Prior Reports

PG&E maintains historical account specific information for customers affected by recorded outages in the Outage reporting system (OUTAGE).  This system tracks outages at the generation, transmission, substation, primary distribution, and individual transformer levels.  Additionally, OUTAGE models the actual electric switching during the circuit restoration process (which is useful for determining customer outage minutes for calculating SAIDI).  PG&E used this data, and information from other databases, to compile the information contained in this report.

System Indices (1993-2002)

Table 1 lists the required final SAIDI, SAIFI, and MAIFI values in accordance with Appendix A of Decision 96-09-045.  It should be noted that electric outage notification (EON) devices were installed during 1994-95 to obtain momentary outage information on automatic non-SCADA sectionalizing devices.  This deployment accounts for much of the MAIFI increase noted after 1994.

The data provided in the prior annual Table 1 reports is outdated and the revised annual values are updated below.  These changes are a result of (a) centralization of outage data records, (b) utilization of a new data query tool that improved data accuracy, and (c) minor individual outage changes due to error corrections.

Table 1 - System Indices (1993-2002)

(Includes Transmission, Distribution and Generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | MAIFI | SAIDI | SAIFI | MAIFI |
| 1993 | 176.5 | 1.680 | 1.876 | 151.4 | 1.549 | 1.807 |
| 1994 | 160.3 | 1.721 | 1.952 | 155.4 | 1.540 | 1.872 |
| 1995 | 600.2 | 2.616 | 2.216 | 170.2 | 1.537 | 1.649 |
| 1996 | 347.0 | 2.462 | 4.855 | 178.1 | 1.709 | 4.654 |
| 1997 | 171.3 | 1.700 | 4.430 | 161.8 | 1.639 | 4.335 |
| 1998 | 317.0 | 2.130 | 3.835 | 180.0 | 1.659 | 3.407 |
| 1999 | 157.2 | 1.481 | 2.427 | 156.7 | 1.477 | 2.420 |
| 2000 | 168.4 | 1.413 | 2.282 | 167.9 | 1.410 | 2.281 |
| 2001 | 249.1 | 1.559 | 2.256 | 211.8 | 1.439 | 2.120 |
| 2002 | 381.9 | 1.670 | 2.576 | 139.2 | 1.112 | 1.998 |

Included in this annual report is supplemental information noted in Tables 2 and 3 representing the corresponding indexes separated for both the distribution and transmission systems.  It should be noted that the totals from these two new tables will not exactly match Table 1 for the following reasons:

- Generation related outages are included in Table 1;

- There are database limitations related to the major event exclusion process when separating the transmission and distribution systems.

Please also note, the MAIFI information is not included in these tables since the existing automatic recording (EON) devices do not distinguish between the two systems.

Table 2 - Distribution System Indices (1993-2002)

(Excludes transmission and generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | SAIDI | SAIFI |
| 1993 | 159.3 | 1.545 | 136.9 | 1.424 |
| 1994 | 139.2 | 1.400 | 139.2 | 1.400 |
| 1995 | 536.6 | 2.393 | 150.3 | 1.384 |
| 1996 | 198.4 | 1.685 | 167.1 | 1.632 |
| 1997 | 157.3 | 1.562 | 148.4 | 1.507 |
| 1998 | 245.0 | 1.812 | 157.3 | 1.493 |
| 1999 | 145.1 | 1.324 | 144.8 | 1.321 |
| 2000 | 152.3 | 1.293 | 151.8 | 1.290 |
| 2001 | 228.6 | 1.430 | 192.5 | 1.315 |
| 2002 | 343.7 | 1.549 | 131.6 | 1.046 |

Table 3 - Transmission System Indices (1993-2002)

(Excludes distribution and generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | SAIDI | SAIFI |
| 1993 | 17.1 | 0.135 | 14.5 | 0.125 |
| 1994 | 20.5 | 0.292 | 17.6 | 0.155 |
| 1995 | 63.6 | 0.223 | 19.9 | 0.152 |
| 1996 | 148.2 | 0.773 | 14.8 | 0.129 |
| 1997 | 13.8 | 0.138 | 13.2 | 0.132 |
| 1998 | 72.0 | 0.318 | 22.6 | 0.166 |
| 1999 | 12.1 | 0.157 | 11.9 | 0.155 |
| 2000 | 15.2 | 0.108 | 15.2 | 0.108 |
| 2001 | 20.5 | 0.129 | 19.3 | 0.123 |
| 2002 | 37.7 | 0.120 | 7.6 | 0.066 |

Significant Outage Events During 2002

Table 4 lists the ten largest outage events experienced during 2002.  PG&E interprets this reporting requirement as the ten days (or in some cases consecutive days) with significant number of customer interruptions in the system or portion of the system.  These events are listed in order of customer interruptions.

Table 4 - Ten Largest 2002 Outage Events

| Rank | Description | Date | Number of Customer Interruptions* | Longest Customer Interruption (Hours) | Number of People Used To Restore Service | CPUC Major Event? |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | During the December 13-21 storms the highest wind speeds were recorded on December 16 when peak winds ranged from 40 to over 80 mph throughout the service area, except for the southern San Joaquin Valley. Peak gusts over 90 mph were recorded at ridgeline sites along the North Coast and Bay Area. Peak winds over 40 mph were reported in the San Joaquin Valley on December 19. In the northern half of the service area between 5 and 15 inches of rainfall was reported, with over 20 inches of rain reported at some stations in the coastal hills north of the Bay Area and Northern Sierra foothills. | 12/13 –12/21 | 1,973,806 | 543 | >3,200** | Y |
| 2 | During the November 7-8 storms, peak wind speeds ranged from 30 to over 60 mph throughout the service area, except for the southern San Joaquin Valley. Peak gusts over 90 mph were recorded at ridgeline stations in the Bay Area. Storm rainfall totals generally ranged from one to three inches throughout the service area, with over five inches recorded at some stations in the coastal hills. | 11/7 – 11/8 | 885,431 | 121 | >3,200** | Y |
| 3 | A series of storm systems moved through the Service Area during this four day period. These storm systems were accompanied by strong gusty winds, especially on the 28th, late on the 30th, and early on the 31st. Peak wind speeds on the 28th included 54 mph in San Francisco, 44 mph in Oakland, 47 mph in Redding, and 43 mph in Bakersfield. Peak wind speeds on the 31st included 103 mph at Kregor Peak, 72 mph at Las Trampas Ridge, 54 mph in San Francisco, 54 mph in Santa Rosa, 49 mph in Concord, and 46 mph in Redding | 12/28 – 12/31 | 356,505 | 146 | Not Requested | N |
| 4 | A heat wave enveloped the entire Service Area beginning on July 8th. Temperatures in the interior valley remained above 100 Deg F through July 15th. The maximum temperatures on the 9th included 92 Deg F in Oakland, 90 in San Francisco, 103 in Santa Rosa, 102 in Concord, 107 in Livermore, 104 in Sacramento, 106 in Fresno. On the 10th, maximum temperatures reached 110 Deg F in Stockton and Sacramento and 115 in Redding. On the 11th, maximum temperatures included 109 in Ukiah, 112 in Redding, 106 in Fresno, and 109 in Bakersfield. | 07/09 – 07/11 | 164,238 | 46 | Not Requested | N |
| 5 | A cold front moved through the Service Area on the 14th and 15th accompanied by gusty west and northwest winds. Peak wind speeds included 52 mph in San Francisco, 52 mph at Los Banos, 43 mph in Redding, 41 mph at Stockton, 41 mph in Fresno, and 37 mph in Bakersfield. | 04/14 – 04/15 | 97,105 | 25 | Not Requested | N |
| 6 | Gusty north winds developed over northern and central portions of the Service Area as a strong high pressure system moved into the Great Basin. Peak wind speeds included 37 mph in San Francisco, 35 mph in Red Bluff, 38 mph in Redding, and 37 mph in Stockton. | 02/28 – 03/01 | 93,922 | 44 | Not Requested | N |
| 7 | An early summer heat wave affected the area with maximum temperatures in the interior valley in the mid-90s to near 100 deg F. Maximum temperatures on the 29th included 96 Deg F in Red Bluff, 95 in Redding, 94 in Stockton, and 94 in Fresno. Maximum temperatures on the 30th included 98 in Redding, 94 in Sacramento, 99 in Stockton, 101 in Fresno, and 99 in Bakersfield. | 05/29-05/30 | 87,244 | 135 | Not Requested | N |
| 8 | A Transmission system outage occurred in Diablo division. | 11/19 | 59,023 | 7 Minutes | Not Requested | N |
| 9 | A storm system pushed through the Service Area on the 6th and 7th accompanied by one to two inches of rain and gusty southerly winds. Peak wind speeds included 37 mph in San Francisco, 43 mph in Red Bluff, and 38 mph in Stockton. | 03/07 | 51.847 | 23 | Not Requested | N |
| 10 | Gusty north winds occurred in the northern half of the Service Area with 39 mph at Red Bluff, 37 mph at San Francisco, 25 mph at Redding, and 24 mph at Stockton. | 03/17 | 46,065 | 23 | Not Requested | N |

* Note:  Values exclude single distribution line transformer and planned outages.  Values reflect all customers in PG&E’s service territory affected by outages for those dates.

** Note:  Values are estimates of the number of PG&E electric field personnel working.  These numbers do not include any non-PG&E personnel.

Of the ten largest events listed in Table 4, two events, November 7-8 and December 13-21, met the CPUC definition of a major event.  Tables 5 & 6 indicate the number of customers without service at the requested periodic intervals for this event.

## Table 5 – November 7-8, 2002 Outage Event Duration Summary

| Outage Duration | Date of Outage | Description of Outage | Number of Customer Interruptions |
| --- | --- | --- | --- |
| 0 TO 1 HRS | 11/7-8/2002 | Noted in Table 4 | 148,826 |
| 1 TO 5 HRS | " | " | 434,220 |
| 5 TO 10 HRS | " | " | 147,786 |
| 10 TO 15 HRS | " | " | 61,686 |
| 15 TO 20 HRS | " | " | 29,368 |
| 20 TO 24 HRS | " | " | 13,523 |
| >=1 AND <=2 Days | " | " | 40,519 |
| >=2 AND <=3 Days | " | " | 2,413 |
| >=3 AND <=4 Days | " | " | 673 |
| >=4 AND <=5 Days | " | " | 248 |
| >=5 AND <=6 Days | " | " | 50 |

Note:  The number of customer outages segmented by restoration period requires a

level of detail not normally maintained by PG&E in its central computerized records.

The information shown above is what PG&E has been able to reconstruct from several

databases and may have a margin of error of around 5%.

# Figure 1 – November 7-8, 2002 Outage Event Duration Summary

Table 6 – December 13-21, 2002 Outage Event Duration Summary

| Outage Duration | Date of Outage | Description of Outage | Number of Customer Interruptions |
| --- | --- | --- | --- |
| 0 TO 1 HRS | 12/13-21/2002 | Noted in Table 4 | 337,928 |
| 1 TO 5 HRS | " | " | 890,960 |
| 5 TO 10 HRS | " | " | 335,885 |
| 10 TO 16 HRS | " | " | 108,435 |
| 15 TO 20 HRS | " | " | 93,117 |
| 20 TO 24 HRS | " | " | 53,358 |
| >=1 AND <=2 Days | " | " | 84,153 |
| >=2 AND <=3 Days | " | " | 25,199 |
| >=3 AND <=4 Days | " | " | 13,902 |
| >=4 AND <=5 Days | " | " | 5,516 |
| >=5 AND <=6 Days | " | " | 2,240 |
| >=6 AND <=7 Days | " | " | 913 |
| > 7 Days | " | " | 998 |

Note:  The number of customer outages segmented by restoration period requires a

level of detail not normally maintained by PG&E in its central computerized records.

The information shown above is what PG&E has been able to reconstruct from several

databases and may have a margin of error of around 5%.

# Figure 2 – December 13-21, 2002 Outage Event Duration Summary

Customers Experiencing > 12 Sustained Outages During 2002

Table 7 lists all circuits where one or more customers on a circuit experienced more than 12 sustained outages in 2002.  Please note, this list does not mean all the customers on the circuit experienced more than 12 outages.

PG&E is addressing the necessary portions of these circuits as part of the overall service reliability improvement plans.

Table 7 - Customers Experiencing > 12 Sustained Outages During 2002

| Division | Feeder Name | Customers Experiencing > 12 Outages |
| --- | --- | --- |
| CENTRAL COAST | CAMP EVERS 2104 | 90 |
| CENTRAL COAST | LOMPICO 0401 | 4 |
| DIABLO | CONTRA COSTA 2109 | 8 |
| FRESNO | DEVILS DEN 1101 | 1 |
| NORTH BAY | CALISTOGA 1102 | 52 |
| NORTH BAY | SILVERADO 2105 | 31 |
| NORTH COAST | EEL RIVER 1101 | 89 |
| NORTH COAST | GARBERVILLE 1101 | 38 |
| NORTH COAST | GARBERVILLE 1102 | 76 |
| NORTH COAST | MONTE RIO 1111 | 2 |
| NORTH VALLEY | LOGAN CREEK 2101 | 53 |
| SAN JOSE | LLAGAS 2104 | 28 |
| YOSEMITE | COTTLE 1702 | 3 |

Historical (1993-2001) Outage Information From Prior Reports

For easy reference, Attachment 1 contains copies of service reliability report information previously submitted for 1993 through 2001.

Attachment 1

Historical (1993-2001) Outage Information From Prior Reports