Table 2 - Largest 1998 Outage Events

| Rank | Description | Date | Number of Customers Affected | Longest Customer Interruption (Hours) | Number of People Used to Restore Service | CPUC Major Event? |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | A series of weather systems pounded northern and central California bringing heavy rains and periods of strong winds. Coastal and coastal mountain areas south of Cape Mendocino were hardest hit. Many service area weather stations reported between 10 and 20 inches of rain during the 12-day period. Widespread flooding resulted along rivers and streams from the Sacramento and Russian Rivers and south as a result of the heavy rains on Feb 3, and additional flooding occurred in the Bay Area and Central Coast areas on Feb 7 and 8. Gusty winds in excess of 50 mph were reported on Feb 1, 2 and 3. On Feb 3, a wind gust of 81 mph was reported along at Pigeon Point and many Central Coast stations reported gusts over 60 mph. Later that day a gust of 58 mph was reported at Bakersfield. Strong thunderstorms were reported on Feb 6 and 7, with a tornado spotted at Sunnyvale on Feb 7. | January 31-Feburary 11 | 1,855,983 | 222.8 | 5,200 | Yes |
| 2 | San Francisco, Northern Peninsula Outage – Human error. Refer to PG&E’s “December 8 1998 Outage Investigation Report” dated January 25, 1999 for complete details. | December 8 | * 496,304 | 7.8 | Not requested | Yes |
| 3 | A strong storm system brought periods of moderate rain and gusty winds to northern and central portions of the service area. Wind gusts above 40 mph were recorded at many Sacramento Valley and Bay Area weather stations. | November 6-7 | 269,880 | 5.1 | Not requested | No |
| 4 | Strong high pressure and offshore winds combined to produce the most intense heat wave in the East Bay Area in several years. Nearly all weather stations in central and eastern Contra Costa and Alameda counties reported afternoon temperatures at or above 105F on August 3 and 4, with Livermore reaching 110F on August 4. | August 2-5 | 268,679 | 28.8 | Not requested | No |
| 5 | A series of storms moved through the service area, the strongest events were on Dec 2-3 and Dec 5. Over 2 inches of rain was reported at Eureka on Dec 2; wind speeds gusted to 40 mph at Redding. On Dec 3, wind gusts of 25-45 mph were recorded in the Bay Area and Sacramento Valley. The December 5 storm was stronger in the Bay Area and Central Coast areas, with San Francisco Airport winds gusting to 51 mph. Strong thundershower activity developed during the afternoon, with tornado reported in the Bay Area and Santa Cruz County areas. Winds in the Sacramento and northern San Joaquin Valley gusted from 25 to 43 mph. | December 2-6 | 225,475 | 30.1 | Not requested | No |
| 6 | Temperatures warmed into the 80’s near the coast and 90’s inland on Jun 15 as northerly flow developed. Strong gusty northerly winds developed on Jun 16, with reported gusts of 47 mph at Travis AFB and gusts to 46 mph at Marysville, Sacramento and Vaca-Dixon. Most other Central Valley stations recorded wind gusts between 30 and 45 mph. | June 14-16 | 218,998 | 46.6 | Not requested | No |
| 7 | A cold storm brought winds of 35-45 mph to the North Coast and Bay Areas on March 28. Most locations had less than 0.50 inches of rain. Afternoon thunderstorm activity was reported at many locations in the service area. | March 28-29 | 194,480 | 11.3 | Not requested | No |
| 8 | A warm frontal storm brought periods of moderate to heavy rains and strong winds to the northern half of the service area. Redding received over 1.25 inches of rain each day with winds gusting to 51 mph on Nov 30. Wind gusts to 53 mph were recorded along the North Coast at Mendocino, and gusts to 40 mph were recorded in the Sacramento Valley. | November 29-30 | 179,717 | 30.8 | Not requested | No |
| 9 | The first storm of the winter season moved across the service area. Winds gusted to 35 mph in Fresno. Between 0.25 and 1.25 inches of rain was recorded in the Bay Area. | October 24 | 123,261 | 20.5 | Not requested | No |
| 10 | A strong winter storm resulted in wind gusts to 51 mph at Redding and brought over one inch of rain to the north Sacramento Valley. Wind gusts above 40 mph were also recorded along the North Coast. | November 23 | 102,980 | 47.5 | Not requested | No |

Note:  Values exclude single distribution line transformer and planned outages

*  Updated March 1, 2000

Table 3 - January 31 through February 11, 1998 Outage Event Duration Summary

| Outage Duration | Date of Outage | Description of Outage | Number of Customers Affected |
| --- | --- | --- | --- |
| 0 TO 1 HRS | 01/31/98 - 02/11/98 | Noted in Table 2 | 456,453 |
| 1 TO 5 HRS | " | " | 882,947 |
| 5 TO 10 HRS | " | " | 152,189 |
| 10 TO 16 HRS | " | " | 68,188 |
| 15 TO 20 HRS | " | " | 41,539 |
| 20 TO 24 HRS | " | " | 37,559 |
| >1 AND <=2 Days | " | " | 46,730 |
| >2 AND <=3 Days | " | " | 12,498 |
| >3 AND <=4 Days | " | " | 3,956 |
| >4 AND <=5 Days | " | " | 701 |
| >5 AND <=6 Days | " | " | 360 |
| >6 AND <=7 Days | " | " | 980 |
| >7 Days | " | " | 262 |

Note:  The number of customer outages segmented by restoration period requires a level of detail not normally maintained by PG&E in its central computerized records.  The information shown above is what PG&E has been able to reconstruct from several databases and may have a margin of error of around 5%.

| Figure 1 - January 31 through February 11, 1998 Outage Event Duration Summary |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |

Table 4 - December 8, 1998 Outage Event Duration Summary  -  Revised March 1,2000

| Outage Duration | Date of Outage | Description of Outage | Number of Customers Affected |
| --- | --- | --- | --- |
| 0 TO 1 HRS | 12/8/98 | Noted in Table 2 | 49,886 |
| 1 TO 5 HRS | " | " | 250,518 |
| 5 TO 10 HRS | " | " | 203,568 |

Note:  The number of customer outages segmented by restoration period requires a level of detail not normally maintained by PG&E in its central computerized records.  The information shown above is what PG&E has been able to reconstruct from several databases and may have a margin of error of around 5%.

Figure 2 - December 8, 1998 Outage Event Duration Summary  -  Revised March 1,2000

Table 5 - Customers Experiencing > 12 Sustained Outages During 1998

| Division | Feeder Name | # Customers Experiencing > 12 Outages |
| --- | --- | --- |
| CENTRAL COAST | POINT MORETTI 1101 | 39 |
| CENTRAL COAST | SAN ARDO 1102 | 332 |
| DE ANZA | CAMP EVERS 2106 | 443 |
| DE ANZA | LOS GATOS 1106 | 402 |
| DIABLO | CONTRA COSTA 2109 | 40 |
| FRESNO | ALPAUGH 1106 | 13 |
| FRESNO | DUNLAP 1103 | 298 |
| FRESNO | STROUD 1101 | 37 |
| LOS PADRES | SANTA MARIA 1105 | 3 |
| NORTH BAY | NAPA 1102 | 173 |
| NORTH BAY | SILVERADO 2105 | 3 |
| NORTH COAST | FORT BRAGG STA A 1 | 3 |
| NORTH COAST | MONTE RIO 1111 | 117 |
| NORTH COAST | MONTE RIO 1113 | 1,361 |
| NORTH COAST | POINT ARENA 1101 | 10 |
| NORTH VALLEY | CAPAY 1102 | 15 |
| NORTH VALLEY | CHALLENGE 1101 | 116 |
| NORTH VALLEY | ELK CREEK 1101 | 55 |
| NORTH VALLEY | ESQUON 1101 | 14 |
| NORTH VALLEY | JACINTO 1101 | 19 |
| NORTH VALLEY | LOGAN CREEK 2101 | 7 |
| PENINSULA | HALF MOON BAY 1103 | 473 |
| SACRAMENTO | CORDELIA 1104 | 17 |
| SACRAMENTO | RICE 1102 | 8 |
| SIERRA | EL DORADO P H 2101 | 85 |
| STOCKTON | OLETA 1101 | 67 |
| STOCKTON | SALT SPRINGS 2101 | 34 |
| YOSEMITE | COTTLE 1701 | 94 |