## Slide 1
DRMEC Spring 2014
Load Impacts Evaluation Workshop
SCE’s 2013 Summer Discount Program Evaluation
May 11, 2015

## Slide 2: Agenda
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 3
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 4: 1. Program Overview
SDP is an A/C cycling program with over 300,000 residential and over 10,000 commercial participants.
Residential participants may select 100% or 50% cycling options. Commercial customers have an additional option of 30% cycling.
The majority of participants are enrolled with 100% cycling.
Residential
Commercial
~320,000 Participants
~12,000
Participants

## Slide 5: 1. Program Overview
SCE called 11 residential and 9 commercial SDP events during the DR season.
This is the first year for which commercial customers have been called for multi-hour events.
All participants were called for all events.
Hottest summer day.

## Slide 6
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 7: 2. Estimation Approach
Residential impacts were estimated using panel data, commercial impacts were estimated using individual customer regressions.
Estimated based on sample of ~25% of all participants.
Sample divided into strata based on the unique combination of A-bank and cycling strategy.
Sample within stratum selected to ensure that distribution of consumption during RA window (1pm – 6pm) of sample was representative of the stratum.
Panel data regression (fixed effects).
Separate regression estimated for groups of participants defined by unique combination of A-bank and cycling strategy
Impacts averaged across groups and output for each combination of cycling strategy and LCA and by aggregations of these categories.
Residential Impacts
Entire participant population used.
Individual regression estimated for each participant (previously, PY2013, panel data approach was used).
Impacts averaged across individuals and output by:
  Cycling strategy
  LCA
  Industry type.
Commercial Impacts

## Slide 8: 2. Estimation Approach
The ex-post regressions model impacts using a battery of dummy variables – one for each event (and snapback) hour observed in 2014.
The residential panel data analysis regression:
Only data from non-holiday weekdays included.
Panel model above estimated for each of the 69 residential strata.
Commercial model very similar, only applied to an individual time-series instead of a panel set.
No PTR variables in commercial regression.
SDP program impacts

## Slide 9: 2. Estimation Approach
Ex-ante estimation very similar to ex-post but with battery of event dummies replaced with event/temperature interaction dummy variable.
From the equation above, these terms
Are replaced by these terms:
Instead of modeling impacts as one-off deviations from a baseline, they are modeled as a function of outdoor temperature to allow for prediction of ex-ante impacts.
Snapback is modeled as a function of the total cooling degree hours observed over the course of the event.

## Slide 10
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 11: 3. Ex-Post Impacts
Ex-post residential impacts appear reasonable and consistent with results in other years and other programs
Plots for all events, by LCA and cycling strategy may be found in the full report Appendices.
kWh
Hour Ending (PPT)

## Slide 12: 3. Ex-Post Impacts
Average impact of 0.73 kW/ event is slightly lower than PY2013 (0.86 kW/ event).
This is likely due to 2013 events being warmer (91OF, on average) and earlier in the day (mostly 3pm – 5pm) compared with 2014 (half of events end at 8pm)
Avg. impact: 0.73 kW
Avg. event temp: 89O F
Ex-post residential per-participant impacts are closely correlated average event temperature.

## Slide 13: 3. Ex-Post Impacts
Ex-post commercial impacts appear reasonable and continue to display negligible snapback, even for longer events.
Plots for all events, by LCA and cycling strategy may be found in the full report Appendices.
kWh

## Slide 14: 3. Ex-Post Impacts
Time of day may be an important driving factor: estimated impacts appear to be higher when events begin earlier.
Time of year may also be an important driving factor: impacts appear to be higher in September than in July and August.
Avg. impact: 4.2 kW
Avg. event temp: 88O F
Ex-post commercial impacts per participant are not as strongly correlated with outdoor temperature as residential impacts.

## Slide 15: 3. Ex-Post Impacts
Program impacts during the September 2013 heat wave were between over 375 and nearly 450 MW.

## Slide 16
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 17: 4. Ex-Ante Impacts
Monthly Peak Day | May | June | July | August | September
1-in-2 | 0.55 | 0.64 | 0.86 | 1.01 | 0.94
1-in-10 | 0.91 | 0.95 | 1.01 | 1.18 | 1.08
Ex-ante forecast residential per-participant impacts are in line with expectations given ex-post impacts
Ex-Ante Impacts

## Slide 18: 4. Ex-Ante Impacts
Ex-ante forecast commercial per-participant impacts are in line with expectations given ex-post impacts
Monthly Peak Day | May | June | July | August | September
1-in-2 | 2.5 | 3.0 | 4.2 | 5.3 | 5.0
1-in-10 | 4.8 | 4.7 | 4.9 | 6.1 | 5.9
Ex-Ante Impacts

## Slide 19: 4. Ex-Ante Impacts
Declining forecast program enrollment will mean lower ex-ante predicted impacts in future years.
August Peak Day Impacts

## Slide 20
3
Ex-Post Impacts
2
Estimation Approach
1
Program Overview
4
Ex-Ante Impacts
5
Conclusions & Recommendations

## Slide 21: 5. Conclusions & Recommendations
Residential impacts are consistent, reliable and well-understood.
Residential impacts are reliable and reasonably consistent year to year.
The accuracy and precision of the residential ex-ante impact estimates could be improved by establishing one (or several) M&V sample groups that could be subject to a wider variety of events (by month, time of day, etc.) – there has only been a single event covering the period 1pm – 2pm (first hour of RA window) over the past 3 years (in 2012).

## Slide 22: 5. Conclusions & Recommendations
Commercial impacts show much greater variation than residential.
Establishing a carefully-selected commercial M&V group for additional events could improve the accuracy and precision of ex-ante impacts (e.g., by testing how time-of-day and month of year affects commercial impacts)
Most commercial participants are small businesses contributing moderate DR impacts, but there are a small number of very large participants that are contributing very large impacts (e.g. just 3 commercial participants contribute 5% of total impacts).
In future, these large customers should be split from the main group of commercial customers and analyzed separately and in greater depth to better understand their contribution to the program’s DR capability.
Commercial impacts warrant additional exploratory analysis.

## Slide 23
Greg Wikler
Director
One Market Street
Spear Street Tower, Suite 1200
San Francisco, CA 94105
greg.wikler@navigant.com
415.399.2109
Peter Steele-Mosey
Managing Consultant
333 Bay St., Suite 1250
Toronto, ON M5H 2R2
peter.steele-mosey@navigant.com
416.956.5050