## Slide 1: PG&E’s SmartAC Program June 3, 2013 Michael Perry Freeman, Sullivan & Co.

## Slide 2: Overview of PG&E’s SmartAC Program
AC load control through installation of control devices that limit the duty cycles of AC units
Residential and small/medium businesses (SMB)
Two types of devices: switches and PCTs
Events called:
  For testing purposes; or
  Under emergency; or
  In anticipation of emergency conditions between May 1st and October 31st, up to 6 hours or less in each event, for a maximum of 100 hours per season
149,200 residential accounts and 5,800 SMB accounts at end of summer 2012

## Slide 3: SmartAC Ex Post Methodology
Basic analytical requirement for ex post SmartAC impact evaluation is the estimation of a reference load during event periods
2012 evaluation was based on the use of control groups for every test event
Residential estimates were based on the use of SmartMeter interval data with very large treatment and control groups (~12,000 treatment customers/event)
Dually enrolled customer’s usage were analyzed separately due to overlap with SmartRate event days
No SMB events were called in 2012
Ex post impacts were calculated by comparing the average event day usage in the control group to the average event day usage in the treated group

## Slide 4: SmartAC 2012 Residential Ex Post Impacts (Excluding Dually-Enrolled Customers)
*Two test events were called on 10/1/2012. One lasted from 2-5 PM; the other lasted from 4-6 PM.
†System-wide event day. The percent of the population was reduced by a factor of 10 before being included in the average.
Event Date | Event Hours | Average Whole-Building Reference Load (kW) | Average Event Impact (kW) | Percent Impact | Percent of Population Called | Average Temperature (°F)
7/9/12 | 4-5 pm | 2.02 | 0.50 | 25% | 10% | 91
7/10/12 | 4-5 pm | 2.41 | 0.70 | 29% | 10% | 97
7/11/12 | 4-5 pm | 2.86 | 0.72 | 25% | 10% | 100
7/12/12 | 4-5 pm | 2.83 | 0.69 | 24% | 10% | 97
8/2/12 | 4-5 pm | 2.39 | 0.65 | 27% | 10% | 95
8/10/12 | 4-5 pm | 2.88 | 0.53 | 19% | 100%† | 99
8/13/12 | 4-5 pm | 3.02 | 0.73 | 24% | 10% | 100
9/13/12 | 4-5 pm | 1.93 | 0.47 | 24% | 10% | 92
9/14/12 | 4-5 pm | 1.91 | 0.34 | 18% | 10% | 90
10/1/12 | 4-5 pm | 2.07 | 0.38 | 19% | 11% | 97
10/1/12* | 4-5 pm | 2.07 | 0.52 | 25% | 11% | 97
Average | 4-5 pm | 2.40 | 0.57 | 24% | 10% | 96

## Slide 5: Dually-enrolled SmartAC/SmartRate Customers
A much higher percentage of SmartAC customers were also enrolled in SmartRate for this year’s evaluation than past evaluations: Nearly 26,800 customers (compared to 4,700 in 2011), or 18%
SmartRate customers provide lower impacts on non-SmartRate days
Date | Hour | Impact |  | Total Treated and Control | 
 |  | SmartAC-only | Dually-Enrolled | SmartAC-only | Dually-Enrolled
12-Jul-12 | 2 – 3 PM | 0.59 | 0.35 | 104,058 | 17,876
 | 3 – 4 PM | 0.60 | 0.34 | 104,058 | 17,876
 | 4 – 5 PM | 0.69 | 0.39 | 104,058 | 17,876
2-Aug-12 | 4 – 5 PM | 0.65 | 0.36 | 105,164 | 17,904
 | 5 – 6 PM | 0.51 | 0.28 | 105,164 | 17,904
13-Aug-12 | 3 – 4 PM | 0.77 | 0.20 | 105,575 | 17,911
 | 4 – 5 PM | 0.73 | 0.19 | 105,575 | 17,911
 | 5 – 6 PM | 0.78 | 0.21 | 105,575 | 17,911

## Slide 6: Dually Enrolled Customers Have Smaller Loads, Lower Impacts
Chart: SmartAC Only Event Day: July 12, 2012
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | SmartAC only | Dually-Enrolled
Untreated | 1.1278 | 0.93585 | 0.81527 | 0.74016 | 0.70286 | 0.71517 | 0.78189 | 0.86428 | 0.95142 | 1.0672 | 1.2294 | 1.4521 | 1.7265 | 2.0216 | 2.3226 | 2.6094 | 2.8316 | 2.9474 | 2.8996 | 2.6455 | 2.3203 | 2.045 | 1.6577 | 1.2862 | 0.98817 | 0.81844 | 0.71443 | 0.65071 | 0.61678 | 0.63508 | 0.71887 | 0.80247 | 0.86155 | 0.93223 | 1.0399 | 1.1723 | 1.3549 | 1.5498 | 1.7151 | 1.937 | 2.1582 | 2.3074 | 2.3249 | 2.2088 | 1.9998 | 1.7672 | 1.4124 | 1.0752
Treated | 1.1157 | 0.92677 | 0.80922 | 0.73828 | 0.69459 | 0.71149 | 0.77565 | 0.86136 | 0.94487 | 1.0574 | 1.2184 | 1.4335 | 1.721 | 2.0176 | 1.728 | 2.0129 | 2.1406 | 3.0648 | 3.1223 | 2.8288 | 2.4757 | 2.153 | 1.7075 | 1.3195 | 0.97387 | 0.80799 | 0.7091 | 0.64333 | 0.62542 | 0.63305 | 0.71508 | 0.78382 | 0.85386 | 0.95109 | 1.0558 | 1.1973 | 1.3807 | 1.5643 | 1.3613 | 1.5994 | 1.7653 | 2.5119 | 2.5662 | 2.3901 | 2.0918 | 1.833 | 1.4518 | 1.0994

## Slide 7: Distribution of Impacts
Local Capacity Area | Impact from 4-5 PM (kW) | Average Temperature (°F)
Greater Bay Area | 0.39 | 90
Greater Fresno | 0.77 | 103
Kern | 0.97 | 102
Northern Coast | 0.26 | 90
Other | 0.60 | 99
Sierra | 0.66 | 98
Stockton | 0.62 | 97
Monthly Usage Decile | Average Monthly Usage (kW) | Average Impact from 4-5 PM (kW)
1 | 212 | 0.28
2 | 329 | 0.43
3 | 399 | 0.48
4 | 459 | 0.53
5 | 518 | 0.57
6 | 581 | 0.62
7 | 654 | 0.67
8 | 745 | 0.69
9 | 881 | 0.71
10 | 1,284 | 0.78
Average Event Impacts by LCA
Average Event Impacts by Usage Decile

## Slide 8: Distribution of Impacts Across Usage Deciles
Chart: Hour Ending
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
First Decile - Control | 0.34942 | 0.29887 | 0.27089 | 0.2543 | 0.24938 | 0.25787 | 0.28937 | 0.31207 | 0.32328 | 0.34065 | 0.37391 | 0.43445 | 0.51706 | 0.6235 | 0.75843 | 0.92112 | 1.0687 | 1.1667 | 1.1598 | 1.0535 | 0.9208 | 0.79112 | 0.6169 | 0.47192
First Decile - Treatment | 0.33944 | 0.29149 | 0.2633 | 0.25032 | 0.24489 | 0.25625 | 0.28752 | 0.30837 | 0.31723 | 0.33475 | 0.36762 | 0.43007 | 0.49789 | 0.60559 | 0.74612 | 0.91119 | 0.78764 | 0.92409 | 1.282 | 1.1553 | 0.95795 | 0.77947 | 0.6066 | 0.46608
Tenth Decile - Control | 1.4958 | 1.3132 | 1.207 | 1.1492 | 1.1351 | 1.199 | 1.3776 | 1.5248 | 1.6031 | 1.7244 | 1.899 | 2.1093 | 2.3754 | 2.6707 | 2.985 | 3.2904 | 3.5707 | 3.7311 | 3.7388 | 3.5417 | 3.2536 | 2.8973 | 2.3754 | 1.8999
Tenth Decile - Treatment | 1.502 | 1.3288 | 1.2218 | 1.1624 | 1.1537 | 1.2198 | 1.3714 | 1.5131 | 1.5972 | 1.7418 | 1.9066 | 2.1181 | 2.3921 | 2.7013 | 2.9894 | 3.3187 | 2.859 | 3.118 | 3.9791 | 3.8262 | 3.3905 | 2.9481 | 2.411 | 1.9308

## Slide 9
Evaluation is required to produce forecasts of load impacts under specified weather conditions
Our method is to use ex post impacts as inputs into a model describing relationship between impacts and temperature
Similar method used for both residential and SMB
Ex post impacts for SMB were taken from 2011 events
Ex Ante Methodology

## Slide 10: Ex Ante Model
Three steps:
  Regress 4-5 PM ex post impacts at LCA-level on customer-weighted average temperature for midnight-5 PM within each LCA
  Use regression to predict impacts for 4-5 PM under ex ante conditions
  Predict impacts for other hours (1-4 PM, 5-6 PM) based on observed ratios between impact at 4-5 PM and impact at each other hour (ratios are LCA-specific and vary with temperature)
Commercial model is essentially the same, but makes concessions for smaller sample sizes
  LCA-specific temperatures, but one model across all LCAs

## Slide 11: Ex Ante Adjustments
2 new adjustments were made this year for residential ex ante analysis
  Scaling up first hour impact
  Dually-Enrolled Customers
Customers started the test events on average 15 minutes into the hour, meaning they are not reaching full impact potential
  To correct: scaled up first hour impact by 60/45=1.33, representing the potential of the program once all AC units are controlled
Mentioned previously, dually enrolled customers provide smaller impacts
  Ex post impacts were adjusted to include dually enrolled customers

## Slide 12: Ex Ante Adjustment: Dually-Enrolled
Average Residential Impacts and Temperatures
from 4-5 PM on 2011 and 2012 Event Days
Average Residential Impacts and Temperatures
from 4-5 PM on 2011 and 2012 Event Days
(2012 Adjusted)

## Slide 13: Ex Ante Methodology (example)
Average Event Impacts From 4-5 PM Versus Mean17 Across All LCAs
Unified model across all LCAs, rather than LCA-specific models

## Slide 14: SmartAC 2012 Residential Ex Ante Impacts
1-in-2 weather year, highest aggregate mean impact from 1-6 PM is on the July peak day, with an impact of 104 MW
Highest individual hourly impact during a 1-in-2 year is also the July value – 125 MW
The July peak day also shows the highest impacts for the 1-in-10 weather year. The largest aggregate impact over the five-hour event is 129 MW and highest individual hour provides an estimated impact of 149 MW

## Slide 15: SmartAC 2012 SMB Ex Ante Impacts
1-in-2 weather year, highest aggregate mean impact from 1-6 PM is on the July peak day, with an impact of 3.6 MW
Highest individual hourly impact during a 1-in-2 year is also the July value – 4.3 MW
July peak day also shows the highest impacts for the 1-in-10 weather year—average 1-6 PM impact of 4.1 MW and peak hourly impact of 4.8 MW

## Slide 16: Questions?
Contact Information
Michael Perry
Freeman, Sullivan & Company
michaelperry@fscgroup.com
415-777-0707
Christine Hartmann
Freeman, Sullivan & Company
christinehartmann@fscgroup.com
415-777-0707