## Slide 1: San Diego Gas & Electric Summer Saver Evaluation Freeman, Sullivan & Co July 25, 2012
Notes: Housekeeping
Introduce EPRI and FSC
Recording session, etc.
Welcome, have everyone introduce themselves to see who is there
Want to focus on your comments questions… please ask questions throughout

## Slide 2: Program Overview
AC load control program with switches only
Commercial and residential customers
Customers cannot override
Payments based on cycling option and weekend availability
Customer Type | Cycling Option | Enrolled Customers | Enrolled Control Devices | Enrolled Tons
Commercial | 30% | 1,882 | 4,627 | 17,447
 | 50% | 3,262 | 8,134 | 31,069
 | Total | 5,144 | 12,761 | 48,516
Residential | 50% | 11,375 | 13,360 | 46,456
 | 100% | 13,072 | 15,961 | 57,165
 | Total | 24,447 | 29,321 | 103,621
Grand Total |  | 29,591 | 42,082 | 152,137

## Slide 3: Program Payments
Residential (average 3.8 tons per AC)
  100%: $49.00 per ton
  50%: $11.50 per ton
Commercial (average 3.6 tons per AC)
  50%: $15.00 per ton
  30%: $ 9.00 per ton
Each customer gets $10 for weekend availability
Credits are applied annually

## Slide 4: Estimating Program Impacts
The objective is to determine the impact of an event-based DR program
We must model a premise’s hourly usage to predict what a premise’s usage would have been in the absence of the program
In an ideal setting we would use a randomized control group
In the absence of a control group, we can turn to alternate methods such as:
  Regression
  Day matching
  Baselines

## Slide 5: Modeling A Premise’s Hourly Load
A good model accurately predicts a premise’s usage on event like days
Chart: Hour Ending
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Average of Actual | 0.97349 | 0.86275 | 0.78203 | 0.67838 | 0.64808 | 0.67299 | 0.7578 | 0.85937 | 0.92201 | 1.0316 | 1.1896 | 1.2885 | 1.4116 | 1.5899 | 1.7866 | 1.8131 | 1.9001 | 1.8662 | 1.8186 | 1.6035 | 1.4867 | 1.4283 | 1.2272 | 0.95973
Average of Predicted | 0.85991 | 0.76157 | 0.69503 | 0.65581 | 0.64841 | 0.66421 | 0.73126 | 0.79493 | 0.84857 | 0.98535 | 1.1445 | 1.2932 | 1.5378 | 1.6394 | 1.7691 | 1.8225 | 1.7865 | 1.7542 | 1.6056 | 1.4769 | 1.4462 | 1.3337 | 1.1543 | 0.92003

## Slide 6: Challenges
Absence of hot non-event days
Chart: Hour Ending
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
8/2/2011 | 702.18 | 592.163 | 550.41 | 523.663 | 524.644 | 551.269 | 600.788 | 669.711 | 726.399 | 834.147 | 980.913 | 1129.012 | 1241.262 | 1346.822 | 1502.086 | 1599.899 | 1674.38 | 1722.349 | 1669.695 | 1483.303 | 1446.153 | 1377.923 | 1151.071 | 927.133
8/25/2011 | 714.662 | 632.792 | 593.756 | 554.302 | 548.106 | 574.541 | 656.554 | 709.791 | 727.382 | 840.179 | 954.985 | 1047.249 | 1189.603 | 1398.946 | 1507.782 | 1595.669 | 1694.269 | 1668.821 | 1607.122 | 1485.089 | 1516.585 | 1389.758 | 1200.559 | 956.527
7/5/2011 | 732.456 | 645.551 | 598.371 | 578.399 | 568.043 | 591.243 | 634.61 | 692.262 | 780.492 | 894.447 | 986.974 | 1129.007 | 1255.33 | 1408.483 | 1500.846 | 1582.518 | 1574.348 | 1578.604 | 1584.297 | 1552.517 | 1558.75 | 1449.98 | 1233.121 | 961.985
7/8/2011 | 862.871 | 741.549 | 662.654 | 619.644 | 590.781 | 640.761 | 689.283 | 764.623 | 853.26 | 972.667 | 1112.898 | 1216.188 | 1314.448 | 1438.325 | 1570.463 | 1619.743 | 1606.245 | 1563.768 | 1508.896 | 1396.681 | 1317.381 | 1250.417 | 1093.704 | 878.206
8/29/2011 | 840.048 | 685.691 | 632.159 | 604.873 | 599.981 | 632.616 | 710.139 | 762.324 | 773.482 | 872.872 | 1015.698 | 1217.326 | 1414.12 | 1571.384 | 1696.167 | 1811.877 | 1792.347 | 1738.1 | 1633.775 | 1519.955 | 1450.212 | 1292.22 | 1048.971 | 844.644
7/6/2011 | 835.409 | 723.494 | 663.59 | 627.18 | 610.914 | 655.896 | 728.34 | 779.052 | 873.401 | 1012.875 | 1157.985 | 1310.868 | 1480.802 | 1582.103 | 1663.051 | 1708.647 | 1677.936 | 1702.31 | 1696.251 | 1564.824 | 1433.552 | 1383.59 | 1218.917 | 949.95
7/7/2011 | 765.693 | 662.778 | 615.075 | 594.566 | 577.567 | 624.827 | 663.079 | 743.429 | 847.223 | 969.276 | 1157.685 | 1305.217 | 1472.333 | 1604.879 | 1748.989 | 1837.549 | 1807.73 | 1815.485 | 1783.207 | 1629.362 | 1524.541 | 1451.631 | 1261.949 | 1056.239
9/6/2011 | 681.932 | 590.666 | 551.533 | 535.483 | 538.979 | 590.864 | 699.738 | 760.754 | 749.31 | 823.883 | 872.784 | 933.703 | 1044.038 | 1274.785 | 1486.274 | 1732.809 | 1980.09 | 2088.395 | 2148.305 | 2060.545 | 2070.392 | 1856.888 | 1499.37 | 1208.423
9/7/2011 | 999.64 | 856.443 | 753.365 | 717.923 | 684.067 | 712.145 | 806.116 | 833.024 | 908.583 | 1062.009 | 1290.117 | 1552.723 | 1880.659 | 2041.126 | 1646.278 | 1549.233 | 1595.953 | 1667.361 | 2423.394 | 2564.636 | 2314.985 | 2074.072 | 1691.497 | 1296.301

## Slide 7: Challenges
On September 8th there was a power outage
Sep 9th was a much cooler event day, with average temp of 73
Chart: Hour Ending
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
7-Sep-11 | 1.0871 | 0.93157 | 0.82171 | 0.78035 | 0.73561 | 0.75409 | 0.85036 | 0.8998 | 0.99895 | 1.1576 | 1.3894 | 1.6793 | 2.0276 | 2.2118 | 1.7544 | 1.662 | 1.7216 | 1.8047 | 2.6375 | 2.7991 | 2.5437 | 2.2725 | 1.845 | 1.4016
8-Sep-11 | 1.2119 | 1.0323 | 0.89923 | 0.8053 | 0.75187 | 0.76537 | 0.86325 | 0.94556 | 1.041 | 1.1927 | 1.376 | 1.6296 | 1.9142 | 1.6293 | 1.6167 | 1.0291 | 0 | 0 | 0.0034837 | 0.0082941 | 0.047222 | 0.1437 | 0.24417 | 0.32346
9-Sep-11 | 0.44556 | 0.65726 | 0.84815 | 0.76307 | 0.70452 | 0.71247 | 0.78861 | 0.84396 | 0.86899 | 0.91128 | 0.9378 | 0.97911 | 1.04 | 1.0833 | 1.051 | 1.06 | 1.1105 | 1.1064 | 1.2343 | 1.2467 | 1.2294 | 1.1258 | 0.97976 | 0.83037

## Slide 8: Analysis Methodology Residential
Individual customer regressions
Used SmartMeter data from 770 residential customers
Controlled for weather and occupancy patterns
  Hourly variables designed to pick up occupancy patterns
  Weighted averages of previous hours temperatures to pick up weathers impact

## Slide 9: Analysis Methodology Commercial
The commercial ex post analysis used day matching because individual customer regressions failed to accurately model load
Same day adjustments were used
Ex ante involves a simple regression of impacts on a temperature variable
Incorporated 2010 data

## Slide 10: Ex Post Load Impacts
There were 6 events in 2011
At its 2011 Peak on Sep 7th, the program provided an average of 24 MW during the 2-6 PM Event
  19 MW from residential customers
  5 MW for commercial customers
Excluding anomalous days, 2010 and 2011 ex post impacts were very similar
Class | Impact |  |  | Average Temperature | 
 | Per CAC Unit (kW) | Per Premise (kW) | Aggregate (MW) | Midnight-5 PM | During Event
Resideintail | 0.48 | 0.57 | 14 | 78 | 87
Commercial | 0.29 | 0.75 | 3.7 | 76 | 85
Program Average | 0.42 | 0.6 | 17.7 | 77 | 86

## Slide 11: Ex Ante
Residential
  Delivers 14 MW and 12 MW on a typical Event Day in 1-in-10 and 1-in-2 weather years respectively
  Delivers 24 MW under the most extreme weather conditions
Commercial
  Delivers 5.1 MW and 4.6 MW on a typical event day in 1-in-10 and 1-in-2 weather years respectively
  Delivers 6.2 MW under the most extreme weather conditions
Enrollment is expected to be stable for the foreseeable future