General

This is the 1997 Reliability Report for Pacific Gas & Electric Company as required by Decision 96-09-045.  It includes four sections:

- System Indices Of The Last 10 Years (1988-1997)

- Significant Outage Events Of 1997

- Customers Experiencing >12 Sustained Outages In 1997

- Historical (1988-1996) Outage Information From Prior Reports

PG&E maintains historical account specific information for customers affected by recorded outages in the Distributed Outage Reporting Computer Application system (D-ORCA).  This system tracks outages at the generation, transmission, substation, primary distribution, and individual transformer levels.  Additionally, D-ORCA models the actual electric switching during the circuit restoration process (which is useful for determining customer outage minutes for calculating SAIDI).  PG&E used this data, and information from other data bases, to compile the information contained in this report.

System Indices (1988-1997)

Table 1 lists final SAIDI, SAIFI, and MAIFI values for 1997 in accordance with Appendix A of Decision 96-09-045, in addition to SAIDI, SAIFI, and MAIFI values for the prior nine years.

Table 1 - System Indices (1988-1997)

|  | Major Event Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | MAIFI | SAIDI | SAIFI | MAIFI |
| 1988 | 191.8 | 2.09 | 1.55 | 146.6 | 1.76 | 1.41 |
| 1989 | 356.5 | 2.11 | 1.50 | 142.7 | 1.82 | 1.46 |
| 1990 | 219.7 | 1.75 | 1.41 | 132.2 | 1.58 | 1.37 |
| 1991 | 150.1 | 1.65 | 1.34 | 150.1 | 1.65 | 1.34 |
| 1992 | 143.3 | 1.61 | 1.37 | 143.3 | 1.61 | 1.37 |
| 1993 | 176.7 | 1.74 | 1.36 | 151.6 | 1.61 | 1.31 |
| 1994 | 157.7 | 1.76 | 1.46 | 152.9 | 1.57 | 1.39 |
| 1995 | 572.4 | 2.63 | 1.71 | 164.9 | 1.55 | 1.27 |
| 1996 | 322.5 | 2.37 | 6.52 | 163.2 | 1.65 | 6.30 |
| 1997 | 170.6 | 1.70 | 4.37 | 160.9 | 1.63 | 4.25 |

Note:   Electric outage notification (EON) devices were installed during 1994-95 to obtain momentary outage information on automatic non-SCADA sectionalizing devices.  This deployment can account for much of the MAIFI increase noted after 1994.

Significant Outage Events During 1997

Table 2 lists the ten largest outage events experienced during 1997.  PG&E interprets this reporting requirement as the ten days (or in some cases consecutive days) with significant number of customer interruptions in the system or portion of the system.  These events are listed in order of customer interruptions.  As can be seen, nine of the ten significant events in 1997 were related to weather conditions.

Table 2 - Ten Largest 1997 Outage Events

| Rank | Description | Date | Number Of Customers Affected | Longest Customer Interruption (Hours) | Number Of People Used To Restore Service | CPUC Major Event? |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | A series of weather fronts with periods of gusty wind, thunderstorms and heavy rains resulting in flood conditions in Sacramento, Placer, Butte, and Solano counties. | January 22-26 | 349,314 | 80.2 | Not requested | No |
| 2 | Strong and gusty northernly winds in northern and central California. Wind speeds of 45 to 50 mph in the Bay area hills and 50 to 70 mph in the Sierras were experienced. | April 1-3 | 341,119 | 27.2 | Not requested | No |
| 3 | Series of warm moisture laden storms crossed the service territory during the last days of December 96 and the first days of January 97. Heavy rainfall and high elevation rain melting the Sierra snowpack triggered widespread flooding which resulted in a state of emergency being declared in 37 California counties during the first week of January. | January 1-4 | 322,958 | 105.6 | 1086 | Yes |
| 4 | Gusty northerly winds occurred over this two day period. Wind gusts of 25 to 62 mph were recorded throughout the service area. | February 23-24 | 205,812 | 60.5 | Not requested | No |
| 5 | Scattered showers and thunderstorm activity experienced in most of northern and central California. A transmission outage occurred in the north coast area caused by lightning. | August 19-20 | 179,199 | 34.0 | Not requested | No |
| 6 | Major San Francisco substation outage due to sabotage. | October 23 | 137,209 | 14.4 | Not requested | No |
| 7 | A strong Alaskan weather system moved through the northwest corner of the state. Wind speeds reached 50 to 80 mph in the Humbolt and Del Norte county areas with heavy rain. This storm reached the Bay Area, Redwood region, and Sacramento Valley with 20-30 mph winds recorded. | November 18-19 | 136,313 | 85.4 | Not requested | No |
| 8 | Pacific storm with gusty winds of 30-65 mph, thunderstorms, and periods of heavy rainfall were experienced throughout the service territory. | November 26 | 122,523 | 52.5 | Not requested | No |
| 9 | Storm system with widespread thunderstorm activity, rainfall, and up to 38 mph winds. | November 10-11 | 120,274 | 53.3 | Not requested | No |
| 10 | A fast moving weather system with heavy rains and gusty 25-35 mph winds in the Sacramento, north coast, central coast, and Bay Area. | November 15 | 93,958 | 28.8 | Not requested | No |
| Note: Values exclude single distribution line transformer and planned outages. |  |  |

Of the ten largest outage events listed in Table 2, only the one occurring on January 1st through the 4th. met the CPUC definition of a major event.  Table 3 below indicates the number of customers without service at the requested periodic intervals for this event.

Table 3 - Jan 1st through Jan 4th 1997 Outage Event Duration Summary

| Outage Duration | Date Of Outage | Description Of Outage | Number Of Customers Affected |
| --- | --- | --- | --- |
| 0 to 1 hour | Jan 1st - Jan 4th | Noted in Table 2 | 89,555 |
| 1 to 5 hours | “ | “ | 185,898 |
| 5 to 10 hours | “ | “ | 22,245 |
| 10 to 15 hours | “ | “ | 6,114 |
| 15 to 20 hours | “ | “ | 1,724 |
| 20 to 24 hours | “ | “ | 1,005 |
| 1 to 2 days | “ | “ | 34 |
| 2 to 3 days | “ | “ | 4 |
| 3 to 4 days | “ | “ | 56 |
| 4 to 5 days | “ | “ | 0 |
| 5 to 6 days | “ | “ | 0 |
| > 7 days | “ | “ | 0 |

Note:  The number of customer outages segmented by restoration period requires a level of detail not normally maintained by PG&E in its central computerized records.  The information shown above is what PG&E has been able to reconstruct from several databases and may have a margin of error of around 5%.

Customers Experiencing > 12 Sustained Outages During 1997

Table 4 lists all circuits where one or more customers on the circuit experienced more than 12 sustained outages in 1997.  Please note, this list does not mean all the customers on the circuit experienced more than 12 outages in 1997.

PG&E is addressing the necessary portions of these circuits as part of the overall service reliability improvement plans.

Historical (1988-1996) Outage Information From Prior Reports

For easy reference, Attachment 1 contains service reliability report information which was submitted previously for 1988 through 1996.

Table 4 - Customers Experiencing > 12 Sustained Outages During 1997

| Division | Feeder Name | Number of Customers Experiencing > 12 Sustained Outages |
| --- | --- | --- |
| CENTRAL COAST | BEN LOMOND 0401 | 38 |
|  | BEN LOMOND 1101 | 159 |
|  | CAMP EVERS 2106 | 282 |
|  | LOMPICO 0401 | 337 |
|  | POINT MORETTI 1101 | 96 |
|  | ROB ROY 2104 | 286 |
|  | SAN ARDO 1102 | 101 |
|  | SOLEDAD 2101 | 200 |
|  | WATSONVILLE 2101 | 1,137 |
| DE ANZA | CAMP EVERS 2104 | 949 |
|  | CAMP EVERS 2105 | 415 |
|  | LOS GATOS 1107 | 3 |
| DIABLO | SAN RAMON 2105 | 79 |
| KERN | TUPMAN 1104 | 1 |
| LOS PADRES | BUELLTON 1101 | 30 |
|  | SISQUOC 1103 | 2 |
|  | TEMPLETON 2109 | 22 |
| NORTH BAY | CALISTOGA 1101 | 41 |
|  | PUEBLO 1104 | 51 |
| NORTH COAST | ANNAPOLIS 1101 | 10 |
|  | FORT ROSS 1121 | 78 |
|  | MIRABEL 1102 | 15 |
|  | MONTE RIO 1111 | 6 |
|  | MONTE RIO 1113 | 27 |
|  | OLEMA 1101 | 35 |
|  | SALMON CREEK 1101 | 378 |
| NORTH VALLEY | CRESCENT MILLS. 2101 | 207 |
|  | ESQUON 1101 | 15 |
|  | ESQUON 1103 | 1 |
|  | GANSNER 1101 | 128 |
|  | GERBER 1102 | 21 |
|  | ORLAND STATION B 1103 | 5 |
| SACRAMENTO | ARBUCKLE 1102 | 5 |
|  | RICE 1102 | 15 |
| SAN JOSE | MC KEE 1103 | 4 |
| SIERRA | EL DORADO P H 2101 | 464 |
|  | PEASE 1103 | 2 |
|  | TAMARACK 1101 | 23 |
|  | TUDOR 1101 | 5 |
| STOCKTON | EIGHT MILE 2102 | 17 |
| YOSEMITE | LIVINGSTON 1105 | 42 |
|  | MERCED FALLS 1102 | 1 |
|  | OAKHURST 1103 | 42 |
|  | SPRING GAP 1701 | 142 |