| Impact | Mitigation Measure | Monitoring/Reporting | Effectiveness | Responsible | Timing |
| --- | --- | --- | --- | --- | --- |
|  |  | Action | Criteria | Agency* |  |
| ALL FACTORS |  |  |  |  |  |
| Extension or work | A. Petitioner must file a Petition | Quarterly reports. | Any work outside of | CPUC | Before construction |
| beyond or outside of | to modify its CPCN. An appropriate |  | existing utility right-of- |  |  |
| of the existing | environmental study of the |  | way is assessed |  |  |
| utility right-of-way | project is done. |  | through an environ- |  |  |
| into undisturbed |  |  | mental study. |  |  |
| areas. |  |  |  |  |  |
| CUMULATIVE EFFECTS |  |  |  |  |  |
| Cumulative im- | B. Coordination efforts among | Quarterly reports. | The number and duration | Local agencies. | Before construction |
| pacts due to | the petitioners and the affect- |  | of disturbances to a |  |  |
| multiple disturb- | ed local agencies so that |  | particular area are |  |  |
| ances to a par- | construction projects in the |  | minimized. |  |  |
| ticular area. | same location can be com- |  |  |  |  |
|  | bined or simultaneous. |  |  |  |  |
| GEOLOGICAL RESOURCES |  |  |  |  |  |
| Potential erosion | C. Petitioners shall comply | Quarterly reports. | Erosion at the project | Local agencies. | Before and during |
| due to excavation, | with all local design, construc- |  | areas is contained. |  | contruction. |
| grading and fill. | tion and safety standards |  |  |  |  |
|  | through permit process. Erosion |  |  |  |  |
|  | control plans for areas identified |  |  |  |  |
|  | as susceptible to erosion. |  |  |  |  |
| WATER RESOURCES |  |  |  |  |  |
| Potential impact on water | D. Petitioners shall consult with | Quarterly reports. | Impacts to water qua- | Federal agencies | Before and during |
| resouces, underground | all appropriate water resource |  | lity, drainage, flow, di- | Local agencies. | construction. |
| or surface due to exca- | agencies for projects in close |  | rection and quantity | Applicable state |  |
| vation or grading work. | proximity to water resouces |  | are averted. | water resource |  |
|  | Appropriate mitigation plans shall |  |  | agencies. |  |
|  | be developed and compliance to |  |  |  |  |
|  | all local and state water regu- |  |  |  |  |
|  | lations is required. |  |  |  |  |
| Impact | Mitigation Measure | Monitoring/Reporting | Effectiveness | Responsible | Timing |
|  |  | Action | Criteria | Agency |  |
| AIR QUALITY |  |  |  |  |  |
| Excessive dust | E. Appropriate dust control | Quarterly reports. | Dust and other emis- | Air quality | Before and during |
| and other air | measures by petitioner. |  | sions are contained. | management | construction. |
| emissions due to | Compliance with all applicable |  | Air quality standards | districts. |  |
| construction. | air quality standards as established |  | for area are met. |  |  |
|  | by air quality management districts. |  |  |  |  |
| TRANSPORTATION & |  |  |  |  |  |
| CIRCULATION & PUBLIC SERVICES |  |  |  |  |  |
| Traffic congestion, insuf- | F. Coordination by petitioners | Quarterly reports. | Traffic congestion is | Caltrans | Before and during |
| ficient parking, and | through local agencies to mi- |  | minimized. | Local agencies. | construction. |
| hazards for pedestrians. | nimize right-of-way encroachments. |  | Public service facilities restored appropriately. |  |  |
| Impacts upon public service facilities located in utility right- | All local safety and construc- |  |  |  |  |
| of-way. | tion standards shall be met |  |  |  |  |
|  | through the local permit process. |  |  |  |  |
|  | Advance notice to surrounding |  |  |  |  |
|  | area of construction date and time. Consultation w/ local agencies on appropriate restoration of impacted public service facilities in right-of-way. |  |  |  |  |
| HAZARDS |  |  |  |  |  |
| Construction in right-of-way | G. Measure F above shall be | Quarterly reports. | Construction projects | Local agencies. | Before and during |
| may interfere with emergency | augmented by informing and |  | do not interfere with |  | construction. |
| or evacuation plans. | consulting with emergency |  | emergency or evacu- |  |  |
|  | and evacuation agencies if the |  | ation routes. |  |  |
|  | proposed project impacts a route |  |  |  |  |
|  | used for emergencies or evacua- |  |  |  |  |
|  | tions. |  |  |  |  |
| Impact | Mitigation Measure | Monitoring/Reporting | Effectiveness | Responsible | Timing |
|  |  | Action | Criteria | Agency |  |
| HAZARDS |  |  |  |  |  |
| Potential increase in overhead | G. Petitioner shall obtain all neces | Quarterly reports. | Poles are built in com- | CPUC | Before and during |
| poles and communication lines. | sary building permits for the poles. |  | pliance with local safe- | Local agencies. | construction. |
|  |  |  | ty standards. Lines |  |  |
|  | CPUC will inspect the overhead |  | are inspected and |  |  |
|  | lines. |  | maintained as safe. |  |  |
| NOISE |  |  |  |  |  |
| Noise standards for the area are | H. All applicable noise standards | Quarterly reports. | Noise from construc- | Local agencies | Before and during |
| exceeded due to construction. | shall be complied with by the peti |  | tion is kept to levels | . | construction. |
|  | tioners. |  | that do not exceed |  |  |
|  | Petitioners shall notice the |  | local standards. |  |  |
|  | surrounding area of construc- |  |  |  |  |
|  | tions dates and times. |  |  |  |  |
| AESTHETICS |  |  |  |  |  |
| Service boxes or cabinets may | I. All applicable aesthetic | Quarterly reports. | Cabinets are placed | Local agencies. | Before and during |
| be a visual blight. Landscaping | standards will be met by |  | within existing build- |  | construction. |
| In utility right-of-way may be | petitioners for above-ground |  | ings, underground, or |  |  |
| impacted by trenching. | facilities, especially service |  | in areas that are land- |  |  |
|  | cabinets. Consult with local |  | scaped so that aesthe- |  |  |
|  | agencies on proper restoration of |  | tic impacts are minimi- |  |  |
|  | landscaping. |  | zed. Landscaping res- tored to original form. |  |  |
| CULTURAL RESOURCES |  |  |  |  |  |
| Cultural resources are encount- | J. All earthmoving that would | Quarterly reports. | Cultural resources that | Local, state | Before and during construction. |
| ered during construction; resour- | impact the resources shall |  | are encountered are | and/or federal |  |
| ces are damaged or moved. | cease or be altered until the |  | not destroyed or ad- | agencies. |  |
|  | petitioner retains the service |  | versely impacted. |  |  |
|  | of an archaeologist who will |  |  |  |  |
|  | propose mitigation. Thorough re- |  |  |  |  |
|  | search done prior to construction to avoid known resources. |  |  |  |  |

# Footnotes

* The CPUC is ultimately responsible for compliance with the mitigation measures listed in this document, but shall defer the responsibility to federal, state and local agencies, unless otherwise designated.