# General

This is the 2003 Reliability Report for Pacific Gas & Electric Company as required by Decision

96-09-045.  It includes four sections:

- System Indices For The Last 10 Years (1994-2003)

- Significant Outage Events Of 2003

- Customers Experiencing >12 Sustained Outages In 2003

- Historical (1994-2002) Outage Information From Prior Reports

PG&E maintains historical account specific information for customers affected by recorded outages in the Outage reporting system (OUTAGE).  This system tracks outages at the generation, transmission, substation, primary distribution, and individual transformer levels.  Additionally, OUTAGE models the actual electric switching during the circuit restoration process (which is useful for determining customer outage minutes for calculating SAIDI).  PG&E used this data, and information from other databases, to compile the information contained in this report.

System Indices (1994-2003)

Table 1 lists the required final SAIDI, SAIFI, and MAIFI values in accordance with Appendix A of Decision 96-09-045.  It should be noted that electric outage notification (EON) devices were installed during 1994-95 to obtain momentary outage information on automatic non-SCADA sectionalizing devices.  This deployment accounts for much of the MAIFI increase noted after 1994.

Table 1 - System Indices (1994-2003)

(Includes Transmission, Distribution and Generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | MAIFI | SAIDI | SAIFI | MAIFI |
| 1994 | 160.3 | 1.721 | 1.952 | 155.4 | 1.540 | 1.872 |
| 1995 | 600.2 | 2.616 | 2.216 | 170.2 | 1.537 | 1.649 |
| 1996 | 347.0 | 2.462 | 4.855 | 178.1 | 1.709 | 4.654 |
| 1997 | 171.3 | 1.700 | 4.430 | 161.8 | 1.639 | 4.335 |
| 1998 | 317.0 | 2.130 | 3.835 | 180.0 | 1.659 | 3.407 |
| 1999 | 157.2 | 1.481 | 2.427 | 156.7 | 1.477 | 2.420 |
| 2000 | 168.4 | 1.413 | 2.282 | 167.9 | 1.410 | 2.281 |
| 2001 | 249.1 | 1.560 | 2.256 | 211.8 | 1.439 | 2.120 |
| 2002 | 381.8 | 1.672 | 2.578 | 139.7 | 1.114 | 2.000 |
| 2003 | 198.9 | 1.328 | 1.806 | 193.0 | 1.308 | 1.802 |

Included in this annual report is supplemental information noted in Tables 2 and 3 representing the corresponding indexes separated for both the distribution and transmission systems.  It should be noted that the totals from these two new tables will not exactly match Table 1 for the following reasons:

- Generation related outages are included in Table 1;

- There are database limitations related to the major event exclusion process when separating the transmission and distribution systems.

Please also note, the MAIFI information is not included in these tables since the existing automatic recording (EON) devices do not distinguish between the two systems.

Table 2 - Distribution System Indices (1994-2003)

(Excludes transmission and generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | SAIDI | SAIFI |
| 1994 | 139.2 | 1.400 | 139.2 | 1.400 |
| 1995 | 536.6 | 2.393 | 150.3 | 1.384 |
| 1996 | 198.4 | 1.685 | 167.1 | 1.632 |
| 1997 | 157.3 | 1.562 | 148.4 | 1.507 |
| 1998 | 245.0 | 1.812 | 157.3 | 1.493 |
| 1999 | 145.1 | 1.324 | 144.8 | 1.321 |
| 2000 | 152.3 | 1.293 | 151.8 | 1.290 |
| 2001 | 228.6 | 1.430 | 192.5 | 1.316 |
| 2002 | 341.2 | 1.533 | 129.7 | 1.030 |
| 2003 | 179.6 | 1.209 | 173.8 | 1.190 |

Table 3 - Transmission System Indices (1994-2003)

(Excludes distribution and generation related outages)

|  | Major Events Included | Major Events Excluded |
| --- | --- | --- |
| YEAR | SAIDI | SAIFI | SAIDI | SAIFI |
| 1994 | 20.5 | 0.292 | 17.6 | 0.155 |
| 1995 | 63.6 | 0.223 | 19.9 | 0.152 |
| 1996 | 148.2 | 0.773 | 14.8 | 0.129 |
| 1997 | 13.8 | 0.138 | 13.2 | 0.132 |
| 1998 | 72.0 | 0.318 | 22.6 | 0.166 |
| 1999 | 12.1 | 0.157 | 11.9 | 0.155 |
| 2000 | 15.2 | 0.108 | 15.2 | 0.108 |
| 2001 | 20.5 | 0.129 | 19.3 | 0.123 |
| 2002 | 40.1 | 0.138 | 10.0 | 0.083 |
| 2003 | 19.3 | 0.119 | 19.1 | 0.118 |

Significant Outage Events During 2003

Table 4 lists the ten largest outage events experienced during 2003.  PG&E interprets this reporting requirement as the ten days (or in some cases consecutive days) with significant number of customer interruptions in the system or portion of the system.  These events are listed in order of customer interruptions.

Table 4 - Ten Largest 2003 Outage Events

| Rank | Description | Date | Number of Customers Affected * | Longest Customer Interruption (Hours) | Number of People Used To Restore Service | CPUC Major Event? |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | The first storm system of the fall season moved through the Service Area. Gusty southerly winds up to 30 mph developed in Northern and Central Service Area Zones on the 2nd. Gusty northwest winds occurred on the 4th. Widespread precipitation occurred in the Service Area with totals generally 1” in the mountains and 0.25” in the Central Valley. | 11/02 –11/04 | 184,849 | 26 | N/A | N |
| 2 | A strong winter storm moved through the service area on December 29th. Peak winds ranged from 30 to 70 mph with the strongest gusts north of a Monterey/Madera line. Peak winds included Red Bluff 46 mph, Beale AFB (Marysville) 59 mph, Clayton 47 mph, Sacramento 55 mph, and Stockton 44 mph. One to five inches of rain fell in the northern half of the state. Heavy snowfall was reported at low elevation locations in the northern Sacramento Valley; 18 inches at North Redding, 8-14 inches in downtown Redding, 15 inches at Burney and 10-12 inches at Nevada City. | 12/29 | 164,363 | 192 | N/A | N |
| 3 | A strong late winter storm system moved through the Service Area. Two to six inches of precipitation fell in the northern half of the Service Area; 0.50” to 1.5” of precipitation fell in the southern half of the Service Area; the southern half of the state also experienced heavy rains with one to four inches in the LA Basin. Peak wind speeds included 51 mph at Redding; 44 mph at SFO; 40 mph at Sacramento; 35 mph in Fresno; and 31 mph at Santa Rosa. Two to three feet of snowfall was recorded in the Sierra Nevada Mountains at elevations above 5,000” during this three-day period. | 03/13 – 03/15 | 160,863 | 29 | N/A | N |
| 4 | A winter storm system moved through the Service Area during this two-day period. One to three inches of precipitation fell over the northern half of the Service Area. Snowfall totals in the northern half of the Sierra Nevada Mountains ranged from one to three feet with 16” at Alpine Meadows; 24” at Soda Springs; and 28” at Sugar Bowl. Peak wind speeds ranged from 20 to 40 mph with 39 mph at SFO; 29 mph at Sacramento and Fresno; and 24 mph at Santa Rosa. | 12/09 – 12/10 | 147,128 | 144 | N/A | N |
| 5 | A cold winter storm system moved through the Service Area during this two-day period. Precipitation totals included 2.34” at Redding; 1.38” at Santa Rosa; 0.83” at Sacramento; 0.70” in SFO; and 0.25 at Fresno. The storm was accompanied by numerous thunderstorms and gusty southerly winds, principally on the 8th. Peak wind speeds included 37 mph at SFO; 30 mph in Redding; 26 mph at Sacramento; and 24 mph at Santa Rosa. | 11/08 – 11/09 | 141,666 | 46 | N/A | N |
| 6 | A strong winter storm, accompanied by heavy rain and gusty southerly winds, moved through the Service Area. Peak wind speeds ranged from 30 to 65 mph with the strongest gusts in the Bay Area, Redwood Coast, and the Northern Interior. Peak wind speeds included 56 mph in Redding; 53 mph in SFO; 33 mph in Santa Rosa; 30 mph in Sacramento; and 23 mph in Fresno. | 12/14 | 108,910 | 24 | N/A | N |
| 7 | A strong earthquake in San Luis Obispo County (Paso Robles). | 12/22 | 107,291 | 34 | N/A | Y |
| 8 | The Mission Substation was de-energized due to a fire. The cause of the fire is still under investigation. | 12/20 | 101,534 | 30 | N/A | N |
| 9 | A cold, upper level low pressure system moved through the State, accompanied by numerous showers and thundershowers, bringing heavy snow to the mountains Six to ten inches of snow fell in Truckee and the Lake Tahoe Region with up to one and on-half feet recorded at higher elevations. Thunder, lightning and small hail was observed in the Bay Area and in the Central Valley from Red Bluff to Sacramento. | 10/31 | 91,907 | 21 | N/A | N |
| 10 | A surge of subtropical moisture resulted in an outbreak of summer season shower and thunderstorm activity through out the Service Area. While precipitation totals were insignificant, there were numerous reports of lightning activity from the evening of the 25th through the evening of the 26th. | 08/26 | 80,159 | 42 | N/A | N |

- Note:  Values exclude single distribution line transformer and planned outage

Of the ten largest events listed in 2003, only one event, the December 22 earthquake met the CPUC definition of a major event. Table 5 indicates the number of customers without service at the requested periodic intervals for this request.

Table 5 – December 22, 2003 Outage Event Duration Summary

| Outage Duration | Date of Outage | Description of Outage | Number of Customers Affected |
| --- | --- | --- | --- |
| 0 TO 1 HRS | 12/22/2003 | Noted in table 4 | 738 |
| 1 TO 5 HRS | " | " | 74,623 |
| 5 TO 10 HRS | " | " | 21,727 |
| 10 TO 15 HRS | " | " | 7,275 |
| 15 TO 20 HRS | " | " | 1,642 |
| 20 TO 24 HRS | " | " | 725 |
| >=1 AND <=2 Days | " | " | 704 |

Note:  The number of customer outages segmented by hourly restoration periods requires a level of detail not normally maintained by PG&E in its central computerized records.  The information shown here is what PG&E has been able to reconstruct from several databases and may have a margin of error of up to 5%.

# Figure 1 – December 22, 2003 Outage Event Duration Summary

Customers Experiencing > 12 Sustained Outages During 2003

Table 6 lists all circuits where one or more customers on a circuit experienced more than 12

sustained outages in 2003.  Please note, this list does not mean all the customers on the

circuit experienced more than 12 outages.

PG&E is addressing the necessary portions of these circuits as part of the overall service

reliability improvement plans.

Table 6 - Customers Experiencing > 12 Sustained Outages During 2003

| Division | Feeder Name | Customers Experiencing > 12 Outages |
| --- | --- | --- |
| CENTRAL COAST | BEN LOMOND 0401 | 6 |
| CENTRAL COAST | BIG BASIN 1101 | 35 |
| CENTRAL COAST | CAMP EVERS 2104 | 22 |
| CENTRAL COAST | GREEN VALLEY 2101 | 38 |
| CENTRAL COAST | LOS OSITOS 2101 | 6 |
| DE ANZA | CAMP EVERS 2105 | 90 |
| DE ANZA | LOS GATOS 1106 | 191 |
| DIABLO | BRENTWOOD SUB 2113 | 6 |
| DIABLO | CLAYTON 2212 | 16 |
| NORTH COAST | BRIDGEVILLE 1102 | 1 |
| NORTH COAST | EEL RIVER 1101 | 121 |
| NORTH COAST | GARBERVILLE 1101 | 5 |
| NORTH COAST | GARBERVILLE 1102 | 7 |
| NORTH COAST | HARTLEY 1101 | 27 |
| NORTH COAST | MENDOCINO 1101 | 145 |
| NORTH COAST | MONTE RIO 1111 | 78 |
| SACRAMENTO | MADISON 1105 | 15 |
| STOCKTON | HERDLYN 1103 | 32 |
| YOSEMITE | GUSTINE 1102 | 2 |
| YOSEMITE | MENDOTA 1102 | 239 |

Historical (1994-2002) Outage Information From Prior Reports

For easy reference, Attachment 1 contains copies of service reliability report information previously submitted for 1994 through 2002.

Attachment 1

## Historical (1994-2002) Outage Information From Prior Reports