CEC Staff Comments to the Utilities

On the Load Profiling Workshop Report

I.  GENERAL COMMENTS

CEC staff is aware of the urgency with which a decision on load profiling is needed.  Utility distribution companies (UDCs) will need time to implement a CPUC decision and retailers have expressed a desire to obtain load profile information to assist in developing marketing strategies and implementation plans.  Expediency, however, should not be an excuse for failure to identify and progress towards solutions on several key issues.  First and foremost, the report should call upon the CPUC to make a policy decision regarding retailer specific load profiles.  Second, movement towards dynamic load profiles is paramount.  Third, criteria for further segmentation of customer classes should be identified.  Lastly, a CPUC ordered process, specific with dates and evaluation criteria, is needed to address solutions to outstanding load profiling issues so that a more permanent methodology can be implemented by January 1, 1999.

1.  Retailer Specific Load Profiles

In order to facilitate competition and cost responsibility, retailers need to have statistically accurate representation of their specific loads.  Given the dynamic nature of bids into the power exchange (PX) and scheduling with the independent system operator (ISO), errors will produce energy imbalance costs.  Incentives to minimize these costs will only occur if retailers are responsible for their specific bids, schedules and energy imbalance settlements.  In lieu of hourly interval meters for all customers, retailer specific load profiles is the next best mechanism available to hold all market participants responsible for their specific loads, both in the anticipatory planning sense and in the retrospective settlement process.   The CPUC needs to provide direction as to whether or not it supports retailer specific load profiles.  The key question is should retailers be allowed to sample, meter, and develop their own specific load profiles for use in the applications outlined in section 3 of the load profiling workshop report.  An early decision on this issue will allow time to develop the appropriate load profiling methodology for implementation January 1, 1999.

2.  Dynamic Load Profiles

The CEC staff is pleased that SCE has proposed to develop dynamic load profiles.  We look forward to a detailed description of their proposed methodology, including how dynamic information can be coordinated among the various users of the data. CEC staff urges that SDG&E and PG&E move immediately towards implementing dynamic load profiles.

The problem with static load profiles is that the load research data upon which it is based reflects historic weather and operating conditions.  Such historic data should not be used directly in the energy imbalance settlement process of the ISO or PX.  At the very least the data should be processed to reflect the specific contribution of weather and unusual operating conditions underlying customer behavior during the settlement period.    For examples see PROPOSALS FOR THE LOAD PROFILING WORKSHOP REPORT by Michael Parti, Applied Econometrics, June 3, 1997.

The process data could also be used to predict customer behavior based on different weather and operating assumptions.

The aforementioned processing techniques, however, should be an interim solution.  A more accurate method with which to representing the weather and unusual operating conditions during the settlement period is dynamic load profiling.  Dynamic load profiles are developed when metered sites are equipped with telemetry and the data uploaded on a daily basis, processed, and load profiles developed as soon as practicable.  These load profiles can then be used as a source of information on which to base load forecasts, make bids into the PX, schedule power with the ISO, and determine settlements for energy imbalances.

2.  Further Segmentation

As expressed in pre-workshop filings, the Energy Commission believes some additional segmentation is both warranted and feasible for January 1, 1998.    COMMENTS OF THE CALIFORNIA ENERGY COMMISSION IN RESPONSE TO D.96-10-074, December 19, 1996, pp. 36-37.

During 1998, even further segmentation could be justified on the basis of information obtained from tracking market activity.  Two key market conditions need to be monitored, hourly price variations in the PX and direct access penetration in the residential and commercial sectors.  A working group comprised of interested stakeholders should be started in September of 1997 to identify criteria upon which further segmentation would be based.  The working group should also do the following.  First, develop a specific test, such as the one suggested by the Office of Ratepayers Advocates   LOAD PROFILING WORKSHOP PROPOSAL, Office of Ratepayer Advocates, June 2, 1997, pp. 15-16. , to identify homogeneous customer groups that have load profiles statistically different from the class average.  Second, develop a mechanism for determining the cost-of-service differences among these groups.  Third, develop estimates of the incremental metering and sampling costs implicit in additional segmentation.  Fourth, identify billing impediments (if any) associated with further segmentation.  Fifth, identify implications for collection of the competitive transition charge (CTC) resulting from further segmentation (if any).  And Sixth, develop a cost/benefit test to ensure that additional segmentation results in an overall net benefit for those customers participating by reducing ISO, SC, and PX energy imbalance settlement costs.

4.  Timeline For Movement Towards Goal

CEC staff suggest the following timeline as a way of moving towards resolution on key issues.  PG&E and SDG&E should examine methodologies to make their static load profiles more dynamic prior to implementation January 1, 1998.  Ways in which this could be accomplished include:  (1) weather sensitive regression adjustments to static profiles; (2) matching the load profiles to the overall system shape; (3) collection of the load research data monthly and producing time period specific profiles prior to final settlements.

Starting in September, 1997, and working through January, 1998, the working group should establish criteria for movement towards further segmentation and retailer specific load shapes.  The working group should also be responsible for completing the following tasks by June 1, 1998:

1.	Develop precision criteria for sampling
a.	identification of error to be minimized
b.	level of precision
c.	size of confidence interval

2.	Develop a methodology for estimating the load profiles of additional segments

·	additional sample points

·	regression analysis

3.	Estimate the implementation costs of improved methodologies

·	dynamic load profiling based on sample points, telemetry to upload data daily, and data processing cost to develop updated load profiles

·	tradeoffs between hardware and labor costs of sampling methods versus regression methods

4.	Estimate the net benefits resulting from additional segmentation

5.	Identify ways to approve and verify load profiles

·	Identify entity to approve load profiles

·	Develop mechanism which could verify the appropriateness of a customer’s load profile

CEC staff agree with the UDCs’ statement in the executive summary:  “A majority of workshop participants supported the UDC proposal to consider further improvements in the design of load profiles in a subsequent proceeding concluding with implementation of any modifications to load profiles on January 1, 1999, subject to re-prioritization of the timing of the proceeding by the Commission.”  The CPUC should, however, give guidance to the overall direction the subsequent proceeding should take (e.g., single entity versus multi-entities production of load profiles, or static versus dynamic load profiling, etc.).  Without direction parties to the proceeding will argue over basic policy and fail to develop a specific methodology to be implemented January 1, 1999.   The CPUC should also set specific dates when tasks should be completed.  The UDCs’ timetable in Section 7 of the draft workshop report is to vague.  Issues outlined need to be addressed in a time ordered fashion.  A timetable without specific dates and action points will lead to no action.

II.  SPECIFIC COMMENTS ON THE TEXT OF THE REPORT

In this section CEC staff makes specific recommendations for changes to the text of the June 10 draft report that we believe would add clarity.  The changes are keyed to specific sections and identified in italics.

Changes to the Executive Summary

1.	In order to achieve a January 1, 1998 implementation date for direct access, UDCs should develop and implement class segment load profiles using load shapes from existing rate categories, systems, procedures, load research meters and samples.

2.	For the second arrow under the minority of workshop participant section the text should read, “more complete implementation of dynamic updating of load profiles than proposed in this report”.

Correction to Section 1 (Introduction)

1.	Dan Kirshner should be referred to as a member of the Governing Board of the ISO, not as a member of the Board of Trustees.

Changes to Section 2 (Principles For The Use Of Load Profiles)

1.	In this section it is CEC staff  that have proposed a set of principles, not the CEC.

2.	The UDCs identify three problems associated with allowing retailer-developed load profiles.  It should be noted here that CEC staff does not believe that churning will be a problem.  Given the size of the class segmentation proposed by the UDCs, a retailer would have to capture a significant portion of customers before the class average load profile would need to be updated.

3.	The verification issues surrounding retailer specific load profiles is a legitimate concern.  CEC staff believes that there are ways to verify the appropriateness of a customer’s load profile and this issue should be address by continuation of a load profiling working group.  Moreover, we agree that standards for retailer-developed load profiles, such as requirements for sampling accuracy, independence of the sample selection process, and frequency of redrawing samples need to be prescribed by an independent regulatory entity before retailers can be allowed to produce their own load profiles.

4.	CEC staff agree with the UDCs when they indicate that the approach to retailer developed load profiles is fundamentally different from a single entity approach.  This is why we urge the CPUC to provide direction as to whether or not retailers will be allowed to developed their own load profiles.

Changes to Section 3 (Applications For Load Profiles)

1.	Applications for load profiles were identified by CEC staff not the CEC.  Furthermore, when the CEC staff stated that load profiles should be used for ISO scheduling and PX bidding applications we meant that information garnered from dynamic load profiles will help produce more accurate PX bids and ISO schedules, thus reducing energy imbalance costs.

2.	In section 3.1 (ISO/PX Settlement Applications) the following text, as shown in italics, should be added.  The ISO is currently considering proposals for separately identifying the load profile portion of UFE and assigning it to Scheduling Coordinators in proportion to their load profile customer loads, but has concluded that such methods cannot be implemented on January 1, 1998, due to vendor software constraints.

3.	In section 3.2 (Power Exchange Credit/Charge Calculation (UDC Billing) clarification is needed about the following, “After the end of the transition period, UDCs would use load profiling to calculate the PX energy charges for any remaining full service customers without hourly metering.”  Our question is, Why is there no longer a need for a PX credit?  Are the UDCs suggesting a “bottoms up” approach to recover the cost of services they provide?

Changes to Section 4 (Methodology)

1.	In section 4.2 (Design of load profiles) CEC staff would like this clarification of the Energy Commission’s position added to the last paragraph.  In other forums, such as the rate unbundling proceeding, the Energy Commission has supported authorization of additional expenditures to permit more accurate load profiling for forecasting and settlement applications.    TESTIMONY OF MICHAEL JASKE AND LORENZO KRISTOV ON BEHALF OF THE CALIFORNIA ENERGY COMMISSION, February 28, 1998, pp.28-30.

2.	In section 4.3 (Reconciliation with available metered data) the text should be changed to describe the methodologies as UDC proposals being adjudicated in the CPUC’s rate unbundling proceeding.

Changes to Section 5 (Eligibility)

1.	In Section 5 (Eligibility) CEC staff have our concerns expressed regarding customers gaining then losing eligibility under the utilities proposal.  If a customer is eligible for load profiling on January 1, 1998, that customer should not have to worry about being screened out at a later date.  If the customer were to grow above the 20 kW limit, that customer should be given the 20 < 50 kW exemption.

2.	In section 5.2 (Customers with maximum demands between 20 kW and 50 kW) we suggest the following be added to the first paragraph.  D.97-05-040 explicitly asks workshop participants to explore exemption for customers with a maximum demand at or above 20 kW but below 50 kW (p. 36).

Changes to Section 6 (Segmentation)

1.	In section 6.2 (Interim segmentation schemes for 1/1/98) and section 6.6 (Establishment of methodologies or revising segmentation schemes) the text should read CEC staff.

2.	In section 6.2 the following text, as shown in italics, should be added.  CEC staff quantified that error due to segmentation methods could amount to tenths of a penny per kWh, assuming a particular set of hourly PX prices that may or may not be representative of what actually occurs in the PX.