Rule 15	Sheet 1 of 15

DISTRIBUTION LINE EXTENSIONS

APPLICABILITY: This rule is applicable to extension of electric Distribution Lines1/ of Edison's standard voltages (less than 50 kV) necessary to furnish Permanent electric service to Applicants, and will be made in accordance with the following provisions:

A.	GENERAL - All provisions of Rule 15 apply to both Edison Bundled Service Customers and Direct Access Customers.

1.	EXTENSION BASIS

a.	DESIGN. Edison will be responsible for planning, designing, and engineering extensions using Edison's standards for material, design, and construction.

b.	OWNERSHIP.  The extension facilities installed under the provisions of this rule, shall be owned, operated, and maintained by Edison, except for Substructures and enclosures that are on, under, within, or part of a building or structure.

c.	PRIVATE LINES. Edison shall not be required to serve any Applicant from extension facilities that are not owned, operated, and maintained by Edison.

2.	EXTENSION LOCATIONS

a.	RIGHTS OF WAY. Edison will own, operate and maintain extension facilities only:

(1)	along public streets, alleys, roads, highways and other publicly dedicated ways and places which Edison has the legal right to occupy (Franchise Areas), and

(2)	on public lands and private property across which rights of way and permits satisfactory to Edison may be obtained without cost to or condemnation by Edison.

b.	NORMAL ROUTE OF LINE.  The length and normal route of an extension will be determined by Edison and considered as the distance along the shortest, most practical, available, and acceptable route which is clear of obstructions from Edison's nearest permanent and available distribution facility to the point from which the service facilities will be connected.

____________________

1/	Certain words beginning with capital letters are defined either within the provisions of this rule or in Part I.

(Continued)

(T)

(N)

(N)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

Rule 15	Sheet 4 of 15

DISTRIBUTION LINE EXTENSIONS

(Continued)

C.	EXTENSION ALLOWANCES

1.	GENERAL.  Edison will complete an extension without charge provided Edison's total estimated installed cost (excluding transformers, meters and services) does not exceed the allowances as determined, from permanent, bona-fide loads to be served by the extension within a reasonable time, as determined by Edison.

2.	BASIS OF ALLOWANCES.  Allowances shall be granted to an Applicant for Permanent Service, or to an Applicant for a subdivision or development under the following conditions:

a.	Edison is provided evidence that construction will proceed promptly and financing is adequate, and

b.	Applicant has submitted evidence of building permit(s) or fully-executed home purchase contract(s) or lease agreement(s), or

c.	Where there is equivalent evidence of occupancy or electric usage satisfactory to Edison.

The allowances in Sections C.3 and C.4 are based on a revenue-supported methodology using the following formula:

ALLOWANCE  =          NET REVENUE

COST OF SERVICE FACTOR

3.	RESIDENTIAL ALLOWANCES.  The allowance for Permanent Residential Service is $____1/ per meter or residential dwelling unit.

4.	NON-RESIDENTIAL ALLOWANCES.  The allowance for Permanent Non-Residential Service is determined by Edison using the formula in Section C.2.

Where the extension will serve a combination of residential and non-residential meters, residential allowances will be added to non-residential allowances.

5.	SEASONAL, INTERMITTENT, AND INSIGNIFICANT LOADS.  When an Applicant requests service that requires an extension to serve loads that are Seasonal or Intermittent, the allowance for such loads shall be determined using the formula in Section C.2.  No allowance will be provided where service is used only for emergency purposes, or for Insignificant Loads.

____________________

1/	Allowance amount to be addressed in the Line Extension Order Instituting Rulemaking.

(Continued)

(T)

(T)

(T)

(T)

(T)

(T)

(N)

Rule 15	Sheet 13 of 15

DISTRIBUTION LINE EXTENSIONS

(Continued)

I.	DEFINITIONS FOR RULE 15  (Continued)

Excavation:  All necessary trenching, backfilling, and other digging to install extension facilities, including furnishing of any imported backfill material and disposal of spoil as required, surface repair and replacement, landscape repair and replacement.

Feeder Conduit:  Conduit for such uses as part of a backbone system to provide for future anticipated load growth outside the subdivision involved, to provide for future anticipated load growth in the existing subdivision and the existing subdivisions in close proximity, to balance loads between substations, to interconnect the service to the subdivision with service to subsequent developments outside the subdivision, and to provide the flexibility and versatility of modifying or supplying emergency backup power to the area involved.

Franchise Area:  Public streets, roads, highways, and other public ways and places where Edison has a legal right to occupy under franchise agreements with governmental bodies having jurisdiction.

Industrial Development:  Two (2) or more enterprises engaged in a process which creates a product or changes material into another form or product and located on a single parcel or on two (2) or more contiguous parcels of land.

Insignificant Loads:  Small operating loads such as gate openers, valve controls, clocks, timing devices, fire protection equipment, alarm devices, etc.

Intermittent Loads:  Loads which, in the opinion of Edison, are subject to discontinuance for a time or at intervals.

Line Extension:  New distribution facilities of Edison that is a continuation of, or branch from, the nearest available existing permanent Distribution Line (including any facility rearrangements and relocations necessary to accommodate the extension) to the point of connection of the last service.  Edison's Line Extension includes transmission underbuilds and converting an existing single-phase line to three-phase in order to furnish three-phase service to an Applicant, but excludes transformers, meters and services.

Net Revenue:  That portion of the total rate that supports Edison's distribution line extension costs and excludes such things as fuel costs, generation, transmission, Competition Transition Charge (CTC), public purpose programs, and other costs that do not support the distribution line extension costs.  This rate is listed in Edison's Preliminary Statement, Part I, Rate Schedule Summary.

(Continued)

(T)

(T)

(T)

(T)

|

|

|

(T)