Rule 16	Sheet 1 of 18

SERVICE EXTENSIONS

Applicability:  This rule is applicable to both (1) Edison Service Facilities1 that extend from Edison's Distribution Line facilities to the Service Delivery Point, and (2) service related equipment required of Applicant on Applicant's Premises to receive electric service.

A.	General - All provisions of Rule 16 apply to both Edison Bundled Service Customers and Direct Access Customers.

1.	Design.  Edison will be responsible for planning, designing, and engineering its Service Facilities and Service Lateral facilities using Edison's standards for design, materials and construction.

2.	Service Facilities.  Edison's Service Facilities shall consist of (a) primary or secondary underground or overhead Service Lateral conductors, (b) poles to support overhead service conductors, (c) service transformers, (d) Edison-owned Metering Facilities, and (e) other Edison-owned service related equipment.

3.	Ownership of Facilities.  Service Facilities installed under the provisions of this rule shall be owned, operated, and maintained by Edison if they are (a) located in the street, road or Franchise Area of Edison, (b) installed by Edison under section D.2 below on Applicant's Premises for the purpose of the delivery of electric energy to Applicant, or (c) installed by Applicant under the provisions of this rule, and conveyed to Edison.

4.	Private Lines.  Edison shall not be required to connect Service Facilities to or serve any Applicant from electric facilities that are not owned, operated, and maintained by Edison.

5.	Special or Added Facilities.  Any special or added facilities Edison installs at the request of Applicant, will be installed at Applicant's expense in accordance with Rule 2, Description of Service.

6.	Temporary Service Facilities.  Service Facilities installed for temporary service or for operations of speculative character or questionable permanency shall be made in accordance with the fundamental installation and ownership provisions of this rule, except that all charges and refunds shall be made under the provisions of Rule 13, Temporary Service.

7.	Street Lights.  Street light services and appurtenant facilities shall be installed in accordance with the service provisions of the applicable street light schedule.

---------------------

1/	Certain words beginning with capital letters are defined either within the provisions of this rule or in Part H.

(Continued)

(T)

(N)

(N)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

Rule 16	Sheet 3 of 18

SERVICE EXTENSIONS

(Continued)

A.	General.  (Continued)

11.	Access to Applicant's Premises. (Continued)

b.	Safe and ready access for Edison personnel free from unrestrained animals,

c.	Unobstructed ready access for Edison's vehicles and equipment to install, remove, repair, or maintain its facilities, and

d.	Removal of any and all of its property installed on Applicant's Premises after the termination of service.

12.	Service Connections.  Only personnel duly authorized by Edison are allowed to connect or disconnect service conductors to or from Edison's Distribution Lines, remove Edison-owned service facilities, or perform any work upon Edison-owned existing facilities.

B.	Metering Facilities

1.	General.

a.	Meter All Usage. Delivery of all electric power and energy will be metered, unless otherwise provided for by Edison's tariff schedules or by other applicable laws.

b.	Meter Location.  All meters and associated metering equipment shall be located at some protected location on Applicant's Premises as approved by Edison.

2.	Number of Meters.  Normally only one meter will be installed for a single-family residence or a single non-residential enterprise on a single Premises, except:

a.	When otherwise required or allowed under Edison's tariff schedules;

b.	At the option of and as determined by Edison, for its operating convenience, consistent with its engineering design; or

c.	When required by law or local ordinance.

d.	When additional services are granted by Edison.

(Continued)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

Rule 16	Sheet 4 of 18

SERVICE EXTENSIONS

(Continued)

B.	Metering Facilities.  (Continued)

2.	Number of Meters.  (Continued)

A single meter is required for each single enterprise operating in one building or group of buildings or other development on a single Premises such as, but not limited to, a commercial business, school campus, industrial manufacturer, or recreational vehicle park, unless otherwise approved by Edison.

3.	Multiple Occupancy.  In a building with two or more tenants, or where more than one meter is furnished on the same Premises, the meters normally shall be grouped at one central location, or as otherwise specified by Edison, and each meter position or socket shall be clearly and permanently marked by Applicant, customer, or owner of the Premises to indicate the particular unit, occupancy, or load supplied by it.

a.	Residential.  For revenue billing, electric service shall be individually metered to every residential unit in a residential building or group of buildings or other development with multiple tenants such as, but not limited to, apartment buildings, mobile home parks, etc., except as may be specified in Rule 18 and applicable rate schedules.

b.	Non-Residential.  For revenue billing, electric service shall be individually metered to each tenant in a non-residential building or group of buildings or other development on a single Premises with multiple tenants or enterprises (such as, but not limited to, an office building or shopping center complex).  Alternative metering arrangements as determined by Edison may be allowed only as specified in Rule 2 and applicable rate schedules.

(Continued)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

Rule 16	Sheet 11 of 18

SERVICE EXTENSIONS

(Continued0

D.	Responsibilities for New Service Facilities.  (Continued)

1.	Applicant Responsibility.  (Continued)

g.	Transformer Installations on Applicant's Premises.  (Continued)

(5)	Transformer Lifting Requirements.  Where Edison has installed or agrees to install, transformers at locations where Edison cannot use its standard transformer lifting equipment and special lifting facilities are required to install or remove the transformers on Applicant's Premises, Applicant shall, at its expense, (a) furnish, install, own, and maintain permanent lifting facilities and be responsible for lifting the transformer to and from its permanent position, or (b) provide (or pay for) portable lifting facilities acceptable to Edison for installing or removing the transformers.  Rights-of-way and space provisions shall be provided by Applicant such that access and required clearances from adjacent structures can be maintained.  Edison may require a separate contract for transformer lifting requirements.

(6)	Overhead Transformers.  In remote areas or in areas not zoned for residential or commercial use or for underground services, padmounted transformers are preferred for installation on Applicant's Premises however, where Edison determines that it is not practical to install a transformer on a pad, in a room or vault, Edison may furnish a pole-type structure at its expense for an installation not exceeding 500 kVA.

h.	Building Code Requirements.  Any service equipment and other related equipment owned by Applicant, as well as any vault, room, enclosure, or lifting facilities for the installation of transformers shall conform with applicable laws, codes, and ordinances of all governmental authorities having jurisdiction.

i.	Reasonable Care.  Applicant shall exercise reasonable care to prevent Edison's Service Lateral, other Edison facilities, and meters owned by Edison or others on the Applicant's Premises from being damaged or destroyed, and shall refrain from interfering with Edison's operation of the facilities and shall notify Edison of any obvious defect.  Applicant may be required to provide and install suitable mechanical protection (barrier posts, etc.) as required by Edison.

(Continued)

(T)

(T)

(T)

(T)

(T)

(T)

(T)

|

|

|

|

(T)

Rule 16	Sheet 12 of 18

SERVICE EXTENSIONS

(Continued)

D.	Responsibilities for New Service Facilities.  (Continued)

2.	Edison Responsibility.

a.	Service, Meter, and Transformer.  Edison will furnish, install, own, and maintain the following Service Facilities as applicable after Applicant meets all requirements to receive service:

(1)	Underground Service.  A set of Service Lateral conductors to supply permanent service from the Distribution Line source to the Service Delivery Point approved by Edison.

(2)	Riser Materials.  Any necessary pole riser material for connecting underground services to an overhead Distribution Line.

(3)	Overhead Service.  A set of overhead Service Lateral conductors and support poles to supply permanent service from a Distribution Line source to a suitable support at the Service Delivery Point approved by Edison.  Such support shall be of a type and located such that service wires may be installed in accordance with good engineering practice and in compliance with all applicable laws, ordinances, rules, and regulations including those governing clearances and points of attachment.

(4)	Metering.  When the meter is owned by Edison, Edison will be responsible for the necessary instrument transformers where required, test facilities, meters, associated metering equipment, and the metering enclosures when Edison elects to locate metering equipment at a point that is not accessible to Applicant.

(5)	Transformer.  The transformer where required, including any necessary switches, capacitors, electrical protective equipment, etc.  When either a padmounted or overhead transformer is installed on Applicant's Premises, the Service Lateral shall include the primary conductors from the connection point at the distribution supply line to the transformer and the secondary conductors, if any, from the transformer to the Service Delivery Point.

(Continued)

(T)

(T)

(T)

(T)

(T)