Universal Meter Identification

Background

As stated in the MDCS document, section V.B.2.f(i), we need a standard for numbering meters:

In order to promote effective transitions and interchangeability of meters between ESPs and UDCs, it is proposed that a state-wide standard for numbering meters be developed.  Another option might be for manufacturers to develop a simple method of replacing meter numbers on their in-service meters.

It is proposed that the manufacturer’s meter serial numbers be adopted as the standard and that manufacturers implement a program to prevent duplicate meter serial numbers across the industry.  Our recommendation would be to use the AEP manufacturer code as a prefix to the meter serial number.  Provided by PacificCorp.

One of the tasks of the universal identifier workshop is to follow up on this recommendation.

Why Do We Need a Standard?

There are several reasons for having a standard way of identifying a meter including:

To support system transactions.  When one participant tells another that a meter has been changed out, it is important for the two parties to have a common way of identifying the meter.  If a participant asks for meter testing data for a meter, the key reference for this information is the meter number, which again means that there should be a common way of identifying the meter.

Unless we choose a common meter numbering scheme, there is no guarantee that current or future market participants will be able to store other participants’ meter numbers in their systems.  This would put additional burden on all parties.

All participants that ever visit a meter need to be able to match the identity of the meter to a record in their system.  This is often used as a verification that the field person is in fact at the right “node ID”.  Both the meter number and the labeling practices need to be standardized.

In order to track a physical meter for liability reasons, it is important that the key identification for the meter not change.  If we stay with three or more meter numbering schemes, and a meter has to be re-badged when it moves between territories, we lose some capability to track that meter.

In order to reliably track meter ownership changes, we need a common way of identifying the meter.

If a common numbering scheme is not adopted, this puts additional burden on ESPs and Metering Agents in that they have to handle UDC territory specific meter number assignment and labeling schemes.  This ultimately results in increased meter inventory levels or longer response times to direct access requests, both of which negatively affect the market.

If a common meter registry is implemented, a standard meter identifier will be an absolute requirement.

There is no guarantee of unique meter numbers if we don’t have a common identification method.  A non-unique identifier for a meter can cause a multitude of problems from incorrectly processed meter change transactions to bad customer bills.

Standards Required

There are two parts of the standard that are required to reap maximum benefits.  The first is the meter identification value that all participants will use to identify the meters on their systems.  The value should be unique, at least across California, and hopefully more globally.  The value should never need to change for a physical meter, even if it crosses a UDC service territory boundary or changes ownership from one ESP or consumer to another.

The other part of the standard is the physical labeling of the meter.  Obviously, one of the requirements for labeling is to include the standard meter number.  To facilitate the meter changing ownership across UDC territories, the label should not include the meter owner or any service territory indicators, such as the UDC name.  The meter nameplate should include attributes of the meter to support UDC and metering agents’ meter shops.

Existing Standards

ANSI C12.10.  This widely accepted standard mainly describes the physical characteristics of electric meters and physical labeling requirements.  The labeling requirements include a description of the meter identifier and the physical barcode specifications.  The specification of the identifier itself is somewhat open ended.  The identifier itself is 17 characters long in the format

XXXYYYYYYYYYZZZZZ

where

XXX 			is “user specified”

YYYYYYYYY	is the serial number (manufacturer’s serial number or utility meter number)

ZZZZZ		is “user specified”

However, the specification also allows that “other formats may be used”.

AEP.  This standard describes the makeup of the actual meter identifier.  It is fully ANSI C12.10 compliant in that it is a 17 character value, and it does follow the format suggested by ANSI.  The value is as follows:

AABYYYYYYYYYZZZZZ

where

AA			is the meter test code

B			is an identifier for the meter manufacturer

YYYYYYYYY	is the manufacturer’s serial number or utility number

ZZZZZ		is user specified

The meter test code is used by calibration equipment manufacturers to automatically set up their equipment to calibrate a given meter.  The user simply scans in the AEP barcode on the meter, and the calibrator will use the correct voltage, test amps, etc.  The one letter meter manufacturer makes this standard a little limiting if we want a single standard for any type of equipment in the field.  The last five characters are still user specified, and many utilities use these characters for an inventory code, a date of manufacture, etc.

Other Standards.  There are other US and international standards that are used to identify various retail products, etc., for example the UPC product code.  One common theme to these methods is to use a combination of a company code and a serial number assigned by that company.  Each company is responsible for keeping all the serial numbers that they assign unique.  This ensures global uniqueness, assuming that no two companies use the same company code.  There is typically an entity that is responsible for assigning company codes and ensuring that they are unique.

Recommendation

On the surface, it appears that the AEP standard satisfies our requirements.  It is ANSI compliant and in wide use by utilities today.  However, there are a couple issues to be addressed.

The first is that it is not necessarily unique in the global sense.  There is the possibility, although remote, that two meters in California have the same AEP code.  This is because each utility can define their own numbering scheme for the serial number instead of using the manufacturer’s serial number.  This could mean that a SDG&E meter and a SCE meter could have the same serial number.  If they also have the same test code and meter manufacturer, we would have duplicate AEP numbers.

The second issue is that although AEP defines how to identify electric meters, it does not cover gas meters, water meters, current transformers, etc.  This is not to say that the AEP code can not be used to identify these other devices, only that it is not currently specified.

Our recommendation, which addresses both issues, is as follows.

Meter Number

The meter number format is:

XXXYYYYYYYYYZZZZZ

where

XXX	is an agreed upon value that allows the continuation of existing functionality, if any, for that specific class of devices

YYYYYYYYY	is the serial number assigned by the company creating the number

ZZZZZ	is the company identifier.  The first character would be an indicator of the organization assigning the company identifiers.

For electric meters, the value of XXX would be the first three characters of the AEP code (the test code and the manufacturer character).  This provides continued functionality for existing calibration equipment without software changes.  For other types of devices, interested parties would agree on a use, if any, for the first three characters.  If not used, the value would be “000”.

For a new meter that an ESP purchases from a meter manufacturer, the company identifier and serial number could be from either party.  If the meter manufacturer can guarantee that they can assign unique serial numbers, then the company code would be theirs.  If the meter manufacturer can not guarantee uniqueness, the ESP would use their company code and would provide the serial number.

For a meter that comes out of the field, the ESP or UDC responsible for putting the meter back into the field would be responsible for re-badging the meter with the new standard.  The meter identifier can be a combination of the original host UDC company identifier and their meter number as the serial number, or the ESP or its metering agent’s company identifier and a new serial number.  This scheme takes advantage of the fact that the meter numbers within a UDC are already unique and also allows for a relatively smooth systems transition for the UDCs.

Meter Labeling

Meter labeling would be according to the ANSI C12.10 specification.  The first data line on the label can be company specific according to ANSI, and most utilities put their name in this line with some sort of meter number.  We recommend that this line not contain any UDC specific information, but instead just the 9 digit serial number from the standard meter number as described above.  This provides a minimum amount of change for existing UDC labeling and field processes, and thus enables a smooth transition to the new numbering standard.

Implementation Issues

Most if not all UDCs in California can not immediately handle a new 17 character meter identifier in their systems.  Until they can, all new meter numbers assigned will need to be UDC format values, depending on the destination UDC territory for the meter.  This is unfortunate in that many of the benefits can not be realized immediately.  One benefit that can be realized immediately is standardized meter labeling, using the full standard meter number in the barcode on the meter.  The UDCs can still treat the meter as one of their regular meters, using the current numbering scheme.  There is a possibility that all parties could use the new scheme in all transactions from day one.  The ESPs and third party metering agents could use the full 17 character value in their systems.  When receiving transactions from the ESPs or MAs, the UDCs would pull out their specific number from the serial number field and use it by itself in their systems.  If the UDC put in a new meter, they could report a full 17 character value pretty easily, with the possible exception of the test code value.  If this is a problem, this part of the number could be set to “00”.  It would not affect the uniqueness, but it might not match the barcode on the meter, which somewhat defeats the purpose of the standard.  This option requires more discussion.

As soon as the UDCs can all handle the new number, all meters installed after that time would be referenced by the new standard.  In addition, there is the option that meters that were installed under the new standard with the new labeling requirements could go through a one-time conversion on the UDC and ESP / MDMA / MA systems.  Long term, there would still be meters in the field with the current UDC numbering schemes, but any meter that was installed to support direct access would be under the new standard.