PG&E DISTRIBUTION LOSS FACTOR DOCUMENTATION FOR OCTOBER 15, 1997 FILING

| Column | Column Contents |
| --- | --- |
| Descriptive Source Notation |
|  | SERVICE TRANSFORMERS: File "SVCTFRLF.XLS" - calculates the annual losses associated with all service transformers (both conventional and network). |
|  | CONVENTIONAL TRANSFORMERS SHEET |
| A | Transformer Size |
| D-EDSA Transformer inventory, kVA nameplate rating |
| B | Number of Transformers |
| D-EDSA Transformer inventory, count of transformers by nameplate rating |
| C | Summer KVA Loads |
| D-EDSA Transformer inventory, sum of summer maximum loads |
| D | Summer KVA per Transformer |
| C / B |
| E | Load per Transformer |
| D / A |
| F | KW/unit load loss |
| Average of nameplate data: unchanged from prior 1996 GRC filings |
| G | KW/unit no-load loss |
| Average of nameplate data: unchanged from prior 1996 GRC filings |
| H | Annual Load Factor |
| Value derived from prior GRC filings*Annual KWH per load duration curve (63,412,308,722) |
|  | / total annual transformer loads based on prior load factors (49,536,914,847) |
| I | Load Responsibility Factor |
| Table look-up value, unchanged from prior GRC filings |
| J | Loss Responsibility Factor |
| I * I |
| K | Total system KW load loss |
| B * F * E^2 |
| L | Coincident system KW load loss |
| K * J |
| M | Annual KWh load loss |
| K * 8760 * (0.3 * H + 0.7 * H^2) |
| N | Total system KW no-load loss |
| B * G |
| O | Annual KWh no-load loss |
| N * 8760 |
| P | Coincident system KW peak [.85 pf] |
| C * I * .85 |
| Q | Annual KWh load |
| C * H * 8760 * 0.85 |
|  | NETWORK TRANSFORMERS SHEET |
| A | Transformer size |
| D-EDSA Transformer loading files, Summer '97 |
| B | Number of Transformers |
| D-EDSA Transformer loading files, Summer '97 |
| C | Summer KVA Loads |
| A * B * E |
| D | Summer KVA per Transformer |
| C / B |
| E | Per Transformer load |
| SFDivision input indicating network peak 422MW / total nameplate 909 MW = .46 |
| F | KW/unit load loss |
| Same value as for conventional transformer see above |
| G | KW/unit no-load loss |
| Same value as for conventional transformer |
| H | Annual Load Factor |
| Same value as for conventional transformer |
| I | Load Responsibility Factor |
| Same value as for conventional transformer |
| J | Loss Responsibility Factor |
| I * I |
| K | Total system KW load loss |
| B * F * E^2 |
| L | Coincident system KW load loss |
| K * J |
| M | Annual KWh load loss |
| K * 8760 * (0.3 * H + 0.7 * H^2) |
| N | Total system KW no-load loss |
| B * G |
| O | Annual KWh no-load loss |
| N * 8760 |
| P | Coincident system KW peak (.85 pf) |
| C * I * .85 |
| Q | Annual KWh load |
| C * H * 8760 * 0.85 |
|  | SECONDARY LAF (tfrs., sec., svc., excl. pri.) BY LOAD: File "SORTED.XLS" - calculates the annual losses assoc. w/ all secondary |
| conductor and services, plus all service transformers. |
|  | A | Hour |
| Rank 8760 hours; Hour 1 = peak load, 8760 = minimum load, secondary- voltage customers only |
| B | Hourly KW load |
| Actual loads from a load-profile-metered semi-random stratified sample, scaled up to metered usage (1995 data) |
| C | Annual transformer load losses |
| From service transformer sheet, column M |
| D | Loss factor |
| B^2 / sum(B^2) |
| E | Hourly load loss in KWh |
| C * D |
| F | Hourly transformer no-load losses |
| From service transformer sheet total of column O / 8760 |
| G | Total service transformation loss (%) |
| (E + F) / B |
| H | Total service transformation LAF |
| 1 / (1 - G) |
| I | Hourly secondary and service transformation loss in KWh |
| Total annual secondary & service losses: (1,379,604,616) * (B^2 / sum(B^2)) |
|  | Total losses=sum(load [Formula22.xls col B]*tou seclaf [Formula22.xls col E]). Used 96 GRC TOU load duration factors. |
| J | Hourly secondary and service transformation loss (%) |
| I / B |
| K | Secondary and service transformation LAF |
| 1 / (1 - J) |
| L | Secondary transformation LAF |
| H * K |
| Q | Secondary transformation LAF per 100 MW increments |
| For each 100 MW, average of LAF's with loads in that range |
|  | SUBSTATION TRANSFORMERS: File "SUBTFRS.XLS" - calculates the annual losses associated with all substation transformers. |
| A | Number of Transformers by Type |
| Substation Asset Management data base (All_txs.xls); sorted by active transformer types |
| B | Number of Phases |
| Substation Asset Management data base (All_txs.xls) |
| C | Transformer Rating #1 |
| Substation Asset Management data base (All_txs.xls) |
| D | Total Kva of Transformer Type |
| A * C |
| E | Copper Loss (%) of each Transformer Type |
| Substation Asset Management data base (All_txs.xls) |
| F | Iron Loss (%) of each Transformer Type |
| Substation Asset Management data base (All_txs.xls) |
| G | Per unit load at peak |
| Peak load from duration curve 13,183,597 / Total nameplate 16,435,928 |
| H | Annual load factor |
| Engineering judgement per EPSAS resources |
| I | KW load loss at peak |
| E * D * G * G |
| J | Annual KWh load loss |
| I * 8760 * (0.3 * H + 0.7 * H^2) |
| K | Total system KW no-load loss |
| F * D |
| L | Annual KWh no-load loss |
| 8760 * K |
|  | PRIMARY LOSSES: File "PRIFDRLF.XLS" - calculates the annual losses associated with all primary conductor and equipment |
| (including substation transformers but excluding service transformers and secondary equipment). |
|  | B | Planning Area |
| Rates' Area Costing data base: DPA capacity and energy losses attributable to feeders |
| C | Number of Circuits |
| Rates' Area Costing data base: Number of circuits system-wide |
| D | DPA Peak Load in KW |
| Rates' Area Costing data base: Calculated from sample loads |
| E | DPA Losses at Peak Load |
| Rates' Area Costing data base: losses calculated per 93 GRC specs |
| F | DPA feeder losses (%) |
| E / D |
| G | Peak load per circuit |
| D / C |
| H | Primary circuit LAF |
| 1 / (1 - F) |
| I | Hour |
| Rank of 8760 hours; Hour 1 is the annual peak load, 8760 is the minimum annual load, primary-voltage customers only |
| J | Hourly KW load |
| Actual loads from a load-profile-metered semi-random stratified sample, scaled up to metered usage (1995 data) |
| K | Hourly Losses in KW |
| sum of column E*(hourly KW/sum of column D)^2 |
| L | Hourly feeder losses (%) |
| K / J |
| M | Feeder LAF |
| 1 / (1 - L) |
| N | Substation Transformer no load losses |
| Annual substation transformer no-load losses (from column L of file subtfrs.xls) / 8760 |
| O | Loss factor |
| J^2/ (sum J^2) |
| P | Sub Tfr load losses |
| O * P5 (annual substation transformer load losses; from column J of file subtfrs.xls) |
| Q | Sub Tfr losses (%) |
| (N + P) / J |
| R | Sub Tfr LAF |
| 1 / (1 - Q) |
| S | Total Primary Transformation LAF |
| M * R |
| W | Primary Transformation LAF per 100 MW increments |
| For each 100 MW, average of LAF's with loads in that range |

Table of loss adjustment factors as revised in January 28, 1998 filing are given below in the table below

PG&E Distribution Loss Adjustment Factors

Distribution Loss Factors

Distribution Loss Factors

UDC Load (100 mW increments)

Primary LF

Secondary LF

UDC Load (100 mW increments)

Primary LF

| Secondary LF |
| --- |
| 4300 | N/A | N/A |
| 7400 | 1.0170 | 1.0651 |
| 4400 | N/A | N/A |
| 7500 | 1.0172 | 1.0653 |
| 4500 | N/A | N/A |
| 7600 | 1.0173 | 1.0655 |
| 4600 | 1.0135 | 1.0659 |
| 7700 | 1.0175 | 1.0657 |
| 4700 | 1.0136 | 1.0655 |
| 7800 | 1.0176 | 1.0659 |
| 4800 | 1.0136 | 1.0651 |
| 7900 | 1.0178 | 1.0662 |
| 4900 | 1.0137 | 1.0649 |
| 8000 | 1.0179 | 1.0664 |
| 5000 | 1.0138 | 1.0646 |
| 8100 | 1.0181 | 1.0666 |
| 5100 | 1.0139 | 1.0644 |
| 8200 | 1.0182 | 1.0669 |
| 5200 | 1.0141 | 1.0642 |
| 8300 | 1.0184 | 1.0672 |
| 5300 | 1.0142 | 1.0640 |
| 8400 | 1.0186 | 1.0674 |
| 5400 | 1.0143 | 1.0639 |
| 8500 | 1.0187 | 1.0677 |
| 5500 | 1.0144 | 1.0638 |
| 8600 | 1.0189 | 1.0680 |
| 5600 | 1.0145 | 1.0637 |
| 8700 | 1.0190 | 1.0683 |
| 5700 | 1.0146 | 1.0636 |
| 8800 | 1.0192 | 1.0686 |
| 5800 | 1.0148 | 1.0636 |
| 8900 | 1.0193 | 1.0689 |
| 5900 | 1.0149 | 1.0635 |
| 9000 | 1.0195 | 1.0692 |
| 6000 | 1.0150 | 1.0635 |
| 9100 | 1.0197 | 1.0695 |
| 6100 | 1.0152 | 1.0635 |
| 9200 | 1.0198 | 1.0698 |
| 6200 | 1.0153 | 1.0636 |
| 9300 | 1.0200 | 1.0701 |
| 6300 | 1.0154 | 1.0636 |
| 9400 | 1.0202 | 1.0704 |
| 6400 | 1.0156 | 1.0637 |
| 9500 | 1.0203 | 1.0707 |
| 6500 | 1.0157 | 1.0638 |
| 9600 | 1.0205 | 1.0711 |
| 6600 | 1.0158 | 1.0639 |
| 9700 | 1.0206 | 1.0714 |
| 6700 | 1.0160 | 1.0640 |
| 9800 | 1.0208 | 1.0717 |
| 6800 | 1.0161 | 1.0641 |
| 9900 | 1.0210 | 1.0721 |
| 6900 | 1.0163 | 1.0642 |
| 10000 | 1.0211 | 1.0724 |
| 7000 | 1.0164 | 1.0644 |
| 10100 | 1.0213 | 1.0728 |
| 7100 | 1.0166 | 1.0645 |
| 10200 | 1.0215 | 1.0731 |
| 7200 | 1.0167 | 1.0647 |
| 10300 | 1.0216 | 1.0735 |
| 7300 | 1.0168 | 1.0649 |
| 10400 | 1.0218 | 1.0738 |

continued

|  | Distribution Loss Factors |
| --- | --- |
|  | Distribution Loss Factors |
| UDC Load (100 mW increments) |

Primary LF

Secondary LF

UDC Load (100 mW increments)

Primary LF

| Secondary LF |
| --- |
| 10500 | 1.0220 | 1.0742 |
| 13800 | 1.0275 | 1.0875 |
| 10600 | 1.0221 | 1.0746 |
| 13900 | 1.0277 | 1.0878 |
| 10700 | 1.0223 | 1.0749 |
| 14000 | 1.0278 | 1.0882 |
| 10800 | 1.0225 | 1.0753 |
| 14100 | 1.0280 | 1.0887 |
| 10900 | 1.0226 | 1.0757 |
| 14200 | 1.0281 | 1.0890 |
| 11000 | 1.0228 | 1.0761 |
| 14300 | 1.0283 | 1.0895 |
| 11100 | 1.0230 | 1.0764 |
| 14400 | 1.0286 | 1.0901 |
| 11200 | 1.0231 | 1.0768 |
| 14500 | 1.0287 | 1.0906 |
| 11300 | 1.0233 | 1.0772 |
| 14600 | 1.0289 | 1.0910 |
| 11400 | 1.0235 | 1.0776 |
| 14700 | 1.0291 | 1.0914 |
| 11500 | 1.0236 | 1.0780 |
| 14800 | 1.0293 | 1.0919 |
| 11600 | 1.0238 | 1.0784 |
| 14900 | 1.0294 | 1.0923 |
| 11700 | 1.0240 | 1.0788 |
| 15000 | 1.0296 | 1.0928 |
| 11800 | 1.0241 | 1.0792 |
| 15100 | 1.0298 | 1.0932 |
| 11900 | 1.0243 | 1.0796 |
| 15200 | 1.0300 | 1.0936 |
| 12000 | 1.0245 | 1.0800 |
| 15300 | 1.0301 | 1.0941 |
| 12100 | 1.0246 | 1.0803 |
| 15400 | 1.0303 | 1.0945 |
| 12200 | 1.0248 | 1.0807 |
| 15500 | 1.0305 | 1.0949 |
| 12300 | 1.0250 | 1.0811 |
| 15600 | 1.0306 | 1.0954 |
| 12400 | 1.0251 | 1.0816 |
| 15700 | 1.0308 | 1.0958 |
| 12500 | 1.0253 | 1.0820 |
| 15800 | 1.0310 | 1.0962 |
| 12600 | 1.0255 | 1.0823 |
| 15900 | 1.0312 | 1.0967 |
| 12700 | 1.0256 | 1.0827 |
| 16000 | 1.0313 | 1.0971 |
| 12800 | 1.0258 | 1.0831 |
| 16100 | 1.0315 | 1.0975 |
| 12900 | 1.0259 | 1.0835 |
| 16200 | 1.0317 | 1.0980 |
| 13000 | 1.0262 | 1.0841 |
| 16300 | 1.0318 | 1.0984 |
| 13100 | 1.0263 | 1.0844 |
| 16400 | 1.0320 | 1.0988 |
| 13200 | 1.0265 | 1.0848 |
| 16500 | 1.0322 | 1.0992 |
| 13300 | 1.0267 | 1.0853 |
| 16600 | 1.0323 | 1.0997 |
| 13400 | 1.0268 | 1.0857 |
| 16700 | 1.0325 | 1.1001 |
| 13500 | 1.0270 | 1.0861 |
| 16800 | 1.0327 | 1.1005 |
| 13600 | 1.0271 | 1.0865 |
| 16900 | 1.0329 | 1.1010 |
| 13700 | 1.0274 | 1.0870 |
| 17000 | 1.0330 | 1.1014 |