Data Quality and Integrity Issues with

Processing of Settlement-Ready Data

Michael R. Jaske, California Energy Commission

April 2, 1998

This brief paper outlines the possible problems that will be encountered in the processing of settlement-ready data by parties other than the ISO during the ISO’s settlement procedures.  These data are developed and submitted under the supervision of the scheduling coordinator.  The ISO uses them in conjunction with comparable data from all other loads and resources in identifying energy imbalances, assigning imbalance costs, and assigning other ISO charges on the basis of loads.  Once the SC receives the settlement statement from the ISO, the SC presumably uses the initial data to allocate the ISO’s charges back down to charges applicable to the SC’s various clients.  This paper amplifies upon the risks, existing controls, and possible additional mitigation strategies included within the transactions matrix.

1. Background

Preparation of settlement-ready data consists of the four following steps:

a.	application of proper load profiles to validated cumulative meter data to yield synthetic hourly interval data at the individual customer level;

b.	application of proper hourly distribution loss factor values for the Trading Day to either synthetic or actual interval data consistent with the voltage level of the retail customer tariff maintaining proper time synchronization;

c.	aggregation of individual customer data into groups of customers clustered to a specific load zone or take out point consistent with the grouping of customers that was used in the submission of preferred schedules for the Trading Day to the ISO; and

d.	the aggregated hourly data of step three is packaged into the format required for submission to the ISO and is submitted according to the ISO’s procedures for settlement-ready data.

The result of these four steps is initially an expansion of the volume of retail customer data as cumulative measurements are replaced by synthetic hourly data and then a contraction of this large volume of data as individual customer data are aggregated into groups of customers clusters into a relatively small number of geographic points.  This kind of data is submitted each day to the ISO as part of the settlement process for a Trading Day that occurred more than a month previously; therefore there is a continuous processing of customer data into settlement ready submissions to the ISO.

2. Processing of Retail Customer Data for Submission to the ISO

Each of the four steps described above can be performed incorrectly, leading to various problems.  This section will describe the known problems, their consequences to the market, methods for detecting these problems, and potential solutions that should be investigated more completely than has been possible in the timeframe to date.

2.1 Application of Load Profiles

Activity: application of proper load profiles to validated cumulative meter data to yield synthetic hourly interval data at the individual customer level.  This is a highly computer computation intensive task.

Every individual customer must have an identifier that allows that customer to be linked to an authorized load profile.  Beginning July 1, 1998, the CPUC has directed that dynamic load profiles be developed.  These will be computed and posted daily by the UDCs.  At some future date it is likely that current groupings of customers will be segmented into more narrowly drawn groups resulting in a greater number of categories.  Taken together, it is likely that a current set of 10 distinct computer files containing monthly static load profiles in use at the market startup will be replaced by 750 load profile files available from the UDC MDMA servers 25 files each day for 30 days per month.  Thus, the party conducting step 2.1 must download data, create 720 hour strings, develop proportional factors from the absolute level s of the LP files, assign the resulting 720 hour file to each customer in a manner that could be unique to that customer.

Potential Problems:  These include:

a. failure to convey retail customer attributes needed for classification

b. failure to ensure only eligible customers use load profiles

c. improper assignment of load profile from correct Trading Day

d. improper assignment of load profile from wrong Trading Day data

e. improper application of load profile to valid cumulative meter data

f. fraudulent use of unauthorized load profiles

Problem 2.1.1 -- Failure to Convey Customer Attributes.  In this problem the DASR response from the UDC failures to provide the identifier that permits a load profile to be linked to each customer.  This is unlikely in the early stages when these attributes are rate group, but increase in probability of occurrence if subpopulations based on occupancy patterns or Standard Industrial Classification codes are used.  These attributes might not be universally available in a UDC master file for its customers.  Rather than hold up the DASR, which ought to happen according to existing protocols, the ESP is tempted to proceed by assigning a “guesstimated value” and resolves to “fix the problem” later.

Implications of Problem 2.1.1:  There are direct financial consequences to all market participants of this problem through the mechanism of increased UFE costs, which must then be born by all market participants since the ISO will use a prorata allocation of UFE costs in its settlement protocols.

The level of risk is low.  This outcome is the product of a low probability of problems in missing customer attribute data needed to assign load profiles, combined with a low magnitude of financial harm provided that there is no fraudulent assignment of systematically inappropriate load profiles.

Existing Controls to Prevent Problem 2.1.1: UDCs are not supposed to provide a DASR response unless all needed variables have been supplied.  If segmentation of LPs takes place as likely from D.97-10-030, then the DASR process must be revised to shift the LP attribute variable from rate group to the new definitions.  Internally the UDC must revise the process it uses to validate DASR responses, and may have to create new attributes for its customer master file.  Therefore, while existing controls may be sufficient for static load profiles defined by rate group, they may become inadequate as the LP community evolves LPs into a more complex representation of customer load patterns.

Potential Solutions to Problem 2.1.1:  There are two potential solutions.  First, UDCs must be sure that their internal DASR processing systems look ahead to potential changes in the definition of load profiles, and be prepared to undertake changes to customer master file or verifications of translations of attributes based upon the customer master file.  Second, there must be sanctions that dissuade an ESP from accepting a DASR response that it finds cannot be properly matched to the authorized LPs, and a process through auditing that can detect when an ESP has ignored a DASR response problem and proceeded to initiate direct access for such a customer.

Problem 2.1.2 -- Ineligible Customer Using Load Profiles

[forthcoming]

Problem 2.1.3 -- Improper Assignment of LP from Correct Trading Day

[forthcoming]

Problem 2.1.4 -- Improper Assignment of LP from Wrong Trading Day

[forthcoming]

Problem 2.1.5 -- Improper Application of the Load Profile:

[forthcoming]

Problem 2.1.6 -- Fraudulent Use of Unauthorized LPs:  In this problem, the party applying an LP to cumulative meter readings uses an incorrect LP with the intent to defraud the ISO of energy payments.  For example, rather than using a set of hourly allocation factors for the 720 hours in a monthly billing period which total to 1.00, the ESP is a set which sum to 0.75.  As long as there is a non-zero entry for every hour, and the pattern of fraud is consistent through time, then this form of fraud is difficult to detect.

This problem can take place because the MDMA source of cumulative meter readings goes in parallel from the MDMA server to two sets of parties for further processing: (1) to the UDC for UDC billing, and (2) to the ESP and/or its agents for processing into the form required by the ISO for settlements.  These two uses are never reconciled, so a fraudulent ESP can “shave” customer loads in reporting to the ISO, while the customer and the UDC are never aware of the problem.  This is one of the two classic problems with the information flow design of the current marketplace identified in the RSIF report in July 1997.

Implications of Problem 2.1.6:  There are direct financial consequences to all market participants of this problem through the mechanism of increased UFE costs, which must then be born by all market participants since the ISO will use a prorata allocation of UFE costs in its settlement protocols.

The level of risk is substantial.  This outcome is the product of a low probability of problems in misassignment of load profiles, but a steady, consistent magnitude of financial harm because the errors are deliberately systematic in one direction.

Existing Controls to Prevent Problem 2.1.6:  There are no controls in place that can detect this problem.

Potential Solutions to Problem 2.1.6:  There are three possible solutions to this problem.

First, a systematic auditing program in which the ISO’s data, and the UDC’s data for specific customers or sets of customers are traced through each and every data processing step from end-to-end.

Second, installation of hourly upstream metering that can develop subcontrol totals on end-use hourly consumption that allow UFE energy to be computed and allocated below the level of the system, which can be used to identify particular locations where anomalies exist.  These would need to be further examined, and might provide a rationale for triggering one or more kinds of auditing.

Third, a periodic reporting requirement of each ESP’s energy reported to the ISO for settlement and provided to the UDC for CPUC-jurisdictional billing purposes, with the ISO required to examine the UDC report and the UDC to examine the ISO report would identify mismatches.  The mere existence of an independent verification check such as this would tend to reduce the incidence of fraud, since there would be an increased chance of being detected.  This kind of reporting requirement might be randomized, with each ESP likely to be required to produce it once per year, but the actual request coming without notice.  Such a selective review would reduce the data review burden on the ISO and UDC.

2.2 Application of Distribution Loss Factors

[forthcoming]

2.3 Aggregation to Groups Based on Geographic Clustering

[forthcoming]

2.4 Conversion into MDAS Format and Submission to the ISO

[forthcoming]

3. Processing of ISO Settlement Charges Using Settlement-Ready Data to Allocate Aggregated Settlement Charges to Specific Scheduling Coordinator Clients

Once the ISO delivers an aggregated settlement statement to the scheduling coordinator, the scheduling coordinator allocates the aggregated settlement charges to each of the scheduling coordinator’s clients.  There is no required methodology that the SC should use to perform this allocation, but the SC will be under some pressure from its clients to do so in a known, replicable manner that is reasonable equitable.  This reversal of the preparation of settlement-ready data is less well understood than the initial preparation of settlement-ready data, but the potential problems which can be encountered can lead to some of the same consequences for the SC’s clients that are of concern to DQIWG, e.g. data quality and integrity issues that raise suspicion and distrust.

[remainder of this section paralleling section 2 is forthcoming]

4. Development of Detailed Implementation Mechanisms

[forthcoming]

5. Process for Achieving Support for Detailed Implementation Mechanisms

[forthcoming]