Revised Strawman California Standards Connecting an

Electric Meter Located on a CEBus LAN to a Telephone Network

A Revised Contribution by

Bill Rush and Vic Tamosaitis

Institute of Gas Technology

Version of April 8,1998

Topology

This document is intended to stimulate discussion by describing a specific implementation of a remote electrical meter reading system.  The general topology, taken from IEEE 1397, is shown in Figure 1.  The IEEE 1397 topology, as adapted for California electric meters, is shown in Figure 2.  The topology for linking electric meters located on a CEBus LAN to the telephone network is shown in Figure 3, as a subset of the general California model.  Interfaces and devices addressed within the scope of this document are indicated by white blocks and solid lines.  Null devices are cross-hatched.  Devices and interfaces not addressed are shaded gray.  Functionally, this implementation is a meter connected to a CEBus LAN, which is then interfaced to the telephone Wide Area Network (WAN).

Reference Model

The system described is based upon the standard reference model, also set forth in IEEE 1397.  The reference model described in IEEE 1397 is shown connected to a router in Figure 4.  The specific CEBus/telephone implementation addresses the following - all of the layers within the router, the physical layer interface up through the analysis layer within the meter, and the primary element and signal conditioning layer associated with the meter.  The two layers directly above the application service - storage and digital conversion - are typically enclosed within the meter, so they are left to the manufacturer’s discretion.

Recommended Standards for Interface

Specific assignment of standards for the services (layers) being provided shall be as follows-

Meter

| Physical and Data Link and Network layers: | EIA-IS-60 CEBus Specification |
| --- | --- |
| Application Layer: |

ISO 9506-1, 2 Manufacturing Message Specification-

Part 1: Service Definition; Part 2: Protocol Specification

| Incorporate PSEM packets in MMS envelope. |
| --- |
| Analysis service: | ANSI C12.19 = IEEE1377 = Utility Industry End Device Data Tables = “Tucker Tables”- Use most recent version since document is under revision |
| Primary Element and Signal Conditioning | KYZ Standard Pulser Interface |

Communication Connector

Any standard electric meter socket.

Router

CEBus Side

| Physical and Data Link and Network layers: | EIA-IS-60 CEBus Specification |
| --- | --- |

Telephone WAN Side

Physical and Data Link layers:

IEEE 1390, Standard For Automatic Meter Reading via Telephone

IEEE P1390.1, Standard For Automatic Meter Reading via Telephone – Profile Protocols for Switched Telephone Network *

| IEEE 1390.2, Standard For Automatic Meter Reading via Telephone – Network to Telemetry Interface Unit |
| --- |
| Network Layer | Standard under development at IEEE SCC31 |

Figure 1 – IEEE 1397 Topology

Figure 2 – IEEE Topology Adapted for California Electric Meters

Figure 3 – IEEE1397 Implementation Connecting Electric Meters on a CEBus LAN to Telephone

Figure 4 – IEEE 1397 End Device Reference Model and Router