Schedule AP - I	Sheet 1 of 3

AGRICULTURAL AND PUMPING - INTERRUPTIBLE

APPLICABILITY

Applicable to customers with a measured demand of 50 kW or greater, or with a connected load of 50 horsepower or greater who are served under an Agricultural and Pumping rate schedule, and who elect to provide Interruptible Load automatically.  However, this schedule is not applicable to customers receiving the Off-Peak Credit provided under Schedule PA-1 or Schedule PA-2, or to customers served under experimental rate schedules.  As of June 7, 1992, this schedule is closed to customers taking service under Schedule TOU-PA-SOP.  In addition, as of January 1, 1993, this schedule is not applicable to Schedule TOU-PA-SOP customers.  Service under this schedule is subject to the availability of a control device and may not be available in certain areas of the Company's service territory where communication signaling equipment has not been installed or signal strength is inadequate to activate or deactivate interruption.  As of November 26, 1996, this schedule is closed except that existing customers adding new load can qualify for this schedule with a Firm Service Level no less than their Maximum Demand in the preceding 12 months.  Customers newly taking service from the Company can take service under this schedule for electrical loads not previously served by the Company.  Service under this Schedule will terminate March 31, 2002 whether or not a written notice of termination has been received from the customer.

TERRITORY

Within the entire territory served.

RATES

The net billing determined under the applicable, regular rate schedule will be credited $0.00827 per kWh per month.

SPECIAL CONDITIONS

1.	Interruptible Load:  The Interruptible Load is the total load served under the regularly applicable rate schedule.

2.	Notice of Interruption:  Interruption can occur under this schedule when:  (1) the next to the last peaker is required to be operated and there is insufficient time to evaluate and secure alternative options; or, (2) spinning reserve is anticipated to fall below 5 percent for more than one hour, and the Company cannot provide energy and capacity at a price below 7¢/kWh.  Advance Notice of Interruption will not be provided.

3.	Period of Interruption:  A Period of Interruption is a time interval which commences upon interruption by the Company.  Under this schedule all interruptions are controlled by the Company.

4.	Number and Duration of Interruption:  The number of Periods of Interruption will not exceed 25 times per calendar year. The duration of the Periods of Interruption will not exceed 6 hours each or 150 hours per calendar year.

(Continued)

Schedule AP - I	Sheet 2 of 3

AGRICULTURAL AND PUMPING - INTERRUPTIBLE

(Continued)

SPECIAL CONDITIONS (Continued)

5.	Ownership and Control of Facilities:  Communication, metering, and interrupting facilities, as specified by the Company, will be installed, owned, and maintained in accordance with Company specifications at customer's expense, including such facilities not located on the customer's property.  These facilities will be solely under operational control of the Company unless otherwise specified by the Company.

Such communications and interrupting facilities may include, but will not be limited to, the following:

a.	Necessary facilities between the customer and the Company to provide Notice of Interruption.

b.	Equipment to permit remote monitoring of the customer's load.

6.	Excess Energy:  The number of kWh consumed after the first thirty minutes during a Period of Interruption shall be considered Excess Energy.

7.	Charges for Excess Energy:  For each Period of Interruption during which, through no fault of the Company, the Interruptible Load is not interrupted and hence Excess Energy occurs, the applicable $/kWh penalty as shown below shall be added to the customer's billing as otherwise provided in this schedule:

Applicable Penalties__________________        				              Service Voltage   Service Voltage   Service Voltage

in Excess of 50 kV    2 kV - 50 kV      Below 2 kV

$/kWh              $/kWh            $/kWh  _

For Each

Failure to Interrupt        5.70   	            5.91 	            6.04

8.	Contracts:  A contract is required for service under this schedule.  To be served under this schedule, eligible customers shall comply with all provisions of the contract within 90 days of contract execution.  During the initial year of service, either the Company or the customer may terminate service under this schedule upon not less than 30 days written notice.  After the initial year not less than five years written notice to modify or terminate service under this schedule will be required.  A customer may not obtain interruptible service within three years following termination of interruptible service under this schedule.  Customers shall not be permitted to prematurely terminate service hereunder for reasons that changes in electrical demand requirements may otherwise preclude them from taking service under this schedule.  Customers permitted by the Company to change to this schedule from another interruptible rate schedule shall, without further action by the Company, retain the termination requirements, if any, of the prior schedule and any contract associated therewith.

(Continued)

Schedule AP - I	Sheet 3 of 3

AGRICULTURAL AND PUMPING - INTERRUPTIBLE

(Continued)

SPECIAL CONDITIONS (Continued)

9.	Customer-Owned Electrical Generation Equipment:  Where customer-owned electrical generation equipment is used to meet a part or all of the customer's electrical requirements, service shall be provided concurrently under the terms and conditions of Schedule S and this schedule.  Parallel operation of such generation equipment with the Company's electrical system is permitted.

The use of customer-owned electrical generation equipment for auxiliary, emergency, or standby purposes (auxiliary/emergency generation equipment) is permitted under this schedule.  However, auxiliary/emergency generation equipment may be used by the customer to serve the customer's load only during a period when the Company's service is unavailable and only when such load is isolated from the service of the Company.  Auxiliary/emergency generation equipment may not be operated in parallel with the Company's electrical system, except that upon approval by the Company, momentary parallel operation may be permitted in order for the customer to avoid interruption of load during a Period of Interruption, or to allow the customer to test the auxiliary/emergency generation equipment.  A Momentary Parallel Generation Contract is required for this type of service.