Rule 9.1				Sheet 3 of 4

RENDERING AND PAYMENT OF BILLS

DIRECT ACCESS/DEPARTING LOAD

(Continued)

C.	Rendering of Bills

1.	Metered Service

Except where the use of Statistical Load Profiling is permitted, Direct Access Customers shall install, at the customer’s expense, meters capable of recording and providing hourly data.  An energy credit will be applied to the Direct Access Customer’s bill in accordance with the provisions of Schedule DA, Direct Access.

2.	Statistical Load Profiles

Small Customers may engage in Direct Access through the use of Statistical Load Profiles established by Edison rather than using hourly metering.  This provision may also apply to certain Direct Access Customers other than Small Customers as determined by the Commission.  These Statistical Load Profiles will be used to determine the energy credit applied to such Direct Access Customer’s bill in accordance with the provisions of Schedule DA, Direct Access.  However, Small Customers may have Edison install, own, and maintain, at the customer’s option and expense, meters capable of recording and providing hourly data.  In such cases, the customer is ineligible for Statistical Load Profiling and the energy credit will be based on the customer’s metered hourly energy usage.

3.	Electronic Data Exchange

When electronic data exchange is utilized, the ESP shall use Electronic Transfer in a format acceptable to Edison.

4.	Energy Service Provider Metering

a.	When metering services are provided by an ESP, such ESP is responsible for maintaining and storing historical billing data and providing current and historical data in a format acceptable to Edison.

b.	When metering services are provided by an ESP, the ESP shall provide meter registration data to Edison on a schedule acceptable to Edison.

(Continued)